The Australian Soil Resource Information System

Technical specifications

www.asris.csiro.au

Australian Collaborative Land Evaluation Program

Prepared by Neil McKenzie, David Jacquier, and David Simon on behalf of the Working Group on Land Resource Assessment

Version 1.1

11 May 2004

1.	Summary	7

2.	User needs for soil and land resource information	9

2.1	Reducing risks in decision making	9

2.2	Improving process understanding	10

2.3	Mapping, monitoring, modeling, and environmental history	10

2.4	Land condition	12

3.	Development of ASRIS	15

4.	Hierarchy of land units and terminology	17

4.1	Concepts and terms	17

4.2	Definition of higher levels in the hierarchy	20

4.3	Relationships between the land unit hierarchy and continental grids	22

4.4	Description of Land Facet and Land System Tracts	22

5.	Accuracy, precision and a basis for stating uncertainty	25

5.1	Rationale	25

5.2	Estimating uncertainty	25

6.	Level-1 descriptors (land division)	29

7.	Level-2 descriptors (land province)	30

8.	Level-3 descriptors (land zone)	31

9.	Level-4 descriptors (land district)	32

10.	Level-5 descriptors (land system)	33

10.1	Identifiers	33

10.2	Mapping Intensity and Scale	34

10.3	Landform	35

11.	Level-6 descriptors (land facets)	37

11.1	Identifiers	37

11.2	Landform	38

11.3	Land Surface	39

11.4	Soil	41

11.5	Substrate	69

12.	Soil Profile Database	73

13.	GIS, database design and data transfer	75

14.	Relationship to SOTER	81

15.	References	83

Appendix: Conversion for pH in water to pH in CaCl2	87

Table 1: Complementary benefits of mapping (contained within ASRIS), monitoring and modelling	12

Table 2: The spatial hierarchy of land-unit tracts (after Speight 1988). Note that the database design for ASRIS allows intermediate Levels to be characterized (e.g., a System with a characteristic dimension significantly less that 100 m would be designated as Level 5.1 or 5.2 in the hierarchy)	20

Table 3: Default estimates of uncertainty for attributes of land-unit tracts in ASRIS – defaults for landform and land surface (relief, modal slope, element, pattern, microrelief, rock outcrop and surface coarse fragments) are yet to be determined.	28

Table 4: Level-5 land unit tract identifiers	33

Table 5: Nature of observations for land unit tract	34

Table 6: Orders of survey (modified from Soil Survey Staff (1993, p48–49))	34

Table 7: Relief and modal slope classes	35

Table 8: Codes for landform pattern	36

Table 9: Level-6 land unit tract identifiers	37

Table 10: Landform morphological type	38

Table 11: Drainage classes	38

Table 12: Landform elements (after Speight 1990)	39

Table 13: Microrelief type	40

Table 14: Described gilgai component (if present)	40

Table 15: Biotic agent for microrelief (if present)	41

Table 16: Biotic component of microrelief (if present)	41

Table 17: Representativeness of the most similar soil profile in the ASRIS Soil Profile Database	42

Table 18: Estimation method for field texture	43

Table 19: Estimation method for clay content	43

Table 20: Field-texture grades, modifiers and qualifiers	45

Table 21: Estimation method for coarse fragments	47

Table 22: Estimation method for bulk density	48

Table 23: Estimation method for pH	49

Table 24: Estimation method for organic carbon	50

Table 25: Estimation method for depths	51

Table 26: Type of impeding layer	52

Table 27: Estimation method for the type of impeding layer	53

Table 28: Estimation method for the estimation of water retention parameters	55

Table 29: Permeability classes	57

Table 30: Estimation method for saturated hydraulic conductivity	57

Table 31: Estimation method for electrical conductivity	58

Table 32: Aggregate stability classes based on Emerson (2002)	59

Table 33: Estimation method for aggregate stability	59

Table 34: Water repellence (after Moore 1998).	60

Table 35: Method for estimating water repellence of the land surface	61

Table 36: Estimation method for exchangeable bases, CEC and ESP	61

Table 37: Method codes for Sum Exchangeable Bases, CEC, and ESP (These are currently under review by the Working Group on Land Resource Assessment)	63

Table 38: Confidence level for the allocation to the Australian Soil Classification	64

Table 39: Version of the Australian Soil Classification used for allocation	64

Table 40: Codes for Soil Orders in the Australian Soil Classification	64

Table 41: Codes for Suborders, Great Groups and Subgroups in the Australian Soil Classification	65

Table 42: Codes for Family criteria in the Australian Soil Classification	67

Table 43: Method for allocating profile to the classification system (either ASC or WRB)	67

Table 44: Reference Soil Group codes for the World Reference Base	68

Table 45: Qualifiers for Reference Soil Groups in the World Reference Base	68

Table 46: Regolith material descriptions used for the characterization of substrate (Pain et al. 2004)	70

Table 47: Estimation method for substrate type	70

Table 48: Estimation method for substrate permeability	71

Table 49: Recommended minimum data set for the ASRIS soil profile database	73

Table 50: The agencies table.	76

Table 51: The projects table	76

Table 52: The site_location table.	77

Table 53: The features table.	77

Table 54: The feature notes table	77

Table 55: The samples table	78

Table 56: The sample notes table	78

Table 57: The results table	78

Table 58: The parameter_num_method table.	79

Table 59: The param_char_method table	79

Table 60: The param_ char_refs table	79

Table 61: The codes table.	79

Table 62: Conversion for pH in water to pH in CaCl2.	87

Figure 1: Mapping, monitoring and modelling are complementary activities for natural resource management and they must be set against the context of the environmental history of events and processes for a given landscape. ASRIS provides the national framework for soil and land resource information.	11

Figure 2: Examples of triangular probability distribution functions for coarse fragments. The mean, 5% and 95% quantiles are shown for the less variable layer.	27

Figure 3: Example control sections for a shallow texture-contrast soil	42

Figure 4: Control sections and layers used for estimating available water capacity for individual layers, and profile available water capacity.	54

Figure 5: Database design for ASRIS. Definitions of variables are provided in the Tables below.	75

# Summary

This document specifies the variables, codes and estimation procedures for the Australian Soil Resource Information System (ASRIS). ASRIS has been developed to meet the demands of a broad range of users including natural resource managers, educational institutions, planners, researchers, and community groups. The online system provides access to the best available soil and land resource information in a consistent format across the county – the level of detail depends on the survey coverage in each region. More specifically, ASRIS provides:

A spatial hierarchy of land unit tracts with seven main levels of generalization. The upper three levels (L1–L3) provide descriptions of soils and landscapes across the complete continent while the lower levels (L4–L6) provide more detailed information, particularly on soil properties, for areas where mapping has been completed. The lowest level (L7) relates to an individual site in the field. The system can also be used to provide summaries of soil and landscape properties for a range of higher level stratifications of the country (e.g., Interim Biogeographic Regions of Australia (v5.1), Groundwater Flow Systems, and catchment management boundaries).

A consistent set of land qualities is described for land-unit tracts. Descriptions from the lowest-level units are used to generate summaries for higher-level units. The land qualities relate to the intrinsic capability of land to support various land uses – the land qualities relate to soil depth, water storage, permeability, fertility, and erodibility.

ASRIS includes a soil profile database with fully characterized sites that are known to be representative of significant areas and environments. The data provide catchment managers with primary source material for improving land literacy in their region, and natural resource specialists with a fundamental data set for assessing and predicting resource condition.

Estimates of uncertainty are provided with most data held within ASRIS. A distinction is made between attribute uncertainty (due to the measurement or estimation procedure for a given soil material) and spatial uncertainty (due to the natural variation across a landscape). The estimates are provided to encourage formal analysis of the uncertainty of predictions generated using ASRIS data (e.g. crop yield, runoff, land suitability for a range of purposes)

ASRIS is being released in stages. ASRIS 2004 will contain some 5,000 soil profiles along with the upper levels of the hierarchy (L1–L3) for most of the country and restricted coverage for lower levels. ASRIS 2006 will complete the coverage at the lower levels and contain an expanded soil profile database. ASRIS can be accessed online at www.asris.csiro.au.

# User needs for soil and land resource information

The general proposition that our natural environment should be mapped and monitored is widely supported by natural resource management agencies, industry groups and community organizations. This information provides a basis for devising, implementing and monitoring land management. It also provides a basis for diagnosing the general condition of landscapes. Information on soil and land resources is fundamental and this is where ASRIS plays a central role.

The emergence of a range of large-scale environmental problems in Australia has added to the general demand for better information on spatial variation and trends in land resource condition. Satisfying this demand requires a clear view of how natural resource information is used to good effect. The first way is through reducing risks in decision-making, and the second involves improving our understanding of biophysical processes.

## Reducing risks in decision making

Reducing risk in decision-making requires the provision of information to be closely linked to, and preferably driven, by the decision-making process, whether at the scale of the paddock, enterprise, small catchment, region or nation. For example, farmers need information at the scale of the paddock, while a Commonwealth funding agency will usually require information at the regional and continental scale. Decision makers in Australia require timely access to information at relevant scales. ASRIS is a significant component in the delivery system. It has been developed with a view to satisfying a diverse range of needs at various levels of resolution. The following demands from government, industry, and community groups were of primary interest.

#### Government

The provision of reliable natural resource information to support policy decisions by Commonwealth, state, territory and regional agencies is necessary to address serious environmental problems, including global warming, dryland salinity and soil acidification. Improved natural resource information is required to:

Design, implement and assess the effectiveness of major natural resource management programs (e.g. schemes for widespread planting of perennials to control recharge);

Implement trading schemes (e.g. for salt, water and carbon) to achieve better natural resource management outcomes;

Establish baselines (e.g. for contaminants); and

Set targets and monitor trends.

#### Industry

Agricultural industries require better soil and land resource information to:

Optimize the matching of land use and management with land suitability (some sectors, most notably viticulture and industrial-scale farm forestry, have increased investment in user-specific land resource assessment during recent years);

Gain market advantage by demonstrating the benign nature of production systems (e.g. green labeling);

Implement environmental management systems to comply with duty of care regulations and industry codes; and

Optimize the use of inputs (e.g. soil nutrient testing to guide fertilizer rates).

#### Regional Communities

Regional communities require better soil and land resource information to:

Assess and improve the efficacy of natural resource management and target community action (e.g. remedial tree planting, fencing, weed control); and

## Improving process understanding

The reasons for using soil and land information outlined in the previous section focus on reducing risk in decision making. Another distinct application for soil information is to improve the understanding of landscape processes. This is largely the domain of educational, research and development organizations. Studies providing an improved understanding of landscape processes vary greatly in scope. For example, geomorphic studies of landscape evolution may involve intensive characterization and dating of stratigraphic sequences. Pedologic investigations of soil formation can require detailed surveys of key areas to determine the influence of different soil forming factors. Long-term monitoring studies usually involve some form of field experiment at the scale of the plot (e.g. agricultural tillage trials), through to the small catchment (e.g. paired-catchment studies in ecohydrology).

ASRIS provides a frame of reference for studies of landscape processes – it gives context by providing a basic stratification of the landscape into zones where baselines can be established, trends monitored, and results extrapolated. It also provides the basis for creating improved models for explanation and prediction (e.g., better statistical models for spatial prediction; improved simulation models to assess the environmental impact of land uses). The knowledge generated from these activities allows development of improved systems of land-use and management, and provides a scientific basis for improved policies in natural resource management.

## Mapping, monitoring, modeling, and environmental history

Land resource survey provides a key spatial component in the biophysical information system necessary for natural resource management.  ASRIS integrates outputs from survey programs across Australia and it must be considered with the mutually beneficial activities of monitoring and modelling, and all three should then be set within the context of environmental history – the latter provides an understanding of rates of soil and landscape change on much longer time scales (decades, centuries and millennia).

In isolation, each activity fails to provide appropriate information for land management and planning. In combination, they provide a powerful and synergistic means for transforming the quality of land management in Australia (Figure 1, Table 1).

Figure 1: Mapping, monitoring and modelling are complementary activities for natural resource management and they must be set against the context of the environmental history of events and processes for a given landscape. ASRIS provides the national framework for soil and land resource information.

Table 1: Complementary benefits of mapping (contained within ASRIS), monitoring and modelling

| Complementary Relationship | Benefits |
| --- | --- |
| ASRIS mapping ( Monitoring | Spatial framework for selecting representative sites System for spatial extrapolation of monitoring results Broad assessment of resource condition |
| ASRIS mapping ( Modelling | Provides input data for modelling Provides spatial association of input variables |
| Monitoring ( ASRIS mapping | Quantifies and defines important resource variables for mapping Provides temporal dimension to land suitability assessment (including risk assessments for recommended land management practices) |
| Modelling ( ASRIS mapping | Allows spatial and temporal prediction of landscape processes |
| Modelling ( Monitoring | Determines whether trends in specific land attributes can be successfully detected with monitoring Identifies key components of system behaviour that can be measured in a monitoring program |
| Monitoring ( Modelling | Provides validation of model results Provides input data for modeling |

## Land condition

In most parts of Australia, land resource surveys are undertaken across a range of seasonal conditions. Land cover and management vary during the course of a season and survey. Furthermore, to maximize objectivity and consistency, observations on land condition (e.g., scald erosion, wind erosion, sheet and rill erosion, gully erosion, mass movement, human-induced saline seepage, surface scalding) are made using the evidence present in the field at the time of survey. The rates of most land degradation processes are difficult to estimate unless permanent monitoring sites are used (see McKenzie et al. 2002). For example, in cropping areas, evidence for severe rill erosion can be obliterated by subsequent trafficking and cultivation. Similarly, the degree of expression and extent of saline seepage areas can vary dramatically with season.

The field observations and interpretations in the state and territory land resource databases span many decades – it is simply not possible to use these to generate a useful assessment of land condition. Fortunately, ASRIS can be used to support the assessment of land condition in other ways and it requires a broad view of the biophysical information base necessary for natural resource management (Figure 1).

ASRIS provides the basis for assessing land-degradation hazard. This can be achieved in various ways. For example, the Universal Soil Loss Equation can be parameterized using attributes from ASRIS to provide estimates of soil erosion by water. Models for predicting the hazard of wind erosion are also available. NLWRA (2001) provides other examples of how broad-scale soil information can be used to predict land condition and threatening processes (e.g., soil acidification).

ASRIS also provides a basis for locating monitoring sites for land condition and a framework for the extrapolation of results (Table 1).

# Development of ASRIS

ASRIS was initiated through the National Land and Water Resources Audit (NLWRA) in 1999 (see NLWRA 2002, Henderson et al. 2002). The initial release (ASRIS 2001) provided primary inputs for a broad range of simulation modeling studies supported by the NLWRA. These studies provided continental perspectives on erosion, sediment delivery to streams, nutrient cycling, acidification, net primary productivity, and water quality (NLWRA 2001, 2002).

The ASRIS 2001 team achieved a great deal given the short time available and daunting nature of the task (see Johnston et al. 2003). During the project, the core team and the Working Group on Land Resource Assessment (which acted as the Steering Committee) identified a series of deficiencies in the land resource information base for Australia. They also identified a logical pathway for overcoming these problems to ensure a greatly improved system for providing information to support natural resource management in Australia. The task was recognized to be long-term, and requiring a permanent project team (NLWRA 2002).

With this background, the Australian Collaborative Land Evaluation Program (ACLEP) was commissioned by the Department of Agriculture, Forestry and Fisheries (DAFF) to provide land managers, regional organizations, industry partners, policy specialists and technical experts in natural resource management, with online access to soil and land resource information, and assessments of land suitability. The information is to be available at a range of scales, and in a consistent and easy-to-use format across Australia. The activity must also provide a scientific framework for assessing and monitoring the extent and condition of Australia’s soil and land resources.

This document presents specifications for releases of the Australian Soil Resource Information System in 2004 and 2006 (ASRIS 2004 and ASRIS 2006 respectively).  These releases augment information provided by ASRIS 2001. More specifically, the releases provide:

A hierarchy of land units for the Australian Soil Resource Information System to allow comprehensive reporting on land suitability and soil resources from the National down to the Subregional scale. Upper levels of the hierarchy are generated using digital terrain analysis and refinements of existing geomorphic maps. Lower levels are derived from the component state, territory and Commonwealth land resource map databases. There is also the facility to represent soil and land resource information using a number of other high-level stratifications including the Interim Biogeographic Regions of Australia (v5.1), Groundwater Flow Systems, and catchment management boundaries.

A consistent set of land qualities are presented for the lowest level units in the hierarchy and these are used to generate summaries for higher-level units. The land qualities relate to the intrinsic capability of land to support various land uses – they relate to soil depth, water storage, permeability, fertility, and erodibility.

The new releases of ASRIS will be in two stages. ASRIS 2004 contains the upper levels of the hierarchy for the whole country but lower levels will be initially from three States. ASRIS 2006 contains the complete coverage for all levels and all states and territories. Both releases are provided via the Internet using SQL Server, the Arc Spatial Data Engine (ArcSDE), and Arc Internet Map Server (ArcIMS). The system is accessed at www.asris.csiro.au.

ASRIS includes a soil profile database with fully characterized sites that are known to be representative of significant areas and environments. ASRIS 2004 contains approximately 5000 soil profiles with full quality assurance. The data are accessible on-line and provide catchment managers with primary source material for improving land literacy in their region, and natural resource specialists with a fundamental data set for assessing and predicting resource condition. The profile database will be expanded to 10,000 profiles with the release of ASRIS 2006.

ASRIS 2004 and 2006 include the original ASRIS 2001 soil information layers for the country in cases where improved coverages have not been generated.

# Hierarchy of land units and terminology

## Concepts and terms

A wide range of survey methods has been used in Australia (Beckett and Bie 1976, Gibbons 1983, McKenzie 1991) but most have been based on some form of integrated or soil-landscape survey (Christian and Stewart 1968; Mabbutt 1968; Northcote 1984) at medium to reconnaissance scales (1:50,000-1:250,000). Speight (1988) notes that the wide variation in mapping practice among different Australian survey organizations is largely a matter of level of classification or precision, rather than a difference in the conceptual units that surveyors recognize and describe.

Only small areas have been mapped using strict soil mapping units (e.g. soil series, type, variant, phase, association etc). Most of these studies have used free survey (Steur 1961, Beckett 1968) as the survey method and the majority of surveys have been detailed (i.e. 1:10,000–1:25,000) and for irrigation developments.

Quantitative surveys based on grid-based methods across small areas (usually <1000 ha), are becoming more common with the growth of precision agriculture. Quantitative surveys are also being applied at more general scales using methods of environmental correlation (e.g. McKenzie and Ryan 1999, Henderson et al. 2002, McKenzie et al. 2004). The key feature of these survey methods is the generation of predictions of individual soil properties rather than soil types.

This document is primarily concerned with capturing information from traditional integrated and soil-landscape surveys because these constitute more than 90% of land resource survey information for Australia. This should not be taken as tacit acceptance of conventional survey methods. There are many aspects of land resource assessment that must be changed to ensure a more technically defensible, and evidence-based, approach to natural resource management in Australia. The new guidelines for land resource survey outline directions for change (McKenzie et al. 2004).

The terminology used to define spatial units in Australia has been confused despite the pre-eminence of Australian workers in land resource survey and the existence of a well-defined literature (e.g. Stewart 1968, Austin and Basinski 1976, Dent and Young 1983, Gunn et al. 1988). Different groups have applied terms such as land unit, land system, and unique mapping area, in various ways. Speight (1988) brings order to the situation and his recommendations on terminology are adopted here because they are consistent with most aspects of current practice.

Individuals in agencies with a well-accepted local terminology may balk at the recommended terminology. This will be a problem for any set of proposed terms and flexibility is required if a consistent national standard is to be achieved. It is worth noting that the definitions of Speight (1988) are broadly consistent with international terminology (e.g. Dent and Young 1981). They are also part of the guidelines for survey practice in Australia (Gunn et al. 1988, McKenzie et al. 2004).

Speight (1988) uses land unit as a generic term and in a different sense to Christian and Stewart (1968).  Land unit does not imply a particular scale and it can be used to refer to:

conceptual units (e.g., land facets or systems as conceptual constructs),

mapping units (e.g. a tract of land or an individual polygon), and

taxonomic units (e.g. a type of land such as the Oxford Land System).

For these reasons, we will refer generally to the hierarchy of land units in ASRIS.

Speight (1988) also defines a land unit individual – this is a particular area of land having the same size as the land unit characteristic dimension.  Users of the Field Handbook (McDonald et al. 1990) will be familiar with this notion through the site concept.  For example, landform element attributes are observed over a circle (the site) of about 40 m diameter – the site in this instance defines the land unit individual and its characteristic dimension. In contrast, landform pattern attributes are observed over a circle of about 600 m diameter.

Speight’s (1988,1990) observations on the characteristic dimensions of landform elements and patterns were intended to provide a guide rather than a fixed value. The concept is far more valuable than this and we use it here in conjunction with sets of defining attributes to construct the hierarchy of land unit tracts.

Table 2 shows the hierarchy of land unit tracts. Each level in the hierarchy has a specified characteristic dimension along with a set of defining attributes measured at the accompanying scale. The characteristic dimension can be viewed as the window size over which the defining attributes can be sensibly measured – different landscapes will have contrasting characteristic dimensions. For example, hillslope lengths may be very short (e.g., only a few metres in a strongly gullied landscape) or long (greater than a kilometer in strongly weathered landscapes of low relief), so land facets of very different size result.  In some landscapes, nested patterns of landform may be evident and sublevels within the hierarchy can be sensibly delineated using the same set of defining attributes at more than one characteristic dimension (e.g., land systems within a land system). The ASRIS hierarchy and database structure allows sublevels to be defined for a given attribute set (e.g., Level 6.1).

The characteristic dimensions in Table 2 have been changed from Speight’s (1988) original proposition to emphasize its role as a variable that defines both the appropriate of measurement and the nature of the landscape. The suggested values also better match the styles of survey undertaken across large areas during the last 15 years.

In Table 2, tracts are mapping units as opposed to taxonomic units.  Note that polygon is often used synonymously with land unit tract. Most land resource assessment in Australia is concerned with the mapping and description of land unit tracts at the land facet and land system level.  Speight (1988) defines these as follows:

Land facet (L6): This is a land unit with attributes that include slope, aspect, toposequence position, microclimate, moisture regime, soil profile class, land surface features, vegetation formation and vegetation community. Speight (1988) considers its characteristic dimension to be about 40 m but it can vary from 100 to just a few metres.  Note that the terms land component and land element have often been equated with this definition of land facet.

Land system (L5): This is a land unit with attributes that include relief, modal slope, stream pattern, toposequences, local climate, lithology, soil association, vegetation type or sequence, and proportional occurrence and arrangement of land facets.  Speight (1988) considers its characteristic dimension to be about 600 m, and he recommends this diameter for a land-system site.

Note that these are definitions of conceptual land units.  Explicit reference can be made to land-unit individuals, types or tracts (e.g. land-facet individual, land-facet tract, land-facet type) but the context will usually convey the appropriate meaning. Particular mention should also be made of unique mapping areas – these are usually instances of land system tracts that are later grouped into land system types.

To reiterate, the concept of scale in the hierarchy of land unit tracts is based not on the cartographic scale of mapping, but rather on the characteristic dimension and set of defining attributes. If land facets and land systems are defined in terms of landform attributes alone, they are identical with the landform elements and landform patterns defined by McDonald et al. (1990).

Mapping land districts (L4) is usually achieved by grouping land systems. Mapping land units at higher levels can be achieved by grouping land districts but in reality, most mapping at the division (L1), province (L2), and zone (L3) level is undertaken using a divisive rather than an agglomerative approach. Furthermore, different criteria for mapping emerge at these more generalized levels and many of the criteria used at lower levels lose significance (and vice versa).

Table 2: The spatial hierarchy of land-unit tracts (after Speight 1988). Note that the database design for ASRIS allows intermediate Levels to be characterized (e.g., a System with a characteristic dimension significantly less that 100 m would be designated as Level 5.1 or 5.2 in the hierarchy)

| Level | Order of land unit tract | Speight | Characteristic dimension | Defining attributes | Appropriate map scale |
| --- | --- | --- | --- | --- | --- |
| 1.0 | Division | 300km | 30 km | broad climate, large-scale geologic structures (e.g. cratons, basins and blocks) | 1:10 million |
| 2.0 | Province | 100 km | 10 km | broad climate, landscape evolution | 1: 2.5 million |
| 3.0 | Zone | 30 km | 3 km | climate, mesoclimate, median relief, related lithologies | 1:1 million |
| ASRIS Mapping Hiatus Levels above are based on subdivisions of the continent Levels below are aggregated from surveys. |
| 4.0 | District | 5 km | 1 km | groupings of geomorphically related systems | 1:250 000 |
| 5.0 | System | 600 | 300 m | local climate, relief, modal slope, single lithology or single complex of lithologies, similar drainage net throughout, related soil profile classes (soil-landscape*) | 1:100 000 |
| 5.1 |  |  | 100 m | As for Level 5 | 1:25 000 |
| 6.0 | Facet | 40 | 30 m | slope, aspect, soil profile class | 1:10000 |
| 6.1 |  |  | 10 m |  | 1:2500 |
| 6.2 |  |  | 3 m |  | 1:1000 |
| 7.0 | Site | 20 | 10 m | soil properties, surface condition, microrelief | rarely mapped in conventional survey |

*  Sensu Thompson and Moore (1984)

## Definition of higher levels in the hierarchy

There are many maps of Australia’s natural resources at scales equivalent to the land zone, land province or land division. Some examples relevant to soils and landscapes include:

Northcote et al. (1960–1968) – Atlas of Australian soils

Löffler and Ruxton (1969) – Relief and landform map of Australia

Laut et al. (1980) – Provisional environmental regions of Australia

CSIRO (1983) – Soil landscape regions

Grant et al. (1984) – Geotechnical landscape map of Australia

Chan et al. (1986) – Regolith terrain map of Australia

Jennings and Mabbutt (1986) – Physiographic regions of Australia

Environment Australia (2000) – Interim biogeographic regions Version 5.1

Coram et al. (2001) – Groundwater flow systems

Williams et al. (2002) – Agro-ecological regions of Australia

Land units at the division, province and zone level in ASRIS are defined using broad physiography, climate, geologic and geomorphic criteria. Given the already overwhelming number of continental stratifications, we used the following approach:

Initially refine the three levels of the Physiographic Regions of Australia (Jennings and Mabbutt 1986) using the continental digital elevation model and the best available information on regolith. Note Jennings and Mabbutt’s (1986) use of the terms division, province and region is equivalent to division, province and zone in the ASRIS land unit hierarchy respectively.

The upper three levels of ASRIS hierarchy of land units (division, province, zone) have conformable boundaries. There is, however, a taxonomic hiatus between these levels (defined primarily by refinement of Jennings and Mabbutt 1986) and relying on broad genetic criteria) and the lower levels (district, system and facet).

The lower levels of the hierarchy are derived from the field-based surveys and mapping provided by state and territory agencies.

ASRIS includes the main continental regionalisations in common use, namely, the IBRA regions, groundwater flow systems, and agro-ecological regions. Catchment management boundaries are included because they are a key target group for ASRIS. It is envisaged that other regionalisations will be added if required.

Access to regionalisations beyond the primary land unit hierarchy (i.e., state and territory mapping at the facet, system and district level combined with the refined Jennings and Mabbutt (1986) land units) within ASRIS is intended to promote integration of natural resource information and more widespread use of soil and land data by non soil-science based groups.

The data summaries (e.g., for soil properties such as pH, exchangeable cations, hydraulic conductivity) in the ASRIS land unit hierarchy are of two basic types:

Area-weighted means (only for attributes where this is appropriate)

Histograms of attributes based on percentage area

These two options, when combined with estimates of uncertainty, should form a sufficient basis for most queries of the system. The provision of histograms is to ensure compatibility with modeling systems such as those used in hydrology that use distributional information rather than simple measures of central tendency (e.g., mean, median). It is also an essential step towards providing better measures of uncertainty for all users of soil and land information.

## Relationships between the land unit hierarchy and continental grids

A theoretical ideal would be to have estimates for all relevant soil and land attributes at all locations with an acceptable level of uncertainty for all forms of decision-making. A grid-based representation of these attributes would be convenient and ASRIS 2001 generated such coverages for selected soil properties using environmental correlation (i.e., point data from field measurements are correlated with environmental variables that are measured everywhere to produce predictions of soil attributes for all locations – see McKenzie and Ryan 1999, Bui et al. 2004, Grundy et al. 2004).  The land unit hierarchy provides another method for providing predictions at locations. Estimates are based on field observations or interpretations of soil variation within land unit tracts. While the mental models used to delineate and describe the land unit tracts are rarely explicit and sampling is purposive, the resulting maps have been useful for many purposes and they contain considerable information.

The land unit hierarchy has been prepared with this context and it is recognized that the predictions of individual attributes will often have a large uncertainty – we cannot estimate this uncertainty in an objective manner unless there is independent statistically based sampling (McKenzie and Ryan 2004).

The land unit hierarchy has another very important role. It can be used to stratify landscapes to allow:

More precise interpretations relating to landscape processes,

Development of robust environmental correlation models for predicting individual soil attributes using a grid-based approach.

The hierarchy of land units and grid-based methods for predicting soil and landscape attributes are complementary both for the analysis and interpretation of data.

Database development within ASRIS will therefore include not only the construction of the soil profile database for fully characterized profiles (i.e., with comprehensive analytical data), but also the development of a much larger soil profile database for all locations characterized during agency survey programs. This comprehensive database will include other sources of data if quality control and privacy considerations can be resolved (e.g., soil-testing data).  However, the initial priority is on development of the land unit hierarchy, interpretations of soil and land qualities, and the database of fully characterized representative profiles.

## Description of Land Facet and Land System Tracts

This version of the ASRIS specifications concentrates on land facet and land system tracts. Land facets are usually described but not mapped in most Australian land resource surveys.  However, the precision of the mapping varies considerably.  For example, the Atlas of Australian Soils uses very general soil-landscapes (equivalent here to land systems) with un-mapped land facets. In contrast, the soil-landscape mapping undertaken in New South Wales is more precise although it still maps soil-landscapes and describes unmapped land facets.

The land-unit hierarchy in ASRIS requires description of individual land system tracts and their component land facets. In some cases, individual land system tracts (i.e. unique mapping areas) may be described according to a land system type (i.e. according to Christian and Stewart’s (1968) original definition of a land system where individual land system tracts belong to the same land system type with the tracts having the same descriptive attributes). It would be preferable to have access to descriptions of each land system tract prior to grouping into a land system type but in many cases these data were never recorded (e.g. in the earlier CSIRO land system surveys).

# Accuracy, precision and a basis for stating uncertainty

## Rationale

Estimates of uncertainty for each attribute in ASRIS are needed to encourage more appropriate use of soil and land resource data. Uncertainty estimates are essential for the tracking of error propagation in various forms of analysis, particularly simulation modeling (e.g., Heuvelink 1998, Moss and Schneider 2000, Minasny and Bishop 2004). In many instances, the information on uncertainty generated by a model is as important as the prediction itself.

As far as possible, we have followed guidelines from the National Institute of Standards and Technology for evaluating and expressing uncertainty (Taylor and Kuyatt 1994, http://physics.nist.gov.cuu/Uncertainty).

Type A evaluations of standard uncertainty are based on any valid statistical method for treating data. These are not common in Australian soil and land resource survey. An example would be estimation of uncertainties in carbon or pH based on stratified random sampling of a land unit tract.

Type B evaluations of standard uncertainty are based on scientific judgement using all the relevant information available, which may include:

Previous measurement data on related soils

Experience with, or general knowledge of, the behaviour and properties of the relevant soils and measurement methods (e.g., accuracy of laboratory determinations and field description methods, reliability of pedotransfer functions)

Uncertainties published in reviews of soil spatial variability (e.g., Beckett and Webster 1971, Wilding and Drees 1983, McBratney and Pringle 1999)

## Estimating uncertainty

Most estimates of uncertainty in ASRIS rely on Type B evaluations. The form of the estimate depends on the measurement scale and assumed probability distribution for each attribute.

Continuous variables with an assumed Normal probability distribution have their uncertainty represented by an estimated standard deviation. This is denoted by ui and uj for Type A and B evaluations respectively. In most cases, an attribute’s uncertainty will arise from several sources and the combined standard uncertainty (uc) is reported. There are many issues to resolve in calculating uc, and it will often be appropriate to simply assume the component variances additive (i.e., uc = ((u12 + u22 + u32…) where u1, u2 and u3 are uncertainties attributable to different sources, for example, field estimation, a pedotransfer function, and spatial variability). Two components of uncertainty are recorded in ASRIS (see below) – Table 2 provides default values.

It is difficult to nominate the most appropriate error distribution for some variables. For example, some must be positive (e.g., CEC, layer thicknesses) so a Gamma distribution may be most appropriate but in practice it will be simpler to use a log-normal distribution. Other variables are bounded (e.g., clay content varies from 0–100%) and the assumptions of the Normal and Gamma distributions are violated so another approach is needed. We have adopted the following conventions.

Continuous variables that are not normally distributed are transformed to an approximately normal distribution and uncertainties are then estimated. Hydraulic conductivity and electrical conductivity are assumed to be distributed log-normally, unless there is evidence to the contrary. The mean is recorded in untransformed units to improve the ease of interpretation but the standard deviation is recorded as a transformed value. For example, the hydraulic conductivity may be estimated to be 100 mm/hr with a standard deviation of 0.5 log(mm/hr). The range of ± 1 standard deviation (i.e., 68% of the population) around the mean of 100 mm/hr would therefore be 32–320 mm/hr. The advantage of recording the transformed standard deviation is that that only one value is needed to represent dispersion of the asymmetric distribution.

Variables with fixed ranges (e.g., percentage coarse fragments) or coarse stepped scales are modeled with triangular probability distributions unless there is evidence to the contrary. The triangular probability distribution is assumed to be symmetric. The mean is estimated and dispersion is defined as (95% quantile – 5% quantile)/2. The distribution between the minimum value and the 5% quantile, and between the 95% quantile and the maximum, is assumed to be flat. The distribution is shown in Figure 2.

Uncertainties for nominal variables are represented by the probability that a class is correct (e.g., the uncertainty that a landform element type is a beach ridge is 0.8). Combined uncertainties are calculated by multiplying component probabilities.

Every soil attribute has an estimated uncertainty with two components.

The first component (u1) is associated with the measurement error for the given attribute at the profile or site – it will be significantly reduced if replicated sampling or bulking has been undertaken. If the attribute (e.g., water retention at –10 kPa) is being estimated using a pedotransfer function, then the uncertainty includes both the measurement error of the explanatory variables (e.g., texture, structure, and bulk density) and error due to model underlying the pedotransfer function.

The second component (u2) of uncertainty is due to spatial variability within the land unit tract at the lowest level in the hierarchy for which data are available.

In most parts of Australia, there is limited information on both of these sources of uncertainty and it will require good judgment to provide estimates. However, the alternative of providing estimates of mean values without information on variability is potentially misleading.

In the absence of better information, we will use default values of uncertainty drawn from the published literature on spatial variability and our general knowledge (Table 3). The default values are conservative (i.e., most likely on the high side) and intended to encourage more attention to the estimation of uncertainty. The component of uncertainty due to measurement (u1) can be determined using the estimation method for each variable as a guide (e.g., Table 22 for bulk density). The component of uncertainty due to spatial variability (u2) can be determined using several lines of evidence including:

cartographic scale of the survey and intensity of sampling (this is expressed via the Order of Survey (Table 6, Rossiter 1998, Soil Survey Staff 1993)), and

qualitative assessment of landscape complexity.

Figure 2: Examples of triangular probability distribution functions for coarse fragments. The mean, 5% and 95% quantiles are shown for the less variable layer.

Table 3: Default estimates of uncertainty for attributes of land-unit tracts in ASRIS – defaults for landform and land surface (relief, modal slope, element, pattern, microrelief, rock outcrop and surface coarse fragments) are yet to be determined.

| Attribute | Units (un-transformed) | Scale of measurement and probability distribution* | Attribute uncertainty due to measurement (u1) | Indicative Spatial Uncertainty (simple– complex landscape)** (u2) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Order 3 Survey | Order 4 Survey | Order 5 Survey |
| Texture |  | Nominal | 0.8 – S, LS, CS, MC, MHC, HC 0.7 – other classes | 0.4–0.7 | 0.2–0.8 | 0.1–0.9 |
| Clay content | % | Triangular | 10% | 10–20% | 20–30% | 30–40% |
| Coarse fragments | % | Triangular | 20% | 20–30% | 30–40% | 40–50% |
| Bulk density | Mg/m3 | Normal | 0.1 | 0.1–0.2 | 0.2–0.3 | 0.3–0.4 |
| pH |  | Normal | 0.2 | 0.2–0.5 | 0.5–1.0 | 1.0–2.0 |
| Organic carbon | % | Normal | 0.2 | 0.4–0.8 | 0.8–1.2 | 1.2–2.0 |
| Depth A1 | m | Triangular | 0.05 | 0.1–0.2 | 0.2–0.3 | 0.3–0.4 |
| Depth to B2 | m | Normal | 0.1 | 0.1–0.2 | 0.2–0.3 | 0.3–0.4 |
| Depth of solum | m | Normal | 0.2 | 0.2–0.4 | 0.4–0.6 | 0.6–1.0 |
| Depth to impeding layer | m | Normal | 0.2 | 0.2–0.4 | 0.4–0.6 | 0.6–1.0 |
| Depth of regolith | m | Normal | 0.3 | 0.3–1.0 | 1.0–2.0 | 2.0–3.0 |
| (–10 kPa | % | Normal | 2 | 2–4 | 4–6 | 6–8 |
| (–1.5MPa | % | Normal | 1 | 1–3 | 3–5 | 5–7 |
| Ksat | mm/hr | Log10-normal | 0.5 | 1–2 | 1.5–3 | 2–4 |
| Electrical conductivity | dS/m | Log10-normal | -1 | -0.7–-0.4 | -0.4–-0.2 | -0.2–-0.1 |
| Aggregate stability |  | Nominal | 0.9 | 0.8–0.7 | 0.7–0.6 | 0.6–0.4 |
| Sum of exchangeable bases | cmol(+)/kg | Normal | 0.5 | 0.5–1 | 1–4 | 4–8 |
| CEC | cmol(+)/kg | Normal | 0.5 | 0.5–1 | 1–4 | 4–8 |
| ESP | % | Normal | 1 | 1–2 | 2–4 | 4–8 |
| ASC (Great Group) |  | Nominal | 0.9 | 0.8–0.7 | 0.7–0.5 | 0.5–0.4 |
| WRB |  | Nominal | 0.8 | 0.7–0.6 | 0.6–0.4 | 0.4–0.1 |
| Substrate type |  | Nominal | 0.8 | 0.7–0.6 | 0.6–0.5 | 0.5–0.4 |
| Substrate permeability | mm/hr | Log10-normal | 0.5 | 1–2 | 1.5–3 | 2–4 |

* Uncertainty for Normally distributed attributes is estimated using the standard deviation (sd) – note 68% of observations are within ±1sd and 95% are within ±2sd.

** Spatial uncertainty includes the component due to measurement or estimation (i.e., u1) along with uncertainty arising from spatial variation within a land unit tract.

# Level-1 descriptors (land division)

The descriptors for Level 1 in the ASRIS hierarchy of land units characterize broad climate (precipitation, evaporation and temperature) and large-scale geologic structures (e.g. cratons, basins and blocks). Details will be provided in the next version of this document.

# Level-2 descriptors (land province)

The descriptors for Level 2 in the ASRIS hierarchy of land units characterize climate (precipitation, evaporation and temperature) and landscape evolution. Details will be provided in the next version of this document.

# Level-3 descriptors (land zone)

The descriptors for Level 3 in the ASRIS hierarchy of land units characterize climate, mesoclimate, median relief, and broadly defined lithological classes. Details will be provided in the next version of this document.

# Level-4 descriptors (land district)

The descriptors for Level 4 in the ASRIS hierarchy of land units characterize groupings of geomorphically related systems. Details will be provided in the next version of this document.

# Level-5 descriptors (land system)

## Identifiers

Most field-based land resource surveys in Australia collect information at Levels 5 and 6. In this section and the next, descriptors are specified for land unit tracts at the system and facet level. State and territory agencies will most commonly provide data at Level 5 (land system) with unmapped tracts at Level 6 (land facets). In some instances, land systems or land facets may be provided at two or more levels of detail (e.g., nested land systems with unmapped facets, or a land system with 2 levels of land facet). In some circumstances, the lowest level may only consist of land systems.

Most source data for ASRIS have been collected during particular projects that cover a specified area and defined period. Project and agency codes are provided with all data. In the case of soil profile data collected independently of survey projects, a miscellaneous code (MISC) is used along with the Agency Code. States and territories need to provide unique Level-5 identifiers for each land system tract. An extra identifier (proportion) is needed when the land-unit tract is described but not mapped. The identifiers are summarized in Table 4.

Table 4: Level-5 land unit tract identifiers

| Variable | Definition | Example and explanation | Comments |
| --- | --- | --- | --- |
| Agency code | SITES agency code | 505 |  |
| Project code | Agency code for the source survey | ALP58 (Alpine survey, 1958) | See ASRIS Website for a full listing of codes |
| Feature identification | Agency defined and unique number for the tract | mtk00245 |  |
| Hierarchy level | Level in the ASRIS land-unit hierarchy | 5.0 |  |
| Component identification | Unique code for the unmapped component if present | 0001 |  |
| Feature name | Plain text description of the land unit | Mt Kosciuszko land system | Text can also include a broad description of the tract (<240 characters) |
| Proportion | Areal occupied by the tract within the parent land unit | 60% | Only applicable when the land unit tract is described but not mapped |

## Mapping Intensity and Scale

#### Observations

The nature of observations within each land unit tract at Level 5 and 6 is recorded according to Table 5. Note that a field observation involves, as a minimum, completion of a full site and profile description according to McDonald et al. (1990).

Table 5: Nature of observations for land unit tract

| Class | Description |
| --- | --- |
| 1 | Multiple field observations recorded and extensive traverses |
| 2 | Single field observation and restricted traverses |
| 3 | Traverses |
| 4 | Characterization relies on field observations made in similar units in the same District (if tract is L5) or System (if tract is L6) |
| 5 | Characterization relies on remotely sensed information only |
| 6 | Unknown |

#### Order of survey

The order of survey used to generate the interpretations for each land unit tract is recorded according to Table 6 (for further details see Soil Survey Staff (1993, p48–49)).

Table 6: Orders of survey (modified from Soil Survey Staff (1993, p48–49))

| Order level | Intensity | Minimum size delineation (ha) | Cartographic scale for publication |
| --- | --- | --- | --- |
| 1 | Very intensive | 1 or less | 1:15,000 or more detailed |
| 2 | Intensive | 0.6 – 4 | 1:10,000 – 1:30,000 |
| 3 | Extensive | 1.6 – 16 | 1:20,000 – 1:50,000 |
| 4 | Extensive | 16 – 252 | 1:50,000 – 1:250,000 |
| 5 | Very Extensive | 252 – 4,000 | 1:250,000 – 1: million or less detailed |

#### Year of survey

The year of generation of the primary source of information used for the interpretations is recorded (the year of publication will usually be sufficient).

## Landform

#### Relief/modal slope

Relief and modal slope will be calculated for land unit tracts above and including the level of land system. Relief and modal slope classes will also be generated according to Table 5 of Speight (1990). The ASRIS team will undertake these tasks using the continent-wide 9-second digital elevation model. It is acknowledged that slopes will be underestimated in some landscapes as a result. Codes are provided in Table 7.

Table 7: Relief and modal slope classes

| Code | Code desciption |
| --- | --- |
| B | Badlands <9m >32% |
| B1 | Badlands 9-30m >56% |
| B2 | Badlands 30-90m >100% |
| GP | Gently undulating plains <9m 1-3% |
| GR | Gently undulating rises 9-30m 1-3% |
| LP | Level plain <9m <1% |
| PH | Precipitous hills 90-300m >100% |
| PM | Precipitous mountains >300m >100% |
| RH | Rolling hills 90-300m 10-32% |
| RL | Rolling low hills 30-90m 10-32% |
| RM | Rolling mountains >300m 10-32% |
| RP | Rolling plains <9m 10-32% |
| RR | Rolling rises 9-30m 10-32% |
| SH | Steep hills 90-300m 32-56% |
| SL | Steep low hills 30-90m 32-56% |
| SM | Steep mountains >300m 32-56% |
| SR | Steep rises 9-30m 32-56% |
| UH | Undulating hills 90-300m 3-10% |
| UL | Undulating low hills 30-90m 3-10% |
| UP | Undulating plains <9m 3-10% |
| UR | Undulating rises 9-30m 3-10% |
| VH | Very steep hills 90-300m 56-100% |
| VL | Very steep low hills 30-90m 56-100% |
| VM | Very steep mountains >300m 56-100% |

#### Landform pattern

Landform pattern is recorded using the terms in the glossary provided by Speight (1990, p48-57, Table 8).

#### Rock outcrop

Rock outcrop is the percentage of the land unit tract occupied by rock outcrop. This attribute is only recorded at Level 5 if data are not available for Level 6. Care is needed to avoid double counting with surface coarse fragments.

#### Surface coarse fragments

The areal percentage of surface coarse fragments is recorded as a percentage for the land unit tract but again only when Level-6 tracts are not described.  These variables are recorded for five size classes: gravelly (2–60mm) (cobbles (60-200 mm), stones (200-600 mm), boulders (600 mm – 2m) and large boulders (>2 m).

Table 8: Codes for landform pattern

| Code | Landform pattern | Code | Landform pattern |
| --- | --- | --- | --- |
| ALF | Alluvial fan | MAD | Made land |
| ALP | Alluvial plain | MAR | Marine plain |
| ANA | Anastomatic plain | MEA | Meander plain |
| BAD | Badlands | MET | Meteor crater |
| BAR | Bar plain | MOU | Mountains |
| BEA | Beach ridge plain | PAR | Parabolic dunefield |
| CAL | Caldera | PED | Pediment |
| CHE | Chenier plain | PEP | Pediplain |
| COR | Coral reef | PLA | Plain |
| COV | Covered plain | PLT | Plateau |
| DEL | Delta | PLY | Playa plain |
| DUN | Dunefield | PNP | Peneplain |
| ESC | Escarpment | RIS | Rises |
| FLO | Flood plain | SAN | Sand plain |
| HIL | Hills | SHF | Sheet-flood fan |
| KAR | Karst | STA | Stagnant alluvial plain |
| LAC | Lacustrine plain | TEL | Terraced land (alluvial) |
| LAV | Lava plain | TER | Terrace (alluvial) |
| LON | Longitudinal dunefield | TID | Tidal flat |
| LOW | Low hills | VOL | Volcano |

# Level-6 descriptors (land facets)

## Identifiers

In the previous section it was noted that in most land resource surveys in Australia, Level-6 land facets are described but not mapped. The areal percentage of each unmapped tract within its parent tract must be recorded to allow the calculation of area-weighted statistics within ASRIS. The identifiers for Level-6 land facets are presented in Table 9 for completeness – they are the same as those for Level-5 tracts.

Table 9: Level-6 land unit tract identifiers

| Variable | Definition | Example and explanation | Comments |
| --- | --- | --- | --- |
| Agency code | SITES agency code | 505 | See ASRIS Website for a full listing of valid codes |
| Project code | Agency code for the source survey | ALP58 (Alpine soil survey, 1958 – Bloggs et al. (1964)) | See ASRIS Website for a full listing of codes |
| Feature identification | Agency defined and unique code for the tract | mtk00245003 |  |
| Component identification | Unique code for the unmapped component if present | 0001 |  |
| Hierarchy level | Level in the ASRIS land-unit hierarchy | 6.0 |  |
| Feature name | Plain text description of the land unit | Feldmark on exposed slopes of Mt Kosciuszko | Text can also include a broad description of the tract (<240 characters) |
| Proportion | Areal percentage occupied by the tract within the parent land unit | 30% | Only applicable when the land unit tract is described but not mapped |

## Landform

The observations method-code (Table 5) is recorded and it forms the basis for assessing the uncertainty of estimates for morphologic type, landform element type, slope class, site drainage, rock outcrop, surface coarse fragments and microrelief.

#### Morphological type

The land facet is described using one of the ten morphologic types defined by Speight (1990, p13) and listed in Table 10.

Table 10: Landform morphological type

| Code | Code desciption |
| --- | --- |
| C | Crest |
| D | Closed Depression |
| F | Flat |
| H | Hillock |
| L | Lower-slope |
| M | Mid-slope |
| R | Ridge |
| S | Simple-slope |
| U | Upper-slope |
| V | Open depression (vale) |

#### Landform element type

Landform element is recorded using the terms in the glossary provided by Speight (1990, p24-34) and listed in Table 12.

#### Slope class

The average slope of the land facet is recorded in percent.

#### Site drainage

Site drainage is recording using the six classes defined by McDonald and Isbell (1990, p151) and shown in Table 11.

Table 11: Drainage classes

| Code | Code description |
| --- | --- |
| 1 | Very poorly drained |
| 2 | Poorly drained |
| 3 | Imperfectly drained |
| 4 | Moderately well drained |
| 5 | Well drained |
| 6 | Rapidly drained |

Table 12: Landform elements (after Speight 1990)

| Code | Landform element | Code | Landform element |
| --- | --- | --- | --- |
| ALC | Alcove | LAK | Lake |
| BAN | Bank | LDS | Landslide |
| BAR | Bar | LEV | Levee |
| BEA | Beach | LUN | Lunette |
| BEN | Bench | MAA | Maar |
| BER | Berm | MOU | Mound |
| BKP | Backplain | OXB | Ox-bow |
| BOU | Blow out | PED | Pediment |
| BRI | Beach ridge | PIT | Pit |
| BRK | Breakaway | PLA | Plain |
| CBE | Channel bench | PLY | Playa |
| CFS | Cliff-foot slope | PST | Prior stream |
| CIR | Cirque | REF | Reef flat |
| CLI | Cliff | RFL | Rock flat |
| CON | Cone | RPL | Rock platform |
| COS | Cut-over surface | SCA | Scarp |
| CRA | Crater | SCD | Scald |
| CUT | Cutface | SCR | Scroll |
| DAM | Dam | SFS | Scarp-foot slope |
| DDE | Drainage depression | SRP | Scroll plain |
| DOL | Doline | STB | Stream bed |
| DUC | Dunecrest | STC | Stream channel |
| DUN | Dune | STF | Supratidal flat |
| DUS | Duneslope | SUS | Summit surface |
| EMB | Embankment | SWL | Swale |
| EST | Estuary | SWP | Swamp |
| FAN | Fan | TAL | Talus |
| FIL | Fill-top | TDC | Tidal creek |
| FLD | Flood-out | TDF | Tidal flat |
| FOO | Footslope | TEF | Terrace flat |
| FOR | Foredune | TEP | Terrace plain |
| GUL | Gully | TOR | Tor |
| HCR | Hillcrest | TRE | Trench |
| HSL | Hillslope | TUM | Tumulus |
| ITF | Intertidal flat | VLF | Valley flat |
| LAG | Lagoon |  |  |

## Land Surface

Descriptions of the land surface are defined by: microrelief type, the described gilgai component (if present), biotic agent, and biotic component. The descriptors follow the definitions of McDonald et al. (1990) and the codes are presented in Table 13, Table 14, Table 15, and Table 16 respectively.

#### Rock outcrop

Rock outcrop is the percentage of the land unit tract (usually a land facet) occupied by rock outcrop. Care is needed to avoid double counting with surface coarse fragments.

#### Surface coarse fragments

The areal percentage of surface coarse fragments is recorded as a percentage for the land facet (Table 12) or land system if it is the lowest level recorded.  These variables are recorded for five size classes: gravelly (2–60mm), cobbles (60-200 mm), stones (200-600 mm), boulders (600 mm – 2m) and large boulders (>2 m).

Table 13: Microrelief type

| Code | Code desciption |
| --- | --- |
| Z | No microrelief |
| NR | Microrelief not recorded |
| A | Lattice gilgai |
| C | Crabhole gilgai |
| D | Debil-debil |
| G | Contour gilgai |
| H | Spring hollow |
| I | Sinkhole |
| K | Karst microrelief |
| L | Linear gilgai |
| M | Melonhole gilgai |
| N | Normal gilgai |
| O | Other |
| P | Spring mound |
| R | Terracettes |
| S | Mass movement microrelief |
| T | Contour trench |
| U | Mound/depression microrelief |
| W | Swamp hummock |

Table 14: Described gilgai component (if present)

| Code | Code desciption |
| --- | --- |
| D | Depression |
| M | Mound |
| S | Shelf |

Table 15: Biotic agent for microrelief (if present)

| Code | Code desciption |
| --- | --- |
| A | Ant |
| B | Bird |
| M | Man |
| N | Animal |
| O | Other |
| T | Termite |
| V | Vegetation |

Table 16: Biotic component of microrelief (if present)

| Code | Code desciption |
| --- | --- |
| D | Depression |
| H | Hole |
| M | Mound |
| O | Other |
| T | Terrace |

## Soil

Soil in the land-unit tract at the finest level of resolution (usually Level 6) is described using the following descriptors (unless the land unit is composed entirely of bare rock). If a land-unit tract (e.g., Level-6 land facet) has several component soils, then the land unit description remains the same with separate soil descriptions for each component.

Soil profiles can have horizons and stratigraphic units that vary greatly in their morphology, composition, dimensions, and arrangement. The soil profiles in the ASRIS profile database give an indication of this diversity. However, generalization and simplification are essential for the purposes of land evaluation and spatial analysis. For these reasons, a simplified profile model is used to describe soils in the land-unit hierarchy. The model uses the concept of control sections. This concept is used implicitly or explicitly in most systems of soil classification.

Each soil profile is represented by four control-sections for most soil properties (see Figure 3 for an example). The definitions of these sections have been developed with a primary focus on how a soil functions in relation to water and gas movement, nutrient supply, plant growth, and physical behavior more generally. Numbers are used to denote control sections (e.g., Layer-1 Texture), but they will often correspond with particular types of soil horizons.

Figure 3: Example control sections for a shallow texture-contrast soil

The soil data include a cross-reference to the ASRIS Soil Profile Database. The cross-reference is a link to a representative soil profile for the land unit tract along with a measure of its similarity (Table 17) – this measure will be possibly augmented with a multivariate statistical metric at a later date.

Table 17: Representativeness of the most similar soil profile in the ASRIS Soil Profile Database

| Similarity | Description |
| --- | --- |
| 1 | Representative profile sampled within the land unit tract |
| 2 | Representative profile sampled from the same land unit type |
| 3 | Representative profile for the soil profile class, and sampled within the region. |
| 4 | Representative profile from another district but allocated to the same taxon within the Australian Soil Classification |
| 5 | Most similar profile from the ASRIS soil profile database based on expert judgement |

#### Texture

Texture class and clay content (%) are estimated for four control sections. In Australia, field texture is not synonymous with the particle size distribution. The former integrates particle size information with extra aspects relating to soil mechanical behaviour – the latter is affected by mineralogy, sodicity, organic matter content and cation composition. Estimates of clay content based on field texturing should therefore take these factors into account. For example, a Red Ferrosol with 80% clay that is very strongly aggregated can have a clay-loam texture, while another soil with a clay content of only 35%, but strong sodicity and abundant fine sand, may have a heavy-clay texture.

Estimation methods for texture and clay content are recorded (Table 18 and Table 19). Field-texture follows the definitions in McDonald and Isbell (1990) – the codes are shown in Table 20. Use of the modifiers and qualifiers is optional.

Table 18: Estimation method for field texture

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of field texture in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of field texture in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

Table 19: Estimation method for clay content

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of field texture in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of field texture in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-1 Texture and clay content

The control section and convention for recording Layer-1 Texture and Clay Content is as follows.

If there is a single A1 horizon without subdivisions (e.g. A11, A12 etc.), then Layer-1 Texture and Clay Content is the texture and clay content of the A1 horizon.

If there are subdivisions within the A1 horizon, the Layer-1 Texture and Clay Content is taken from the thickest A horizon layer within the top 0.20 m of the soil profile (the upper layer is used if thicknesses are equal).

If the surface layer is an O horizon, the texture of the underlying A horizon is used in accord with the above criteria.  If there is no underlying A horizon, the Layer-1 Texture and Clay Content is taken from the thickest layer in the 0.20 m directly beneath the O horizon.

If the surface layer is a peat, Layer-1 Texture and Clay Content is recorded using the 7 classes of organic materials defined by McDonald and Isbell (1990) and shown in Table 20.

##### Layer-2 Texture and clay content

The Layer-2 Texture and Clay Content is the average texture of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon.

##### Layer-3 Texture and clay content

The B-horizon definition below follows the Field Handbook with the modification suggested by Isbell (1996) (the criteria in part being “…an illuvial concentration of silicate clay, iron, aluminium, humus, carbonates, gypsum, or silica, alone or in combination”). The Layer-3 Texture and Clay Content is defined as follows.

- If a B horizon is present, the Layer-3 Texture and Clay Content is the maximum texture (i.e. heaviest) encountered in the B1, B2 or B3 horizon.

- If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Texture and Clay Content is taken from the thickest layer in the 0.20 m directly below the A horizon.

##### Layer-4 Texture and clay content

The Layer-4 Texture and Clay Content is estimated at a depth between 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 3 estimate, then the Layer-4 Texture and Clay Content applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

Table 20: Field-texture grades, modifiers and qualifiers

| Code | Grade | Code | Modifiers and qualifiers |
| --- | --- | --- | --- |
| S | Sand | FS | Fine sand |
|  |  | MS | Medium sand |
|  |  | KS | Coarse sand |
|  |  | SA | Sapric sand |
|  |  | SI | Fibric sand |
| LS | Loamy sand | LFS | Loamy fine sand |
|  |  | LMS | Loamy medium sand |
|  |  | LKS | Loamy coarse sand |
|  |  | LSA | Sapric loamy sand |
|  |  | LSI | Fibric loamy sand |
| CS | Clayey sand | CFS | Clayey fine sand |
|  |  | CMS | Clayey medium sand |
|  |  | CKS | Clayey coarse sand |
|  |  | CSA | Sapric clayey sand |
|  |  | CSI | Fibric clayey sand |
| SL | Sandy loam | FSL | Fine sandy loam |
|  |  | MSL | Medium sandy loam |
|  |  | KSL | Coarse sandy loam |
|  |  | SLA | Sapric sandy loam |
|  |  | SLI | Fibric sandy loam |
| L | Loam | LA | Sapric loam |
|  |  | LI | Fibric loam |
| ZL | Silty loam | ZLA | Sapric silty loam |
|  |  | ZLI | Fibric silty loam |
| SCL | Sandy clay loam | SCLFS | Sandy clay loam, fine sand |
|  |  | SCLA | Sapric sandy clay loam |
|  |  | SCLI | Fibric sandy clay loam |
| CL | Clay loam | FSCL | Fine sandy clay loam |
|  |  | MSCL | Medium sandy clay loam |
|  |  | KSCL | Coarse sandy clay loam |
|  |  | CLA | Sapric clay loam |
|  |  | CLI | Fibric clay loam |
| CLS | Clay loam, sandy | CLFS | Clay loam, fine sandy |
|  |  | CLMS | Clay loam, medium sandy |
|  |  | CLKS | Clay loam, coarse sandy |
|  |  | CLSA | Sapric clay loam, sandy |
|  |  | CLSI | Fibric clay loam, sandy |
| ZCL | Silty clay loam | ZCLA | Sapric silty clay loam |
|  |  | ZCLI | Fibric silty clay loam |
| LC | Light clay | SLC | Sandy light clay |
|  |  | FSLC | Fine sandy light clay |
|  |  | MSLC | Medium sandy light clay |
|  |  | KSLC | Coarse sandy light clay |
|  |  | ZLC | Silty light clay |
|  |  | LCA | Sapric light clay |
|  |  | LCI | Fibric light clay |
| LMC | Light medium clay | ZLMC | Silty light medium clay |
|  |  | SLMC | Sandy light medium clay |
|  |  | FSLMC | Fine sandy light medium clay |
|  |  | MSLMC | Medium sandy light medium clay |
|  |  | KSLMC | Coarse sandy light medium clay |
|  |  | LMCA | Sapric light medium clay |
|  |  | LMCI | Fibric light medium clay |
| MC | Medium clay | ZMC | Silty medium clay |
|  |  | SMC | Sandy medium clay |
|  |  | FSMC | Fine sandy medium clay |
|  |  | MSMC | Medium sandy medium clay |
|  |  | KSMC | Coarse sandy medium clay |
|  |  | MCA | Sapric medium clay |
|  |  | MCI | Fibric medium clay |
| MHC | Medium heavy clay | ZMHC | Silty medium heavy clay |
|  |  | SMHC | Sandy medium heavy clay |
|  |  | FSMHC | Fine sandy medium heavy clay |
|  |  | MSMHC | Medium sandy medium heavy clay |
|  |  | KSMHC | Coarse sandy medium heavy clay |
|  |  | MHCA | Sapric medium heavy clay |
|  |  | MHCI | Fibric medium heavy clay |
| HC | Heavy clay | SHC | Sandy heavy clay |
|  |  | FSHC | Fine sandy heavy clay |
|  |  | MSHC | Medium sandy heavy clay |
|  |  | KSHC | Coarse sandy heavy clay |
|  |  | ZHC | Silty heavy clay |
|  |  | HCA | Sapric heavy clay |
|  |  | HCI | Fibric heavy clay |
| AP | Sapric peat |  |  |
| SP | Sandy peat |  |  |
| LP | Loamy peat |  |  |
| CP | Clayey peat |  |  |
| GP | Granular peat |  |  |
| HP | Hemic peat |  |  |
| IP | Fibric peat |  |  |

##### Layer-1 Coarse fragments

The control section for the Layer-1 Texture is adopted for the recording of coarse fragments. The abundance of Layer-1 coarse fragments is estimated as a percentage (if source data rely on the classes listed by McDonald et al. (1990, p97), then use midpoints of each class).

##### Layer-2 Coarse fragments

The control section for the Layer-2 Texture is adopted for the recording of coarse fragments. The abundance of Layer-2 coarse fragments is estimated as a percentage (if source data rely on the classes listed by McDonald et al. (1990, p97), then use midpoints of each class).

##### Layer-3 Coarse fragments

The control section for the Layer-3 Texture is adopted for the recording of coarse fragments. The abundance of Layer-3 coarse fragments is estimated as a percentage (if source data rely on the classes listed by McDonald et al. (1990, p97), then use midpoints of each class).

##### Layer-4 Coarse fragments

The control section for the Layer-4 Texture is adopted for the recording of coarse fragments. The abundance of Layer-4 coarse fragments is estimated as a percentage (if source data rely on the classes listed by McDonald et al. (1990, p97), then use midpoints of each class).

Table 21: Estimation method for coarse fragments

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of coarse fragments in an exposure or soil pit within the land unit tract |
| 2 | Estimate based on an un-replicated measurement of coarse fragments in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils |

#### Bulk density

The bulk density estimation method is recorded (Table 22) along with the bulk density for each layer.

##### Layer-1 Bulk density

The control section used for Layer-1 Texture is also used for Layer-1 Bulk Density. It is recorded with units of Mg/m3.

##### Layer-2 Bulk density

The Layer-2 Bulk Density is the average bulk density of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon.

Table 22: Estimation method for bulk density

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of bulk density in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of bulk density in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-3 Bulk density

The Layer-3 Bulk Density is estimated as follows.

In soils with a B2 horizon, the estimate is for the densest portion of the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Bulk Density is taken from the densest layer in the 0.20 m directly below the A horizon.

##### Layer-4 Bulk density

The control section for the Layer-4 Texture is adopted for the recording of Layer-4 Bulk Density.

#### pH profile

The pH in a 1:5 CaCl2 solution is estimated at four depths in the soil profile. If measurements have been performed using 1:5 soil-to-water, then use the conversion table in Appendix 1 taken from Henderson and Bui (2003). The estimation method is shown in Table 23.

##### Layer-1 pH

The Layer-1 pH is recorded as follows.

In most instances, the estimate applies to the upper 50 mm of the A1 horizon.

If the surface layer is an O horizon, the estimate applies to the upper 50 mm of the underlying A horizon.  If there is no underlying A horizon, the Layer-1 pH refers to the 50 mm thick layer directly beneath the O horizon.

If the surface layer is a peat, the estimate applies to the upper 50 mm of the surface horizon.

If the A1 horizon is thinner than 50 mm, then the estimate is for the horizon.

Table 23: Estimation method for pH

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of pH in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of pH in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-2 pH

The Layer-2 pH is the average pH of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon.

##### Layer-3 pH

The Layer-3 pH estimate in most cases is for the upper B horizon, and this is defined as follows.

In soils with a B2 horizon, the estimate is for the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 pH is taken from the layer 0.20 m directly below the A horizon.

##### Layer-4 pH

The Layer-4 pH is estimated at a depth between 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 3 estimate, then the Layer-4 pH applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

#### Organic carbon

Organic carbon is estimated at four depths in the soil profile. The estimation methods are shown in Table 24

Table 24: Estimation method for organic carbon

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of organic carbon in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of organic carbon in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-1 Organic carbon

The Layer-1 Organic carbon is recorded as follows.

In most instances, the estimate applies to the upper 50 mm of the soil profile.

If the A1 horizon is thinner than 50 mm, then the estimate is for the horizon.

##### Layer-2  Organic carbon

The Layer-2 Organic carbon is the average organic carbon content of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon.

##### Layer-3 Organic carbon

The estimate for this layer in most cases is the upper B horizon and this is defined as follows.

In soils with a B2 horizon, the estimate is for the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Organic carbon is taken from the layer 0.20 m directly below the A horizon.

##### Layer-4 Organic carbon

The Layer-4 Organic carbon is estimated at a depth between 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 3 estimate, then the Layer-4 Organic carbon applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

#### Depth

Six depths are recorded (m) to allow a flexible analysis of the estimates for soil properties (e.g., calculation of plant available water capacity). The estimation method is also recorded (Table 25).

Table 25: Estimation method for depths

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of depth in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of depth supplemented by opportunistic sampling (e.g. road cuttings) |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils and landscapes from other regions |

##### Depth of A1

The depth of A1 horizon is recorded in meters. If an A1 is not presented (e.g. OB profile), then the attribute is recorded as missing.

##### Depth to B2 horizon

The depth from the landsurface to the top of the B2 is recorded in meters.  If there is no B horizon (e.g. AC profile), then the combined thickness of the surface and near surface horizons is recorded (e.g. A, P, O)

##### Depth of solum

The thickness of the combined A and B horizons is recorded in meters.  Note that BC horizons are excluded.

##### Depth to impeding layer

The depth to impeding layer will in many cases be difficult to estimate.  An impeding layer prevents root growth beyond the layer. If sufficient information is available, the depth to impeding layer is estimated for:

Annual crops and pastures – ACP (e.g., wheat, barley, canola)

Perennial pastures – PP (e.g., lucerne), and

Perennial native vegetation – PNV (e.g., trees and shrubs).

##### Impeding layer type

Impeding layer type is recorded for each vegetation type (Table 26). Peverill et al. (1999) provide a basic reference on chemical toxicities and deficiencies.

##### Depth of regolith

Regolith refers to the “mantle of earth and rock, including weathered rocks and sediments, altered or formed by land surface processes” (Speight and Isbell 1990). The depth of regolith is estimated in meters.  It will be difficult to estimate in many instances, particularly in deeply weathered landscapes where depths greater than 100 m are not uncommon.

Table 26: Type of impeding layer

| Code | Type of impeding layer |
| --- | --- |
| CT | chemical toxicity (e.g., boron) |
| CD | chemical deficiency (e.g., very low or zero available P) |
| PI | direct physical impedance (e.g., moist soil strength > 4 MPa) |
| HY | hydrologic (e.g., permanent water table) |

Table 27: Estimation method for the type of impeding layer

| Code | Estimation method |
| --- | --- |
| 1 | Direct field observation of root patterns for the plant type (ACP, PP, PNV) with supporting soil analytical data within the land-unit tract |
| 2 | Interpretation of analytical data (relying on published limits for plants in question) |
| 3 | Direct field observation of root patterns for the plant type (ACP, PP, PNV) with supporting soil analytical data for similar soils in the region |
| 4 | Interpretation of analytical data (relying on published limits for plants in question) for similar soils in the region |
| 5 | General experience with morphologically similar soils |

#### Water retention and available water capacity

An estimate is made of the volumetric water content at –10 kPa (notional field capacity) and –1.5 MPa (notional wilting point) for four control sections.  An accompanying method code is also recorded (Table 28). The estimates of volumetric water content are averages for the relevant control section and the intention is to obtain estimates that allow calculation of an approximate profile available water capacity.  Note that these attributes can be estimated using Williams et al. (1992) on the basis of field texture, bulk density and structure grade.

Plant available water capacity can be estimated for the three generalized types of vegetation noted above (viz. annual crops and pastures, perennial pastures, and native trees and shrubs) by discounting the available water capacity for each layer. This discounting can be based on generalized models of root distribution and likely water extraction patterns (e.g., McKenzie et al. 2003) or through estimation of the non-limiting water range for each layer (e.g., using information on bulk density and nutrient availability).

The control sections are similar to those used for texture, coarse fragments and bulk density. The volumetric water contents at –10 kPa and –1.5 MPa are accompanied by the upper and lower depths over which the estimate is to be applied. Furthermore, the layers are contiguous so the total thickness of all layers must equal that of the complete profile (e.g., if a soil profile has an R horizon at 1.6m, then the thicknesses of the four layers must sum to 1.6m). As a result, the control section for estimating volumetric water contents at –10 kPa and –1.5 MPa may be thinner than the distance between the upper and lower depths. For example, the control section for estimating water contents for Layer 1 may be restricted to the top 0.20 m of the profile but the section to which it is applied may range from 0.00 m to 0.30 m. This is illustrated in . The approach is a compromise between practicality and the technical ideal of depth weighted averages for each layer – there are rarely sufficient data to justify the latter approach.

Figure 4: Control sections and layers used for estimating available water capacity for individual layers, and profile available water capacity.

##### Layer-1 (–10 kPa and (–1.5MPa

The control section and convention for recording Layer-2 (–10 kPa and (–1.5MPa is as follows.

If there is a single A1 horizon without subdivisions (e.g. A11, A12 etc.), then Layer-1 (–10 kPa and (–1.5MPa is for the A1 horizon.

If there are subdivisions within the A1 horizon, the Layer-1 (–10 kPa and (–1.5MPa is taken from the thickest A horizon layer within the top 0.20 m of the soil profile (the upper layer is used if thicknesses are equal).

If the surface layer is an O horizon, the (–10 kPa and (–1.5MPa of the underlying A horizon is used in accord with the above criteria.  If there is no underlying A horizon, the Layer-1 (–10 kPa and (–1.5MPa is taken from the thickest layer in the 0.20 m directly beneath the O horizon.

If the surface layer is a peat, Layer-1 (–10 kPa and (–1.5MPa is recorded only if direct measurements are available. Reliable pedotransfer functions for Australian conditions are not yet available and very few such soils have been characterized.

The upper and lower depths of the control section are recorded

##### Layer-2 (–10 kPa and (–1.5MPa

The Layer-2 (–10 kPa and (–1.5MPa is for the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon – in this instance, the estimates for Layer 2 can be recorded as zero as long as the Layer 1 estimates span the complete A horizon.

##### Layer-3 (–10 kPa and (–1.5MPa

The B-horizon definition below follows the Field Handbook with the modification suggested by Isbell (1996) (the criteria in part being “…an illuvial concentration of silicate clay, iron, aluminium, humus, carbonates, gypsum, or silica, alone or in combination”). The Layer-3 (–10 kPa and (–1.5MPa  is defined as follows.

- If a B horizon is present, the Layer-3 (–10 kPa and (–1.5MPa is the maximum texture (i.e. heaviest) encountered in the B1, B2 or B3 horizon.

- If no B horizon is present and the sequence consists of an AC profile, the Layer-3 (–10 kPa and (–1.5MPa is taken from the thickest layer in the 0.20 m directly below the A horizon.

Table 28: Estimation method for the estimation of water retention parameters

| Method | Description |
| --- | --- |
| 1 | Estimate derived from direct measurements of water retention in the land-unit tract |
| 2 | Water retention data estimated from direct measurements (e.g. Cresswell and Paydar (1996)) |
| 3 | Water retention data estimated using pedotransfer functions such as Williams et al. (1992) and with predictor variables derived from measurements in the land-unit type |
| 4 | Estimate based on direct measurements of similar soils |
| 5 | Estimate based on experience with similar soils |

##### Layer-4 (–10 kPa and (–1.5MPa

The Layer-4 (–10 kPa and (–1.5MPa is estimated at a depth between 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 3 estimate, then the Layer-4 (–10 kPa and (–1.5MPa applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

#### Permeability

The permeability of individual control sections is recorded using estimates of saturated hydraulic conductivity. A coarse stepped scale is presented in Table 29, the median values for each class are equidistant on a logarithmic scale because Ks data are generally log-normally distributed. The descriptive names are approximately the same as McDonald and Isbell (1990).  The accompanying method codes are presented in Table 30.

##### Layer-1 Ks

The Layer-1 Ks is for the soil surface.

If the soil has a surface crust or surface flake (McDonald et al. 1990), the estimate is for the upper 10 mm of the surface horizon.

If there is no surface crust or flake, the estimate applies to the upper 0.20 m of the A1 horizon if present. If the Layer-3 Ks control section upper boundary is within 0.20 m of the surface, Layer-1 Ks applies to the layer above the upper boundary of the Layer-3 Ks control section.

If the surface layer is an O horizon, the estimate applies to the upper 50 mm of the underlying A horizon.  If there is no underlying A horizon, the Layer-1 Ks refers to the 50 mm thick layer directly beneath the O horizon.

If the surface layer is a peat, the estimate applies to the upper 50 mm of the surface horizon.

If the A1 horizon is thinner than 50 mm, then the estimate is for the horizon.

##### Layer-2 Ks

The Layer-2 Ks is the average saturated hydraulic conductivity of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 200 mm, then Layer-2 Ks is recorded as missing.

##### Layer-3 Ks

In soils with a B2 horizon, the estimate is for the least permeable portion of the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Ks is taken from the least permeable layer in the 0.20 m directly below the A horizon.

##### Layer-4 Ks

The Layer-4 Ks is estimated as the least permeable layer between 1.0–3.0 m.  If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 3 estimate, then the Layer-4 Ks applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

Table 29: Permeability classes

| Class | Median Ks (mm/hr) | Class boundaries (mm/hr) |
| --- | --- | --- |
|  |  | 0 |
| Impermeable | 0.01 |  |
|  |  | 0.03 |
| Very slowly permeable | 0.1 |  |
|  |  | 0.3 |
| Slowly permeable | 1 |  |
|  |  | 3 |
| Moderately permeable | 10 |  |
|  |  | 30 |
| Highly permeable | 100 |  |
|  |  | 300 |
| Extremely permeable | 1000 |  |
|  |  | >>1000 |

Table 30: Estimation method for saturated hydraulic conductivity

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on direct laboratory measurements of saturated hydraulic conductivity using undisturbed soil cores within the land-unit type |
| 2 | Estimate based on direct field measurements of saturated hydraulic conductivity using permeameters within the land-unit type |
| 3 | Estimate based on pedotransfer functions using predictor variables from the land unit tract |
| 4 | Estimate based on direct measurements on similar soils |
| 5 | Estimate based on experience with similar soils |

#### Electrical conductivity

The electrical conductivity (EC) is estimated at four depths in the soil profile. The  estimation method is recorded according to Table 31. The electrical conductivity refers to a 1:5 soil:water extract and the units are dS/m.

##### Layer-1 EC

If there is a single A1 horizon without subdivisions (e.g. A11, A12 etc.), then estimate the Layer-1 EC using the A1 horizon.

If there are subdivisions within the A1 horizon, the Layer-1 EC is taken from the thickest A horizon layer within the top 0.20 m of the soil profile (the upper layer is used if thicknesses are equal).

If the surface layer is an O horizon, the underlying A horizon is used in accord with the above criteria.

If the surface layer is a peat, the estimate applies to the upper 0.20 m of the surface horizon.

##### Layer-2  EC

The Layer-2 EC is the average electrical conductivity of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon.

##### Layer-3 EC

In soils with a B2 horizon, the estimate is for the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 EC is taken from the layer 0.20 m directly below the A horizon.

##### Layer-4 EC

The Layer-4 EC is estimated at a depth of approximately 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer-3 estimate, then the Layer-4 EC applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

Table 31: Estimation method for electrical conductivity

| Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of electrical conductivity in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of electrical conductivity in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

#### Aggregate stability

Aggregate stability is estimated using a three-class system based on Emerson (2002) (Table 32) using the same control sections as for electrical conductivity. The method code is also recorded (Table 33).

Table 32: Aggregate stability classes based on Emerson (2002)

| Code | Class | Description |
| --- | --- | --- |
| S | Stable | Aggregates are stable in distilled water (e.g., Emerson Classes 1 and 2) |
| M | Moderately stable | Dispersion occurs after re-moulding when wet (e.g., Emerson Classes 3a and 3b ) |
| U | Unstable | Aggregates disperse spontaneously in distilled water (e.g., Emerson Classes 5 to 7) |

##### Layer-1 Aggregate stability

The control section and convention for recording Layer-1 Aggregate Stability is as follows.

If there is a single A1 horizon without subdivisions (e.g. A11, A12 etc.), then estimate the Layer-1 Aggregate Stability using the A1 horizon.

If there are subdivisions within the A1 horizon, the Layer-1 Aggregate Stability is taken from the surface layer.

If the surface layer is an O horizon, the underlying A horizon is used in accord with the above criteria.

If the surface layer is a peat, the estimate applies to the upper 0.20 m of the surface horizon.

Table 33: Estimation method for aggregate stability

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of aggregate stability in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of aggregate stability in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-2  Aggregate stability

The Layer-2 Aggregate Stability is estimated for the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon.

##### Layer-3 Aggregate stability

In soils with a B2  horizon, the estimate is for the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Aggregate Stability is taken from the layer 0.20 m directly below the A horizon.

##### Layer-4 Aggregate stability

The Layer-4 Aggregate Stability is estimated at a depth of approximately 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 3 estimate, then the Layer-4 Aggregate Stability applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

#### Water repellence

Water Repellence of the dry surface-soil layer is allocated to one of three levels according to

Table 34. The estimation method is also recorded (Table 35). The Molarity of Ethanol Drop (MED) test has been used by some survey agencies during recent years (see Carter 2002). The attribute is not mandatory but is recorded in regions where water repellence is significant for hydrology and plant growth.

Table 34: Water repellence (after Moore 1998).

| Code | Severity | Description |
| --- | --- | --- |
| N | None | Not significant (MED <1) |
| M | Moderate | Observed in most years and a strong manifestation 1 year in 3 (MED 1-2) |
| S | Severe | Strong manifestation in most years (MED >2) |

Table 35: Method for estimating water repellence of the land surface

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of water repellence in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of water repellence in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type and under a similar land management system |
| 4 | Estimate based on direct measurements of similar soils and land-use systems in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

#### Exchangeable bases, CEC, and ESP

Estimates of exchangeable bases (ie ((Ca+Mg+Na+K) in cmol/kg), CEC (cmol/kg), and Exchangeable Sodium Percentage (ESP) are made for four control sections.  Method codes describe both the estimation procedure (Table 36) and laboratory procedure – the latter is needed to distinguish between buffered and un-buffered methods (Table 37).

Table 36: Estimation method for exchangeable bases, CEC and ESP

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of exchangeable bases, CEC and ESP in the land unit tract |
| 2 | Estimate based on an un-replicated measurement of exchangeable bases, CEC and ESP in the land unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-1 Exchangeable bases, CEC, and ESP

In most instances, estimates for the three variables are for the upper 50 mm of the A1 horizon.

If the surface layer is an O horizon, the estimates apply to the upper 50 mm of the underlying A horizon.  If there is no underlying A horizon, the estimates refer to the 50 mm thick layer directly beneath the O horizon.

If the surface layer is a peat, the attributes are recorded as missing.

If the A1 horizon is thinner than 50 mm, then the estimate is for the horizon.

##### Layer-2 Exchangeable bases, CEC, and ESP

The Layer-2 Exchangeable Bases, CEC, and ESP are estimated for the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thinner than 100 mm, then the estimate is for the complete A horizon.

##### Layer-3 Exchangeable bases, CEC, and ESP

The estimate in most cases is the upper B horizon and this is defined as follows.

In soils with a B2 horizon, the estimate is for the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Exchangeable Bases, CEC, and ESP are taken from the layer 0.20 m directly below the A horizon.

##### Layer-4 Exchangeable bases, CEC, and ESP

The Layer-4 Exchangeable Bases, CEC, and ESP are estimated at a depth of approximately 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 3 estimate, then the Layer-4 Exchangeable Bases, CEC, and ESP applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

Table 37: Method codes for Sum Exchangeable Bases, CEC, and ESP (These are currently under review by the Working Group on Land Resource Assessment)

| Code | Code description |  |
| --- | --- | --- |
| 15A1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, no pretreatment for soluble salts |  |
| 15A2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, pretreatment for soluble salts |  |
| 15A3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, adjusted for soluble sodium |  |
| 15B1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, no pretreatment for soluble salts |  |
| 15B2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, pretreatment for soluble salts |  |
| 15B3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, adjusted for soluble sodium |  |
| 15C1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) - alcoholic 1M ammonium chloride at pH 8.5, pretreatment for soluble salts |  |
| 15D1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; manual leach |  |
| 15D2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; automatic extractor |  |
| 15D3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium acetate at pH 7.0, rapid method with no pretreatment for soluble salts |  |
| 15E1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) by compulsive exchange, no pretreatment for soluble salts |  |
| 15E2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) by compulsive exchange, pretreatment for soluble salts |  |
| 15E3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) by compulsive exchange, adjusted for soluble sodium |  |
| 15F1_BASES | Exchangeable bases by 0.01M silver-thiourea (AgTU)+, no pretreatment for soluble salts |  |
| Cation Exchange Capacity |  |
| 15B1_CEC | CEC – 1M ammonium chloride at pH 7.0, no pretreatment for soluble salts |  |
| 15B2_CEC | CEC – 1M ammonium chloride at pH 7.0, pretreatment for soluble salts |  |
| 15B3_CEC | CEC – 1M ammonium chloride at pH 7.0, adjusted for soluble sodium |  |
| 15C1_CEC | CEC - alcoholic 1M ammonium chloride at pH 8.5, pretreatment for soluble salts |  |
| 15D1_CEC | CEC – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; manual leach |  |
| 15D2_CEC | CEC – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; automatic extractor |  |
| 15E1_CEC | CEC by compulsive exchange, no pretreatment for soluble salts |  |
| 15E2_CEC | CEC by compulsive exchange, pretreatment for soluble salts |  |
| 15E3_CEC | CEC by compulsive exchange, adjusted for soluble sodium |  |
| 15F3_CEC | CEC by 0.01M silver-thiourea (AgTU)+ |  |
| 15I1_CEC | CEC measurement - distillation of ammonium ions |  |
| 15I2_CEC | CEC measurement - automated determination of ammonium ions |  |
| 15I3_CEC | CEC measurement - automated determination of ammonium and chloride ions |  |
| 15I4_CEC | CEC measurement - titration of ammonium and chloride ions |  |
| 15JG_CEC | Effective CEC using 15G1 for exchangeable acidity |  |
| 15JH_CEC | Effective CEC using 15H1 for exchangeable acidity |  |
| 15K1_CEC | CEC – pH 8.2 |  |

#### Australian Soil Classification

The Australian Soil Classification (Isbell 1996) is recorded at the Soil Order level as a minimum.  Recording at the Sub-Order or Great Group level along with the Family level is preferred but in some areas will not be feasible. The confidence levels, version and method for allocation are also recorded (Table 38, Table 39, and

Table 43)

Table 38: Confidence level for the allocation to the Australian Soil Classification

| Code | Code description |
| --- | --- |
| - | No confidence level recorded. |
| 1 | All necessary analytical data are available. |
| 2 | Analytical data are incomplete but reasonable confidence. |
| 3 | No analytical data are available but confidence is fair. |
| 4 | No analytical data and little or no knowledge of this soil. |

Table 39: Version of the Australian Soil Classification used for allocation

| Code | Code description |
| --- | --- |
| 2 | A Classification System for Australian Soils 2nd approximation |
| 3 | A Classification System for Australian Soils 3rd approximation |
| 4 | Australian Soil Classification 1st Edition |
| 5 | Australian Soil Classification Revised Edition |

Table 40: Codes for Soil Orders in the Australian Soil Classification

| Code | Soil Order | Code | Soil Order |
| --- | --- | --- | --- |
| AN | Anthroposol | KU | Kurosol |
| CA | Calcarosol | OR | Organosol |
| CH | Chromosol | PO | Podosol |
| DE | Dermosol | RU | Rudosol |
| FE | Ferrosol | SO | Sodosol |
| HY | Hydrosol | TE | Tenosol |
| KA | Kandosol | VE | Vertosol |

Table 41: Codes for Suborders, Great Groups and Subgroups in the Australian Soil Classification

| Code | Code description |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| AA | Red | BR | Epihypersodic | DL | Melanic-Bleached |
| AB | Brown | BS | Epic-Pedal | DM | Melanic-Mottled |
| AC | Yellow | BT | Extratidal | DN | Melanic-Vertic |
| AD | Grey | BU | Ferric | DO | Mellic |
| AE | Black | BV | Arenaceous | DP | Mesonatric |
| AF | Dystrophic | BW | Fibric | DQ | Mottled |
| AG | Mesotrophic | BX | Fluvic | DR | Subhumose |
| AH | Eutrophic | BY | Fragic | DS | Orthic |
| AI | Acidic | BZ | Gypsic | DT | Oxyaquic |
| AJ | Acidic-Mottled | CB | Calcarosolic | DU | Paralithic |
| AK | Andic | CC | Halic | DV | Parapanic |
| AL | Aeric | CD | Haplic | DW | Peaty |
| AM | Aquic | CE | Hemic | DX | Peaty-Parapanic |
| AN | Anthroposols | CF | Histic | DY | Pedal |
| AO | Arenic | CG | Humic | DZ | Petrocalcic |
| AP | Argic | CH | Chromosol | EA | Petroferric |
| AQ | Argillaceous | CI | Humic/Humosesquic | EB | Pipey |
| AR | Basic | CJ | Humic/Sesquic | EC | Placic |
| AS | Bauxitic | CK | Humose | ED | Redoxic |
| AT | Bleached | CL | Humose-Magnesic | EE | Rendic |
| AU | Bleached-Acidic | CM | Humose-Mottled | EF | Reticulate |
| AV | Bleached-Ferric | CN | Humose-Parapanic | EG | Salic |
| AW | Bleached-Leptic | CO | Humosesquic | EH | Sapric |
| AX | Bleached-Magnesic | CP | Hypervescent | EI | Self-Mulching |
| AY | Bleached-Manganic | CQ | Hypercalcic | EJ | Semiaquic |
| AZ | Bleached-Mottled | CR | Hypernatric | EK | Sesquic |
| BA | Bleached-Sodic | CS | Hypersalic | EL | Shelly |
| BB | Bleached-Vertic | CU | Epihypersodic-Epiacidic | EM | Silpanic |
| BC | Calcareous | CV | Hypocalcic | EN | Snuffy |
| BD | Calcic | CW | Intertidal | EO | Sodic |
| BE | Chernic | CX | Kurosolic | EP | Episodic-Epiacidic |
| BF | Chernic-Leptic | CY | Leptic | EQ | Sodosolic |
| BG | Chromosolic | CZ | Lithic | ER | Stratic |
| BH | Crusty | DA | Lithocalcic | ES | Subnatric |
| BI | Densic | DB | Magnesic | ET | Subplastic |
| BJ | Duric | DC | Manganic | EU | Sulfidic |
| BK | Pedaric | DD | Marly | EV | Sulfuric |
| BL | Endoacidic | DF | Massive | EW | Supratidal |
| BM | Endic | DG | Melacic | EX | Vertic |
| BN | Episodic | DH | Melacic-Magnesic | EY | Humose-Bleached |
| BO | Endic-Pedal | DI | Melacic-Mottled | EZ | Melacic-Bleached |
| BP | Endohypersodic | DJ | Melacic-Parapanic | FA | Siliceous |
| BQ | Epic | DK | Melanic | FB | Supracalcic |
| FC | Melanic-Calcareous | GU | Humose-Calcareous | IO | Brown-Orthic |
| FD | Natric | GV | Lutic | IP | Yellow-Orthic |
| FF | Submelacic | GX | Manganic-Acidic | IQ | Grey-Orthic |
| FG | Submelanic | GY | Humose-Acidic | IR | Black-Orthic |
| FH | Palic | GZ | Bleached-Orthic | IS | Ferric-Reticulate |
| FI | Ochric | HA | Melanic-Sodic | XX | Available Class Inappropriate |
| FJ | Hypergypsic | HB | Mottled-Sodic | YY | Class Undetermined |
| FK | Ferric-Duric | HC | Ferric-Sodic | ZZ | No Available Class |
| FL | Gypsic-Subplastic | HD | Rudaceous |  |  |
| FM | Epicalcareous-Epihypersodic | HE | Endocalcareous-Mottled |  |  |
| FN | Mottled-Subnatric | HF | Tephric |  |  |
| FO | Mottled-Mesonatric | HG | Carbic |  |  |
| FP | Mottled-Hypernatric | HH | Clastic |  |  |
| FQ | Dermosolic | HI | Colluvic |  |  |
| FR | Kandosolic | HJ | Lithosolic |  |  |
| FS | Terric | HK | Supravescent |  |  |
| FT | Humose-Basic | HL | Episulfidic |  |  |
| FU | Melacic-Basic | HM | Episulfidic-Petrocalcic |  |  |
| FV | Melanic-Acidic | HN | Densic-Placic |  |  |
| FW | Faunic | HO | Acidic-Sodic |  |  |
| FX | Lutaceous | HP | Palic-Acidic |  |  |
| FY | Epicalcareous | HQ | Ochric-Acidic |  |  |
| FZ | Endocalcareous | HR | Cumulic |  |  |
| GA | Epiacidic | HS | Hortic |  |  |
| GB | Epicalcareous-Endohypersodic | HT | Garbic |  |  |
| GC | Melacic-Reticulate | HU | Urbic |  |  |
| GD | Peaty-Placic | HV | Dredgic |  |  |
| GE | Ferric-Petroferric | HW | Spolic |  |  |
| GF | Regolithic | HX | Scalpic |  |  |
| GG | Episodic-Endoacidic | HZ | Ashy |  |  |
| GH | Episodic-Epicalcareous | IA | Inceptic |  |  |
| GI | Episodic-Endocalcareous | IB | Epibasic |  |  |
| GJ | Epicalcareous-Endoacidic | IC | Ceteric |  |  |
| GK | Epiacidic-Mottled | ID | Subpeaty |  |  |
| GL | Endoacidic-Mottled | IE | Effervescent |  |  |
| GM | Endocalcareous-Endohypersodic | IF | Folic |  |  |
| GN | Epihypersodic-Endoacidic | IG | Humosesquic/Sesquic |  |  |
| GO | Epihypersodic-Endocalcareous | IH | Humic/Alsilic |  |  |
| GP | Magnesic-Natric | IJ | Modic |  |  |
| GQ | Episodic-Gypsic | IK | Histic-Sulfidic |  |  |
| GR | Rudosolic | IL | Sequi-Nodular |  |  |
| GS | Epipedal | IM | Calcenic |  |  |
| GT | Tenosolic | IN | Red-Orthic |  |  |

Table 42: Codes for Family criteria in the Australian Soil Classification

| Code | Code description |  |  |
| --- | --- | --- | --- |
| - | Not recorded | M | Clay-loamy |
| A | Thin | N | Silty |
| B | Medium | O | Clayey |
| C | Thick | P | Granular |
| D | Very thick | Q | Fine |
| E | Non-gravelly | R | Medium fine |
| F | Slightly gravelly | S | Very fine |
| G | Gravelly | T | Very shallow |
| H | Moderately gravelly | U | Shallow |
| I | Very gravelly | V | Moderately deep |
| J | Peaty | W | Deep |
| K | Sandy | X | Very deep |
| L | Loamy | Y | Giant |

Table 43: Method for allocating profile to the classification system (either ASC or WRB)

| Method | Description based on: |
| --- | --- |
| 1 | Morphology and analytical data from the land-unit tract |
| 2 | Morphology data from the land-unit tract |
| 3 | Morphology and analytical data from similar soils in the same land unit type |
| 4 | Morphology data for similar soils in the region or project area |
| 5 | Experience with morphologically similar soils in other regions |

#### World Reference Base

Allocation to the World Reference Base to the level of the Reference Group with one or two qualifiers is preferred but conversion of historic data sets may not be possible in the short term. This attribute is required to ensure compatibility with SOTER.

Table 44: Reference Soil Group codes for the World Reference Base

| Code | Code description |  |  |
| --- | --- | --- | --- |
| AB | Albeluvisol | HS | Histosol |
| AC | Acrisol | KS | Kastanozem |
| AL | Alisol | LP | Leptosol |
| AN | Andosol | LV | Luvisol |
| AR | Arenosol | LX | Lixisol |
| AT | Anthrosol | NT | Nitisol |
| CH | Chernozem | PH | Phaeozem |
| CL | Calcisol | PL | Planosol |
| CM | Cambisol | PT | Plinthosol |
| CR | Cryosol | PZ | Podzol |
| DU | Durisol | RG | Regosol |
| FL | Fluvisol | SC | Solonchak |
| FR | Ferralsol | SN | Solonetz |
| GL | Gleysol | UM | Umbrisol |
| GY | Gypsisol | VR | Vertisol |

Table 45: Qualifiers for Reference Soil Groups in the World Reference Base

| Code | Qualifier | Code | Qualifier | Code | Qualifier |
| --- | --- | --- | --- | --- | --- |
| AB | Albic | FI | Fibric | LEN | Endoleptic |
| ABG | Glossalbic | FL | Ferralic | LEP | Epileptic |
| ABH | Hyperalbic | FLH | Hyperferralic | LI | Lithic |
| AC | Acric | FLW | Hypoferralic | LIP | Paralithic |
| AD | Aridic | FO | Folic | ME | Melanic |
| AE | Aceric | FR | Ferric | MG | Magnesic |
| AH | Anthropic | FRH | Hyperferric | MO | Mollic |
| AI | Aric | FU | Fulvic | MS | Mesotrophic |
| AL | Alic | FV | Fluvic | MZ | Mazic |
| AM | Anthric | GA | Garbic | NA | Natric |
| AN | Andic | GC | Glacic | NI | Nitic |
| ANA | Aluandic | GE | Gelic | OA | Oxyaquic |
| ANS | Silandic | GI | Gibbsic | OH | Ochric |
| AO | Acroxic | GL | Gleyic | OHH | Hyperochric |
| AP | Abruptic | GLN | Endogleyic | OM | Ombric |
| AQ | Anthraquic | GLP | Epigleyic | OR | Orthic |
| AR | Arenic | GM | Grumic | PA | Plaggic |
| AU | Alumic | GP | Gypsiric | PC | Petrocalcic |
| AX | Alcalic | GR | Geric | PD | Petroduric |
| AZ | Arzic | GS | Glossic | PE | Pellic |
| CA | Calcaric | GSM | Molliglossic | PF | Profondic |
| CB | Carbic | GSU | Umbriglossic | PG | Petrogypsic |
| CC | Calcic | GT | Gelistagnic | PH | Pachic |
| CCH | Hypercalcic | GY | Gypsic | PI | Placic |
| CCO | Orthicalcic | GYH | Hypergypsic | PL | Plinthic |
| CCW | Hypocalcic | GYW | Hypogypsic | PLH | Hyperplinthic |
| CH | Chernic | GZ | Greyic | PLO | Orthiplinthic |
| CL | Chloridic | HA | Haplic | PLP | Epiplinthic |
| CN | Carbonatic | HG | Hydragric | PLR | Paraplinthic |
| CR | Chromic | HI | Histic | PN | Planic |
| CT | Cutanic | HIB | Thaptohistic | PO | Posic |
| CY | Cryic | HIF | Fibrihistic | PP | Petroplinthic |
| DN | Densic | HIS | Saprihistic | PR | Protic |
| DU | Duric | HK | Hyperskeletic | PS | Petrosalic |
| DY | Dystric | HT | Hortic | PT | Petric |
| DYE | Epidystric | HU | Humic | PTP | Epipetric |
| DYH | Hyperdystric | HUM | Mollihumic | RD | Reductic |
| DYO | Orthidystric | HUU | Umbrihumic | RG | Regic |
| ES | Eutrisilic | HY | Hydric | RH | Rheic |
| ET | Entic | II | Lamellic | RO | Rhodic |
| EU | Eutric | IR | Irragric | RP | Ruptic |
| EUH | Hypereutric | IV | Luvic | RS | Rustic |
| EUN | Endoeutric | IVW | Hypoluvic | RU | Rubic |
| EUO | Orthieutric | IX | Lixic | RZ | Rendzic |
| FG | Fragic | LE | Leptic | SA | Sapric |
| SD | Spodic | SU | Sulphatic | TY | Takyric |
| SI | Silic | SZ | Salic | UB | Urbic |
| SK | Skeletic | SZN | Endosalic | UM | Umbric |
| SKN | Endoskeletic | SZP | Episalic | VI | Vitric |
| SKP | Episkeletic | SZW | Hyposalic | VM | Vermic |
| SL | Siltic | TF | Tephric | VR | Vertic |
| SO | Sodic | TI | Thionic | VT | Vetic |
| SON | Endosodic | TIO | Orthithionic | XA | Xanthic |
| SOW | Hyposodic | TIT | Protothionic | YE | Yermic |
| SP | Spolic | TR | Terric | YES | Nudiyermic |
| ST | Stagnic | TU | Turbic |  |  |
| STN | Endostagnic | TX | Toxic |  |  |

#### Local taxonomic class

If available, the local taxonomic class, established by soil and land resource survey, is recorded.  The local class will most commonly be a Soil Profile Class (Isbell 1988).

## Substrate

#### Substrate type

The substrate (as defined by Speight and Isbell 1990) is characterized using the codes and descriptions for regolith published in the ‘RTMAP database field guide and users guide’ (CRCLEME 2004) and shown in Table 46 and Table 47.

Table 46: Regolith material descriptions used for the characterization of substrate (Pain et al. 2004)

| Code | Regolith | Code | Regolith |
| --- | --- | --- | --- |
| BU00 | unweathered bedrock | SDS00 | coastal sediments |
| EVA00 | evaporite | SDS01 | beach sediments |
| EVA01 | halite | SDS02 | estuarine sediments |
| EVA02 | gypsum | SDS03 | coral |
| EVA03 | Calcrete | SDT00 | terrestrial sediments |
| SDA00 | alluvial sediments | UOC00 | clay (unknown origin) |
| SDA10 | channel deposits | UOM00 | weathered material (unknown origin) |
| SDA20 | overbank deposits | UOS00 | sand (unknown origin) |
| SDC00 | colluvial sediments | VOL00 | Volcanic sediments |
| SDC01 | scree | VOL01 | lava flow |
| SDC02 | landslide deposit | VOL02 | tephra |
| SDC03 | mudflow deposit | WIR10 | Saprolith |
| SDC04 | creep deposit | WIR11 | saprock |
| SDC05 | sheet flow deposit | WIR12 | moderately weathered bedrock |
| SDC06 | fanglomerate | WIR13 | highly weathered bedrock |
| SDE00 | aeolian sediments | WIR14 | very highly weathered bedrock |
| SDE01 | aeolian sand | WIR15 | completely weathered bedrock |
| SDE02 | loess | WIR15.1 | mottled zone |
| SDE03 | parna | WIR15.2 | pallid zone |
| SDF00 | fill | WIR16 | saprolite |
| SDG00 | glacial sediments | WIR20 | residual material |
| SDL00 | lacustrine sediments | WIR21 | lag |
| SDM00 | marine sediments | WIR22 | residual sand |
| SDP00 | swamp (paludal) sediments | WIR23 | residual clay |
| SDP01 | peat | WIR24 | soil on bedrock |

Table 47: Estimation method for substrate type

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on direct observation of substrate at the observation site(s) used for soil description |
| 2 | Estimate based on direct observations of substrate in the land-unit tract |
| 3 | Estimate based on direct observations of substrate in the same land-unit type within the region or project area |
| 4 | Estimate based on broad-scale regolith mapping for the area |
| 5 | Estimate based on geological mapping for the area |

#### Substrate permeability

The permeability of the substrate is estimated using the classes in Table 29. The estimate refers to the least permeable layer. Note that the substrate permeability may be the same as the Layer-4 Ks. Estimates are restricted to the upper 10 m.

Table 48: Estimation method for substrate permeability

| Method | Description |
| --- | --- |
| 1 | Estimate based on direct measurement of saturated hydraulic conductivity within the land-unit type |
| 2 | Estimate based on pedotransfer functions using predictor variables from the land unit tract |
| 3 | Estimate based on direct measurements on similar substrate materials |
| 4 | Estimate based on general knowledge of groundwater movement |
| 5 | Estimate based on experience with similar substrate materials |

# Soil Profile Database

As noted earlier, ASRIS includes a soil profile database that contains fully characterized sites that are known to be representative of significant areas and environments. The minimum data set is listed in Table 49. Further details on the ASRIS soil profile database will be included in the next version of this document.

Table 49: Recommended minimum data set for the ASRIS soil profile database

| Attribute | Method | Attribute | Method |
| --- | --- | --- | --- |
| Site | Soil chemical properties (major horizons) |
| Location |  | pH(1:5 CaCl2) |  |
| Type of observation |  | EC1:5 |  |
| Landform element |  | Organic carbon |  |
| Land use |  | Exch. Ca |  |
| Microrelief type |  | Exch. Mg |  |
| Surface coarse fragments |  | Exch. K |  |
| Rock outcrop |  | Exch. Na |  |
| Surface condition |  | CEC |  |
|  |  | Total P |  |
| Morphology (horizon/depth basis) | Available P |  |
| Horizon type |  | Total N |  |
| Depth |  | Total K |  |
| Boundary shape |  |  |  |
| Boundary distinctness |  | Soil Physical Properties (major horizons) |
| Colour hue, value, chroma |  | Bulk density |  |
| Mottle abundance |  | Particle size |  |
| Coarse fragment abundance |  | –10 kPa (v |  |
| Field pH |  | –1.5 MPa (v |  |
| Texture |  | Soil shrinkage |  |
| Structure grade |  | Dispersion class |  |
| Structure size |  | Saturated K |  |
| Structure type |  | Unsaturated K (–50mm) |  |
| Segregation abundance |  |  |  |
| Segregation type |  | Taxonomy |  |
| Carbonate effervescence |  | ASC (to Family level) |  |
|  |  | World Reference Base |  |

# GIS, database design and data transfer

The database design for ASRIS is presented in Figure 5. Definitions and formats used for the variables in each component database table are listed in the following tables. The full list of method codes, including those for the profile data, is available from the ASRIS team. When providing data to ASRIS, it is necessary to supply the necessary decode data and tables (e.g., the codes used for identifying officers responsible for soil descriptions). Identify instances where codes from McDonald et al. (1990) have not been used.

Figure 5: Database design for ASRIS. Definitions of variables are provided in the Tables below.

The procedure for data transfer from the relevant agencies to the ASRIS team has to be robust and updates must be easy to generate to ensure good quality assurance. A comprehensive EXCEL spreadsheet for data transfer is available from the ASRIS team. While it would be advantageous for agencies to provide data using the ASRIS database design, it is recognized that many field operators have difficulty with the sometimes abstract principles guiding relational database design and that most prefer the flat file format provided by a spreadsheet. However, referential integrity is necessary within the ASRIS database so ensure that unique identifiers are used for land-unit tracts. Avoid using upper or lower case letters as a means of creating unique keys. Also avoid including the letters o or i in unique keys wherever possible. Data transfer for the Representative Soil Profile Database within ASRIS should follow the SITES protocol (Kidston and McDonald 1995).

ASRIS is provided via the Internet using SQL Server, the ARC Spatial Data Engine, and ARC Internet Map Server. As a result, the spatial data should be supplied to ASRIS with a defined topology and in a format that can be imported to ARC Info. These data need a nominated projection and datum along with metadata conforming at least to ANZLIC standards. It would be advantageous for the polygon coverages to conform to the vector baseline GEODATA COAST 100K 1992.  This dataset contains boundaries for the coastline, states and territories. It is available as a free download from the Geoscience Australia website.

Table 50: The agencies table.

| Column Name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nnvarchar | 3 | no | Agency identifier |
| state_code | nnvarchar | 3 | no | State code i.e. NSW=1, VIC=2, QLD=3, SA=4, WA=5, TAS=6, NT=7, ACT=8 |
| agency_name | nnvarchar | 240 | no | Name of agency |
| agency_acronym | nnvarchar | 10 | yes | Agency acronym, e.g. WADA |

Table 51: The projects table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| project_name | nvarchar | 240 | no | Project name |
| project_contact | nvarchar | 4 | no | Project contact officer |
| project_biblio_ref | nvarchar | 240 | yes | Bibliographic reference |

Table 52: The site_location table.

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 10 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| site_lat | numeric | 9 | yes | Latitude decimal degrees |
| site_long | numeric | 9 | yes | Longitude decimal degrees |
| site_east | numeric | 9 | yes | Australian Map Grid Easting |
| site_north | numeric | 9 | yes | Australian Map Grid Northing |
| site_zone | nvarchar | 3 | yes | Australian Map Grid Zone |
| site_datum | nvarchar | 10 | yes | Datum |
| site_spheroid | nvarchar | 10 | yes | Spheroid |
| loc_method | nvarchar | 15 | yes | Location method (e.g. hand held GPS, 1:100,000 mapsheet) |

Table 53: The features table.

| Column Name | Data type | Length | Nullable | Description |  |
| --- | --- | --- | --- | --- | --- |
| agency_code | nnvarchar | 3 | no | Agency identifier |
| project_code | nnvarchar | 10 | no | Project identifier |
| feature_id | nnvarchar | 10 | no | Feature identifier |
| component_id | nnvarchar | 30 | no | Unmapped component identifier |
| proportion | int | 4 | no | Feature proportion if component_id=0 otherwise component proportion |
| feature_type | nnvarchar | 2 | no | Feature type, e.g. point, tract |
| hierarchy | nnvarchar | 3 | no | Level of ASRIS hierarchy |
| feature_name | nnvarchar | 30 | yes | Name of the feature |
| ref_agency_code | nnvarchar | 3 | yes | Parent feature's agency code |
| ref_project_code | nnvarchar | 10 | yes | Parent feature's project code |
| ref_feature_id | nnvarchar | 10 | yes | Parent feature's feature code |
| ref_component_id | nnvarchar | 30 | no | Parent feature's component identifier |

Table 54: The feature notes table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nnvarchar | 3 | no | Agency identifier |
| project_code | nnvarchar | 10 | no | Project identifier |
| feature_id | nnvarchar | 10 | no | Feature identifier |
| component_id | nnvarchar | 30 | no | Unmapped component identifier |
| notes | nnvarchar | 240 | yes | Feature notes if component_id = 0 otherwise notes refers to the component |

Table 55: The samples table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 10 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| samp_no | int | 4 | no | Sample number |
| samp_type | nvarchar | 15 | yes | Type of sample (e.g. fine earth, whole soil) |
| samp_method | nvarchar | 15 | yes | Sampling method |
| samp_upper_depth | numeric | 5 | yes | Sample upper depth (m) |
| samp_lower_depth | numeric | 5 | yes | Sample lower depth (m) |
| samp_desc | nvarchar | 240 | yes | Sample description |

Table 56: The sample notes table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 10 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| samp_no | int | 4 | no | Sample number |
| samp_notes | nvarchar | 240 | yes | Sample notes |

Table 57: The results table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 10 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| samp_no | int | 4 | no | Sample number |
| res_no | int | 4 | no | Result number |
| param_char_id | nvarchar | 20 | no | Parameter method identifier (categorical data) |
| param_num_id | nvarchar | 20 | no | Parameter method identifier (continuous data) |
| parameter_type | nvarchar | 20 | no | Qualifier for the parameter (e.g. control section layer, lithology, A horizon) |
| res_value_type | nvarchar | 1 | yes | (Value type, e.g. maximum, minimum, mean) |
| res_value_pref | nvarchar | 1 | yes | Value prefix (e.g. –, <, >) |
| res_char_value | nvarchar | 25 | yes | Character value |
| res_num_value | numeric | 5 | no | Numerical value |
| res_proportion | int | 4 | yes | Percentage of area the value represents |
| res_uc1 | numeric | 5 | yes | Result uncertainty1 |
| res_uc_type1 | nvarchar | 2 | yes | Uncertainty type1 |
| res_uc2 | numeric | 5 | yes | Result uncertainty2 |
| res_uc_type2 | nvarchar | 2 | yes | Uncertainty type2 |

Table 58: The parameter_num_method table.

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| param_num_id | nvarchar | 20 | no | Parameter method identifier |
| parameter | nvarchar | 20 | no | Parameter measured (e.g. pH, organic carbon) |
| parameter_desc | nvarchar | 240 | yes | Method description |
| param_method_units | nvarchar | 10 | yes | Units of measurement |
| param_method_ref | nvarchar | 20 | yes | Technical reference for the method |
| error | numeric | 5 | yes | Error of measurement |
| min_detect | numeric | 5 | yes | Minimum detection limit |
| max_detect | numeric | 5 | yes | Maximum detection limit |
| correction | numeric | 5 | yes | Required corrections |

Table 59: The param_char_method table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nnvarchar | 3 | no | Agency identifier |
| param_char_id | nnvarchar | 20 | no | Parameter method identifier e.g. texture, mottle abundance, segregation form |
| code_value | nnvarchar | 25 | no | Code value (e.g. LC, 2, N) |
| parameter | nnvarchar | 20 | no | Parameter measured (e.g. pH, texture, depth, mottles) |
| code_desciption | nnvarchar | 128 | yes | Code description (e.g. light clay, few 2-10%, nodules) |

Table 60: The param_ char_refs table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| param_char_id | nnvarchar | 20 | no | Parameter method identifier (e.g. texture, mottle abundance, segregation form) |
| code_reference | nnvarchar | 50 | yes | Page of reference from McDonald et al. (1990) |

Table 61: The codes table.

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nnvarchar | 3 | no | Agency identifier |
| code_domain | nnvarchar | 20 | no | Code domain |
| code_value | nnvarchar | 20 | no | Code value |
| code_parameter | nnvarchar | 20 | no | Parameter measured (e.g. officers, feature type) |
| code_desciption | nnvarchar | 128 | yes | Code description |

# Relationship to SOTER

ASRIS has been designed to facilitate the Australian contribution to SOTER – this is the new global soil and land resource information system. Details on the conversion protocols will be provided in the next version of this document.

# References

Austin, MP, Basinski JJ (1978) Bio-physical survey techniques. In Land use on the South Coast of New South Wales.  A study in methods of acquiring and using information to analyse regional land use options. Volume 1. General report. (General Eds. MP Austin and KD Cocks).

Beckett PHT (1968) Method and scale of land resource srveys, in relation to precision and cost.  In Land evaluation. (Ed. GA Stewart). (MacMillan: Melbourne).

Beckett PHT, Bie, SW (1978) Use of soil and land system maps to provide soil information in Australia.  CSIRO Aust. Div Soils Tech. Paper No. 33.

Carter DJ (2002) Water repellence. In Soil physical measurement and interpretation for land evaluation.  Australian Soil and Land Survey Handbook Series Vol. 5. (Eds McKenzie NJ, Coughlan K, Cresswell HP) (CSIRO Publishing: Melbourne).

Chan RA (1986) Regolith terrain map of Australia 1:5 000 000. Record 1986/27. Bureau of Mineral Resources, Geology and Geophysics, Canberra.

Christian CS Stewart GA (1968).  Methodology of integrated surveys. In Aerial surveys and integrated studies. Proceedings of the Tolouse Conference of 1964. (UNESCO: Paris).

Cresswell HP, Paydar Z (1996) Water retention in Australian soils. I. Description and prediction using parametric functions. Australian. Journal of Soil Research 34, 195–212.

Dent D, Young A (1981). Soil survey and land evaluation. (George Allen and Unwin: London).

Emerson WW (2002) Emerson dispersion test. In Soil physical measurement and interpretation for land evaluation.  Australian Soil and Land Survey Handbook Series Vol. 5. (Eds McKenzie NJ, Coughlan K, Cresswell HP) (CSIRO Publishing: Melbourne).

Gibbons FR (1983). Soil mapping in Australia. In Soils: an Australian viewpoint. CSIRO Aust. Div. Soils. (CSIRO: Melbourne\Academic Press: London).

Gunn RH, Beattie JA, Reid RE, van de Graaff RHM (1988) Australian soil and land survey handbook:  guidelines for conducting surveys. (Inkata Press: Melbourne).

Heuvelink GBM (1998) Error propagation in environmental modelling with GIS. (Taylor and Francis: London).

Kidston L, McDonald WS (1995) Soil information transfer and evaluation system user manual. ACLEP Technical Report No. 5, (CSIRO Division of Soils: Canberra).

King, PM (1981). Comparison of methods for measuring severity of water repellence of sandy soils and assessment of some factors that affect its measurement. Australian Journal of Soil Research 19, 275–285.

Mabbutt JA (1968) Review of concepts of land evaluation. In Land evaluation. (Ed. GA Stewart). (MacMillan: Melbourne).

Minasny B, Bishop T (2004) Uncertainty analysis. In Guidelines for conducting surveys 2nd edition. Australian Soil and Land Survey Handbook Series Volume 2. (CSIRO Publishing: Melbourne) (in press).

McBratney AB, Pringle MJ (1999) Estimating proportional and average variograms of soil properties and their potential use in precision agriculture. Precision Agriculture, 1, 125–152.

McDonald RC, Isbell RF (1990). Soil profile. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS (1990). Australian soil and land survey field handbook. 2nd Edn.  (Inkata Press:  Melbourne).

McKenzie NJ (1991) A strategy for coordinating soil survey and land evaluation in Australia.  CSIRO Division of Soils, Divisional Report No. 114.

Moore G (1998) Soilguide: A handbook for understanding and managing agricultural soils. Agriculture Western Australia, Bulletin 4343.

Moss RH, Schneider SH (2000) Uncertainties in the IPCC Third Assessment Report. Recommendations to lead authors for more consistent assessment and reporting. In Guidance Papers on the Cross Cutting Issues of the Third Assessment Report of the IPCC (Eds R Pachauri, T Taniguchi, K Tanaka) (World Meteorological Organization: Geneva).

Northcote KH (1984) Soil-landscapes, taxonomic units and soil profiles.  A personal perspective on some unresolved problems of soil survey.  Soil Survey and Land Evaluation, 4, 1–7.

Pain C, Chan R, Craig M, Gibson D, Kilgour P, Wilford J (in press) RTMAP regolith database field book and users guide (second edition). CRC LEME Report 138.

Raupach M, Tucker BM (1959) The field determination of soil reaction.  J. Aust. Inst. Agric. Sci. 25, 129–133.

Speight JG (1988) Land classification. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Speight JG (1990) Landform. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Speight JG, Isbell RF (1990) Substrate. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Steur GGL (1961) Methods of soil surveying in use at the Netherlands Soil Survey Institute. Boor en Spade 11, 59–77.

Stewart GA (1968) Land evaluation. (MacMillan: Melbourne).

Taylor BN, Kuyatt CE (1994) Guidelines for evaluating and expressing the uncertainty of NIST measurement results. NIST Technical Note 1297, United States Government Printing Office, Washington.

Walker J, Hopkins MS (1990) Vegetation. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Wilding LP, Drees LR (1983) Spatial variability and pedology. In ‘Pedogenesis and Soil Taxonomy. I Concepts and interactions.’  (Eds LP Wilding, NE Smeck and GF Hall) Developments in Soil Science 11A (Elsevier: Amsterdam).

Williams J, Ross PJ, Bristow KL (1992) Prediction of the Campbell water retention function from texture, structure and organic matter. In Proc.international workshop on indirect methods for estimating the hydraulic properties of unsaturated soils. (Eds. M Th van Genuchten, FJ Leij, LJ Lund) Univ. of California, Riverside, CA.

# Appendix: Conversion for pH in water to pH in CaCl2

The conversion table for pH in water (1:5 soil to water) to pH in CaCl2 (1:5 soil to 0.01M CaCl2) is from Henderson and Bui (2002). It is based on 70,465 observations collated to support ASRIS 2001. The values in italics are to be regarded as more doubtful extrapolations of the statistical curve because they are supported by a smaller number of observations.

Table 62: Conversion for pH in water to pH in CaCl2.

| Observed pH water | Predicted pH CaCl2 | Observed pH water | Predicted pH CaCl2 | Observed pH water | Predicted pH CaCl2 |
| --- | --- | --- | --- | --- | --- |
| 3.0 | 2.8 | 5.4 | 4.6 | 7.8 | 7.2 |
| 3.1 | 2.9 | 5.5 | 4.7 | 7.9 | 7.3 |
| 3.2 | 3.0 | 5.6 | 4.8 | 8.0 | 7.4 |
| 3.3 | 3.0 | 5.7 | 4.9 | 8.1 | 7.5 |
| 3.4 | 3.1 | 5.8 | 5.0 | 8.2 | 7.5 |
| 3.5 | 3.2 | 5.9 | 5.1 | 8.3 | 7.6 |
| 3.6 | 3.2 | 6.0 | 5.2 | 8.4 | 7.7 |
| 3.7 | 3.3 | 6.1 | 5.3 | 8.5 | 7.8 |
| 3.8 | 3.4 | 6.2 | 5.4 | 8.6 | 7.8 |
| 3.9 | 3.5 | 6.3 | 5.5 | 8.7 | 7.9 |
| 4.0 | 3.5 | 6.4 | 5.7 | 8.8 | 8.0 |
| 4.1 | 3.6 | 6.5 | 5.8 | 8.9 | 8.0 |
| 4.2 | 3.7 | 6.6 | 5.9 | 9.0 | 8.1 |
| 4.3 | 3.7 | 6.7 | 6.0 | 9.1 | 8.2 |
| 4.4 | 3.8 | 6.8 | 6.2 | 9.2 | 8.2 |
| 4.5 | 3.9 | 6.9 | 6.3 | 9.3 | 8.3 |
| 4.6 | 3.9 | 7.0 | 6.4 | 9.4 | 8.4 |
| 4.7 | 4.0 | 7.1 | 6.5 | 9.5 | 8.4 |
| 4.8 | 4.1 | 7.2 | 6.6 | 9.6 | 8.5 |
| 4.9 | 4.2 | 7.3 | 6.7 | 9.7 | 8.6 |
| 5.0 | 4.2 | 7.4 | 6.8 | 9.8 | 8.7 |
| 5.1 | 4.3 | 7.5 | 6.9 | 9.9 | 8.7 |
| 5.2 | 4.4 | 7.6 | 7.0 | 10.0 | 8.8 |
| 5.3 | 4.5 | 7.7 | 7.1 | 10.1 | 8.9 |

# Footnotes

The term land capability was used in the original brief – this term is usually associated with the United States Department of Agriculture eight-class system for classifying land. The term land suitability is preferred here (see Dent and Young 1981; McKenzie 1991).

A missing value is recorded as -99 for numeric fields and NA for alphanumeric fields

See http://lime.isric.nl/index.cfm?contentid=236 for information on SOTER

# Text boxes

(ASRIS)

Land resource survey (ASRIS)

Land condition monitoring