The Australian Soil Resource Information System

Technical specifications

www.asris.csiro.au

Australian Collaborative Land Evaluation Program

Prepared by Neil McKenzie, David Jacquier and David Maschmedt on behalf of the Working Group on Land Resource Assessment

Version 1.4

10th March 2005

1.	Summary	7

2.	User needs for soil and land resource information	9

2.1	Reducing risks in decision making	9

2.2	Improving process understanding	10

2.3	Mapping, monitoring, modeling, and environmental history	10

2.4	Land condition	12

2.5	Striking a balance between general-purpose and problem-specified information	13

2.6	The task of interpretation	13

3.	Development of ASRIS	15

4.	Hierarchy of land units and terminology	17

4.1	Concepts and terms	17

4.2	Upper levels of the hierarchy	20

4.3	Relationships between the land unit hierarchy and continental grids	22

4.4	Description of Land Facet and Land System Tracts	22

5.	Accuracy, precision and a basis for stating uncertainty	24

5.1	Rationale	24

5.2	Estimating uncertainty	24

6.	Level-1 descriptors (land division)	28

7.	Level-2 descriptors (land province)	30

8.	Level-3 descriptors (land zone)	32

8.	Level-3 descriptors (land zone)	32

9.	Level-4 descriptors (land district)	33

10.	Level-5 descriptors (land system)	34

10.1	Identifiers	34

10.2	Mapping Intensity and Scale	35

10.3	Landform	36

11.	Level-6 descriptors (land facets)	38

11.1	Identifiers	38

11.2	Landform	39

11.3	Land Surface	40

11.4	Soil	42

11.5	Substrate	69

12.	Soil Profile Database	72

13.	Data conventions, transfer procedures and database design	73

13.1	Missing data, explicit zeros and explanatory notes	73

13.2	Database design	73

14.	Relationship to SOTER	79

15.	References	80

Appendix 1: Conversion for pH in water to pH in CaCl2	84

Appendix 2: Updates to the Technical Specifications	85

Table 1: Complementary benefits of mapping (contained within ASRIS), monitoring and modelling	12

Table 2: The main soil properties included in ASRIS and their significance	14

Table 3: The spatial hierarchy of land-unit tracts (after Speight 1988). Note that the database design for ASRIS allows intermediate Levels to be characterized (e.g., a System with a characteristic dimension significantly less that 100 m would be designated as Level 5.1 or 5.2 in the hierarchy)	20

Table 4: Default estimates of uncertainty for attributes of land-unit tracts in ASRIS – defaults for landform and land surface (relief, modal slope, element, pattern, microrelief, rock outcrop and surface coarse fragments) are yet to be determined.	27

Table 5: Level-5 land-unit tract identifiers	34

Table 6: Nature of observations for land-unit tract	35

Table 7: Orders of survey (modified from Soil Survey Staff (1993, p48–49))	35

Table 8: Relief and modal slope classes	36

Table 9: Codes for landform pattern	37

Table 10: Level-6 land-unit tract identifiers	38

Table 11: Landform morphological type	39

Table 12: Drainage classes	39

Table 13: Landform elements (after Speight 1990)	40

Table 14: Microrelief type	41

Table 15: Described gilgai component (if present)	41

Table 16: Biotic agent for microrelief (if present)	42

Table 17: Biotic component of microrelief (if present)	42

Table 18: Representativeness of the most similar soil profile in the ASRIS Soil Profile Database	44

Table 19: Estimation method for field texture	45

Table 20: Estimation method for clay content	45

Table 21: Field-texture grades, modifiers and qualifiers	47

Table 22: Estimation method for coarse fragments	49

Table 23: Estimation method for bulk density	50

Table 24: Estimation method for pH	51

Table 25: Estimation method for organic carbon.	52

Table 26: Estimation method for depths and layer thicknesses	52

Table 27: Type of impeding layer	53

Table 28: Estimation method for the type of impeding layer	54

Table 29: Estimation method for the estimation of water retention parameters	55

Table 30: Permeability classes	58

Table 31: Estimation method for saturated hydraulic conductivity	58

Table 32: Estimation method for electrical conductivity	60

Table 33: Aggregate stability classes based on Emerson (2002)	60

Table 34: Estimation method for aggregate stability	61

Table 35: Water repellence (after Moore 1998).	61

Table 36: Method for estimating water repellence of the land surface	61

Table 37: Estimation method for exchangeable bases, CEC and ESP	62

Table 38: Method codes for Sum Exchangeable Bases, CEC, and ESP (These are currently under review by the Working Group on Land Resource Assessment)	63

Table 39: Confidence level for the allocation to the Australian Soil Classification	64

Table 40: Version of the Australian Soil Classification used for allocation	64

Table 41: Codes for Soil Orders in the Australian Soil Classification	64

Table 42: Codes for Suborders, Great Groups and Subgroups in the Australian Soil Classification	64

Table 43: Codes for Family criteria in the Australian Soil Classification	66

Table 44: Method for allocating profile to the classification system (either ASC or WRB)	67

Table 45: Reference Soil Group codes for the World Reference Base	67

Table 46: Qualifiers for Reference Soil Groups in the World Reference Base	68

Table 47: Regolith material descriptions used for the characterization of substrate (after Pain et al. 2004)	70

Table 48: Estimation method for substrate type	70

Table 49: Estimation method for substrate permeability	71

Table 50: Recommended minimum data set for the ASRIS soil profile database	72

Table 51: The agencies table.	75

Table 52: The projects table	75

Table 53: The site_location table.	75

Table 54: The features table.	76

Table 55: The feature notes table	76

Table 56: The samples table	76

Table 57: The sample notes table	77

Table 58: The results table	77

Table 59: The param_num_method table.	77

Table 60: The param_char_method table	78

Table 61: The param_ char_refs table	78

Table 62: The codes table.	78

Table 63: Conversion for pH in water to pH in CaCl2.	84

Figure 1: The ASRIS land-unit hierarchy (see also Table 3)	8

Figure 2: Mapping, monitoring and modelling are complementary activities for natural resource management and they must be set against the context of the environmental history of events and processes for a given landscape. ASRIS provides the national framework for soil and land resource information.	11

Figure 3: Examples of triangular probability distribution functions for coarse fragments. The mean, 5% and 95% quantiles are shown for the less variable layer.	26

Figure 4: The Multi-resolution Valley Bottom Flatness index identifies erosional and depositional areas from continental to local scales.	29

Figure 5: Relative relief	29

Figure 6: Average annual excess water (mm deep drainage and runoff per annum) (Raupach et al. 2001)	31

Figure 7: Examples of horizon sequences and allocation to the five-layer model used to describe idealized soil profiles in the land-unit hierarchy.  Example (a) is a common sequence. In example (b), Layers 2 and 4 are recorded as missing because the profile is shallow and has only a few horizons. Example (c) is a complex profile and Layers are specified according to their influence on plant growth and water movement.	44

Figure 8: Scaling term for water storage. The curves range from those likely for a soil with severe root constraints (e.g. Sodosols, Xi=0.2–0.4 m) to a deep soil without constraints (e.g. Red Ferrosol, Xi=2.0 m).	56

Figure 9: Calculation procedure for plant available water capacity	56

Figure 10: Database design for ASRIS. Definitions of variables are provided in the Tables below.	74

# Summary

This document specifies the variables, codes and estimation procedures for the Australian Soil Resource Information System (ASRIS). ASRIS has been developed to provide primary data on soil and land to meet the demands of a broad range of users including natural resource managers, educational institutions, planners, researchers, and community groups. The online system provides access to the best available soil and land resource information in a consistent format across the country – the level of detail depends on the survey coverage in each region. More specifically, ASRIS provides:

A spatial hierarchy of land-unit tracts with seven main levels of generalization (Figure 1). The upper three levels (L1–L3) provide descriptions of soils and landscapes across the complete continent while the lower levels (L4–L6) provide more detailed information, particularly on soil properties, for areas where mapping has been completed. The lowest level (L7) relates to an individual site in the field. The system can also be used to provide summaries of soil and landscape properties for a range of higher level stratifications of the country (e.g., Interim Biogeographic Regions of Australia (v5.1), Groundwater Flow Systems, and catchment management boundaries).

A consistent set of land qualities is described for land-unit tracts. Descriptions from the lowest-level units are used to generate summaries for higher-level units. The land qualities relate to the intrinsic capability of land to support various land uses – the land qualities relate to soil depth, water storage, permeability, fertility, and erodibility.

ASRIS includes a soil profile database with fully characterized sites that are known to be representative of significant areas and environments. The data provide catchment managers with primary source material for improving land literacy in their region, and natural resource specialists with a fundamental data set for assessing and predicting resource condition.

Estimates of uncertainty are provided with most data held within ASRIS. A distinction is made between attribute uncertainty (due to the measurement or estimation procedure for a given soil material) and spatial uncertainty (due to the natural variation across a landscape). The estimates are provided to encourage formal analysis of the uncertainty of predictions generated using ASRIS data (e.g. crop yield, runoff, land suitability for a range of purposes)

ASRIS is being released in stages. ASRIS 2004 will contain some 5,000 soil profiles along with the upper levels of the hierarchy (L1–L3) for most of the country and restricted coverage for lower levels. ASRIS 2006 will complete the coverage at the lower levels and contain an expanded soil profile database. ASRIS can be accessed online at www.asris.csiro.au.

Figure 1: The ASRIS land-unit hierarchy (see also Table 3)

| Level illustration | Level and tract name | Mapping window | Main attributes used for mapping | Typical uses for the information | Area of Australia covered |
| --- | --- | --- | --- | --- | --- |
|  | Level 1 Division | 30 km | Broad physiography (slope and relief) and geology | Broad geographic context | ILUZ: 100% Rangelands: 100% |
|  | Level 2 Province | 10 km | Physiography, water balance, dominant soil-order and substrate | National natural resource policy | ILUZ: 100% Rangelands: 100% |
|  | Level 3 Zone | 3 km | Physiography, regolith materials, age of land surface, water balance, dominant soil suborder | Regional natural resource policy | ILUZ: 100% Rangelands: 100% |
|  | Level 4 District | 1 km | Groupings of geomorphically related systems | Catchment planning, location of new industries | ILUZ: –% Rangelands: –% |
|  | Level 5 System | 300 m | Local climate, relief, modal slope, lithology, drainage network, related soil profile class | Catchment management, hydrological modelling, land conservation strategies, infrastructure planning | ILUZ: –% Rangelands: –% |
|  | Level 6 Facet | 30 m | Slope, aspect, land curvature, soil profile class | Farm management, land-use planning, on-ground works | ILUZ: –% Rangelands: –% |
|  | Level 7 Site | 10 m | Soil properties, surface condition, microrelief | Precision agriculture, site development | ILUZ: –% Rangelands: –% |

# User needs for soil and land resource information

The general proposition that our natural environment should be mapped and monitored is widely supported by natural resource management agencies, industry groups and community organizations. This information provides a basis for devising, implementing and monitoring land management. It also provides a basis for diagnosing the general condition of landscapes. Information on soil and land resources is fundamental and this is where ASRIS plays a central role.

The emergence of a range of large-scale environmental problems in Australia has added to the general demand for better information on spatial variation and trends in land resource condition. Satisfying this demand requires a clear view of how natural resource information is used to good effect. The first way is through reducing risks in decision-making, and the second involves improving our understanding of biophysical processes.

## Reducing risks in decision making

Reducing risk in decision-making requires the provision of information to be closely linked to, and preferably driven, by the decision-making process, whether at the scale of the paddock, enterprise, small catchment, region or nation. For example, farmers need information at the scale of the paddock, while a Commonwealth funding agency will usually require information at the regional and continental scale. Decision makers in Australia require timely access to information at relevant scales. ASRIS is a significant component in the delivery system. It has been developed with a view to satisfying a diverse range of needs at various levels of resolution. The following demands from government, industry, and community groups are of primary interest.

#### Government

The provision of reliable natural resource information to support policy decisions by Commonwealth, state, territory and regional agencies is necessary to address serious environmental problems, including global warming, dryland salinity and soil acidification. Improved natural resource information is required to:

Design, implement and assess the effectiveness of major natural resource management programs (e.g. schemes for widespread planting of perennials to control recharge);

Implement trading schemes (e.g. for salt, water and carbon) to achieve better natural resource management outcomes;

Establish baselines (e.g. for contaminants); and

Set targets and monitor trends.

#### Industry

Agricultural industries require better soil and land resource information to:

Optimize the matching of land use and management with land suitability (some sectors, most notably viticulture and industrial-scale farm forestry, have increased investment in user-specific land resource assessment during recent years);

Gain market advantage by demonstrating the benign nature of production systems (e.g. green labeling);

Implement environmental management systems to comply with duty of care regulations and industry codes; and

Optimize the use of inputs (e.g. soil nutrient testing to guide fertilizer rates).

#### Regional Communities

Regional communities require better soil and land resource information to:

Assess and improve the efficacy of natural resource management and target community action (e.g. remedial tree planting, fencing, weed control); and

## Improving process understanding

The reasons for using soil and land information outlined in the previous section focus on reducing risk in decision making. Another distinct application for soil information is to improve the understanding of landscape processes. This is largely the domain of educational, research and development organizations. Studies providing an improved understanding of landscape processes vary greatly in scope. For example, geomorphic studies of landscape evolution may involve intensive characterization and dating of stratigraphic sequences. Pedologic investigations of soil formation can require detailed surveys of key areas to determine the influence of different soil forming factors. Long-term monitoring studies usually involve some form of field experiment at the scale of the plot (e.g. agricultural tillage trials), through to the small catchment (e.g. paired-catchment studies in ecohydrology).

ASRIS provides a frame of reference for studies of landscape processes – it gives context by providing a basic stratification of the landscape into zones where baselines can be established, trends monitored, and results extrapolated. It also provides the basis for creating improved models for explanation and prediction (e.g., better statistical models for spatial prediction; improved simulation models to assess the environmental impact of land uses). The knowledge generated from these activities allows development of improved systems of land-use and management, and provides a scientific basis for improved policies in natural resource management.

## Mapping, monitoring, modeling, and environmental history

Land resource survey provides a key spatial component in the biophysical information system necessary for natural resource management.  ASRIS integrates outputs from survey programs across Australia and it must be considered with the mutually beneficial activities of monitoring and modelling, and all three should then be set within the context of environmental history – the latter provides an understanding of rates of soil and landscape change on much longer time scales (decades, centuries and millennia).

In isolation, each activity fails to provide appropriate information for land management and planning. In combination, they provide a powerful and synergistic means for transforming the quality of land management in Australia (Figure 1, Table 1).

Figure 2: Mapping, monitoring and modelling are complementary activities for natural resource management and they must be set against the context of the environmental history of events and processes for a given landscape. ASRIS provides the national framework for soil and land resource information.

Table 1: Complementary benefits of mapping (contained within ASRIS), monitoring and modelling

| Complementary Relationship | Benefits |
| --- | --- |
| ASRIS mapping ( Monitoring | Spatial framework for selecting representative sites System for spatial extrapolation of monitoring results Broad assessment of resource condition |
| ASRIS mapping ( Modelling | Provides input data for modelling Provides spatial association of input variables |
| Monitoring ( ASRIS mapping | Quantifies and defines important resource variables for mapping Provides temporal dimension to land suitability assessment (including risk assessments for recommended land management practices) |
| Modelling ( ASRIS mapping | Allows spatial and temporal prediction of landscape processes |
| Modelling ( Monitoring | Determines whether trends in specific land attributes can be successfully detected with monitoring Identifies key components of system behaviour that can be measured in a monitoring program |
| Monitoring ( Modelling | Provides validation of model results Provides input data for modeling |

## Land condition

In most parts of Australia, land resource surveys are undertaken across a range of seasonal conditions. Land cover and management vary during the course of a season and survey. Furthermore, to maximize objectivity and consistency, observations on land condition (e.g., scald erosion, wind erosion, sheet and rill erosion, gully erosion, mass movement, human-induced saline seepage, surface scalding) are made using the evidence present in the field at the time of survey. The rates of most land degradation processes are difficult to estimate unless permanent monitoring sites are used (see McKenzie et al. 2002). For example, in cropping areas, evidence for severe rill erosion can be obliterated by subsequent trafficking and cultivation. Similarly, the degree of expression and extent of saline seepage areas can vary dramatically with season.

The field observations and interpretations in the state and territory land resource databases span many decades – it is simply not possible to use these to generate a useful assessment of land condition. Fortunately, ASRIS can be used to support the assessment of land condition in other ways and it requires a broad view of the biophysical information base necessary for natural resource management (Figure 1).

ASRIS provides the basis for assessing land-degradation hazard. This can be achieved in various ways. For example, the Universal Soil Loss Equation can be parameterized using attributes from ASRIS to provide estimates of soil erosion by water. Models for predicting the hazard of wind erosion are also available. NLWRA (2001) provides other examples of how broad-scale soil information can be used to predict land condition and threatening processes (e.g., soil acidification).

ASRIS also provides a basis for locating monitoring sites for land condition and a framework for the extrapolation of results (Table 1).

## Striking a balance between general-purpose and problem-specified information

There is a long history of land resource survey failing to satisfy the needs of decision makers. It is very difficult to provide the right soil information at an appropriate scale in a timely manner. Dalal-Clayton and Dent (2001) provide a sobering assessment. A difficult challenge here is anticipating the demand for soil information well ahead of time. Surveys are rarely commissioned and completed in time to solve a particular problem, instead, general-purpose surveys are undertaken and a suite of likely problems is anticipated. It is easy to miss collecting key soil properties or to undertake the survey at an inappropriate scale.

Despite these difficulties, our experience has been that a core set of soil properties is needed for most applications. These are listed in Table 2.

## The task of interpretation

ASRIS aims to provide access to consistent soil information at the finest resolution available across Australia. It is a source of primary data for natural resource management and research. Wherever possible, these data have been presented in a form that can be readily interpreted; for example, estimates of functional landscape attributes such as plant available water capacity are given rather than more obscure variables that may be used to estimate the attribute. Of course, this is far short of the information required by most natural-resource decision-makers. For example, the profile available water capacity will only be one of many variables needed to estimate the potential productivity of different farming systems. More complex analyses of environmental risk or optimal mixes of land-use require much higher levels of integration (e.g. incorporating social, economic and political considerations).

At this point in time, ASRIS does not provide a system for making interpretations of soils and landscapes. However, a logical pathway for development would see the addition of an interface for performing rule-based analysis (e.g. land suitability for a range of uses). There is a limit to the level of complexity and it will often be more logical to download data from ASRIS for use within a purpose-built simulation modeling environment or decision support system.

Table 2: The main soil properties included in ASRIS and their significance

| Attribute | Significance |
| --- | --- |
| Texture | Affects most chemical and physical properties. Indicates some processes of soil formation |
| Clay content | As for texture |
| Coarse fragments | Affects water storage and nutrient supply |
| Bulk density | Suitability for root growth. Guide to permeability. Necessary for converting gravimetric estimates to volumetric |
| pH | Controls nutrient availability and many chemical reactions. Indicates the degree of weathering |
| Organic carbon | Guide to nutrient levels. Indicator of soil physical fertility |
| Depths to A1, B2, impeding layers, thickness of solum and regolith | Used to calculate volumes of water and nutrient (e.g. plant available water capacity, storage capacity for nutrients and contaminants), |
| (–10 kPa | Used to calculate water availability to plants and water movement |
| (–1.5MPa | Used to calculate water availability to plants and water movement |
| Plant available water capacity | Primary control on biological productivity and soil hydrology |
| Ksat | Indicates likelihood of surface runoff and erosion. Indicator of the potential for water logging. Measure of drainage. |
| Electrical conductivity | Presence of potentially harmful salt. Indicates the degree of leaching. |
| Aggregate stability | Guide to soil physical fertility. Potential for clay dispersal and adverse impacts on water quality. |
| Sum of exchangeable bases | Guide to nutrient levels. Indicates the degree of weathering |
| CEC | Guide to nutrient levels. Indicates the degree of weathering. Guide to clay mineralogy (when used with clay content) |
| ESP | Indicator of dispersive clays and poor soil physical properties. |
| ASC (Great Group) | Shorthand for communication across Australia |
| WRB | Shorthand for communication internationally |
| Substrate type | Control on soil formation, landscape hydrology, groundwater movement, nutrients and solutes. |
| Substrate permeability | Affects landscape hydrology and groundwater movement. |

# Development of ASRIS

ASRIS was initiated through the National Land and Water Resources Audit (NLWRA) in 1999 (see NLWRA 2002, Henderson et al. 2002). The initial release (ASRIS 2001) provided primary inputs for a broad range of simulation modeling studies supported by the NLWRA. These studies provided continental perspectives on erosion, sediment delivery to streams, nutrient cycling, acidification, net primary productivity, and water quality (NLWRA 2001, 2002).

The ASRIS 2001 team achieved a great deal given the short time available and daunting nature of the task (see Johnston et al. 2003). During the project, the core team and the Working Group on Land Resource Assessment (which acted as the Steering Committee) identified a series of deficiencies in the land resource information base for Australia. They also identified a logical pathway for overcoming these problems to ensure a greatly improved system for providing information to support natural resource management in Australia. The task was recognized to be long-term, and requiring a permanent project team (NLWRA 2002).

With this background, the Australian Collaborative Land Evaluation Program (ACLEP) was commissioned by the Department of Agriculture, Forestry and Fisheries (DAFF) to provide land managers, regional organizations, industry partners, policy specialists and technical experts in natural resource management, with online access to soil and land resource information, and assessments of land suitability. The information is to be available at a range of scales, and in a consistent and easy-to-use format across Australia. The activity must also provide a scientific framework for assessing and monitoring the extent and condition of Australia’s soil and land resources.

This document presents specifications for releases of the Australian Soil Resource Information System in 2004 and 2006 (ASRIS 2004 and ASRIS 2006 respectively).  These releases augment information provided by ASRIS 2001. More specifically, the releases provide:

A hierarchy of land units for the Australian Soil Resource Information System to allow comprehensive reporting on land suitability and soil resources from the National down to the Subregional scale. Upper levels of the hierarchy are generated using digital terrain analysis and refinements of existing geomorphic maps. Other information sources include results from continent-wide calculations of the water balance and geologic mapping. Lower levels are derived from the component state, territory and Commonwealth land resource map databases. There is also the facility to represent soil and land resource information using a number of other high-level stratifications including the Interim Biogeographic Regions of Australia (v5.1), Groundwater Flow Systems, and catchment management boundaries.

A consistent set of land qualities are presented for the lowest level units in the hierarchy and these are used to generate summaries for higher-level units. The land qualities relate to the intrinsic capability of land to support various land uses – they relate to soil depth, water storage, permeability, fertility, and erodibility.

The new releases of ASRIS will be in two stages. ASRIS 2004 contains the upper levels of the hierarchy for the whole country but lower levels will be initially from three States. ASRIS 2006 contains the complete coverage for all levels and all states and territories. Both releases are provided via the Internet using SQL Server, the Arc Spatial Data Engine (ArcSDE), and Arc Internet Map Server (ArcIMS). The system is accessed at www.asris.csiro.au.

ASRIS includes a soil profile database with fully characterized sites that are known to be representative of significant areas and environments. ASRIS 2004 contains approximately 5000 soil profiles with full quality assurance. The data are accessible on-line and provide catchment managers with primary source material for improving land literacy in their region, and natural resource specialists with a fundamental data set for assessing and predicting resource condition. The profile database will be expanded to 10,000 profiles with the release of ASRIS 2006.

ASRIS 2004 and 2006 include the original ASRIS 2001 soil information layers for the country in cases where improved coverages have not been generated.

# Hierarchy of land units and terminology

## Concepts and terms

A wide range of survey methods has been used in Australia (Beckett and Bie 1978, Gibbons 1983, McKenzie 1991) but most have been based on some form of integrated or soil-landscape survey (Christian and Stewart 1968; Mabbutt 1968; Northcote 1984) at medium to reconnaissance scales (1:50,000–1:250,000). Speight (1988) notes that the wide variation in mapping practice among different Australian survey organizations is largely a matter of level of classification or precision, rather than a difference in the conceptual units that surveyors recognize and describe.

Only small areas have been mapped using strict soil mapping units (e.g. soil series, type, variant, phase, association etc). Most of these studies have used free survey (Steur 1961, Beckett 1968) as the survey method and the majority of surveys have been detailed (i.e. 1:10,000–1:25,000) and for irrigation developments.

Quantitative surveys based on grid-based methods across small areas (usually <1000 ha), are becoming more common with the growth of precision agriculture. Quantitative surveys are also being applied at more general scales using methods of environmental correlation (e.g. McKenzie and Ryan 1999, Henderson et al. 2002, McKenzie et al. 2004). The key feature of these survey methods is the generation of predictions of individual soil properties rather than soil types.

This document is primarily concerned with capturing information from traditional integrated and soil-landscape surveys because these constitute more than 90% of land resource survey information for Australia. This should not be taken as tacit acceptance of conventional survey methods. There are many aspects of land resource assessment that must be changed to ensure a more technically defensible, and evidence-based, approach to natural resource management in Australia. The new guidelines for land resource survey outline directions for change (McKenzie et al. 2004).

The terminology used to define spatial units in Australia has been confused despite the pre-eminence of Australian workers in land resource survey and the existence of a well-defined literature (e.g. Stewart 1968, Austin and Basinski 1978, Dent and Young 1981, Gunn et al. 1988). Different groups have applied terms such as land unit, land system, and unique mapping area, in various ways. Speight (1988) brings order to the situation and his recommendations on terminology are adopted here because they are consistent with most aspects of current practice.

Individuals in agencies with a well-accepted local terminology may balk at the recommended terminology. This will be a problem for any set of proposed terms and flexibility is required if a consistent national standard is to be achieved. It is worth noting that the definitions of Speight (1988) are broadly consistent with international terminology (e.g. Dent and Young 1981). They are also part of the guidelines for survey practice in Australia (Gunn et al. 1988, McKenzie et al. 2004).

Speight (1988) uses land unit as a generic term and in a different sense to Christian and Stewart (1968).  Land unit does not imply a particular scale and it can be used to refer to:

conceptual units (e.g., land facets or systems as conceptual constructs),

mapping units (e.g. a tract of land or an individual polygon), and

taxonomic units (e.g. a type of land such as the Oxford Land System).

For these reasons, we will refer generally to the hierarchy of land units in ASRIS.

Speight (1988) also defines a land unit individual – this is a particular area of land having the same size as the land unit characteristic dimension.  Users of the Field Handbook (McDonald et al. 1990) will be familiar with this notion through the site concept.  For example, landform element attributes are observed over a circle (the site) of about 40 m diameter – the site in this instance defines the land unit individual and its characteristic dimension. In contrast, landform pattern attributes are observed over a circle of about 600 m diameter.

Speight’s (1988, 1990) observations on the characteristic dimensions of landform elements and patterns were intended to provide a guide rather than a fixed value. The concept is far more valuable than this and we use it here in conjunction with sets of defining attributes to construct the hierarchy of land-unit tracts.

Table 3 shows the hierarchy of land-unit tracts. Each level in the hierarchy has a specified characteristic dimension along with a set of defining attributes measured at the accompanying scale. The characteristic dimension can be viewed as the window size over which the defining attributes can be sensibly measured – different landscapes will have contrasting characteristic dimensions. For example, hillslope lengths may be very short (e.g., only a few metres in a strongly gullied landscape) or long (greater than a kilometer in strongly weathered landscapes of low relief), so land facets of very different size result.  In some landscapes, nested patterns of landform may be evident and sublevels within the hierarchy can be sensibly delineated using the same set of defining attributes at more than one characteristic dimension (e.g., land systems within a land system). The ASRIS hierarchy and database structure allows sublevels to be defined for a given attribute set (e.g., Level 6.1).

The characteristic dimensions in Table 3 have been changed from Speight’s (1988) original proposition to emphasize its role as a variable that defines both the appropriate of measurement and the nature of the landscape. The suggested values also better match the styles of survey undertaken across large areas during the last 15 years.

In Table 3, tracts are mapping units as opposed to taxonomic units.  Note that polygon is often used synonymously with land-unit tract. Most land resource assessment in Australia is concerned with the mapping and description of land-unit tracts at the land facet and land system level.  Speight (1988) defines these as follows:

Land facet (L6): This is a land unit with attributes that include slope, aspect, toposequence position, microclimate, moisture regime, soil profile class, land surface features, vegetation formation and vegetation community. Speight (1988) considers its characteristic dimension to be about 40 m but it can vary from 100 to just a few metres.  Note that the terms land component and land element have often been equated with this definition of land facet.

Land system (L5): This is a land unit with attributes that include relief, modal slope, stream pattern, toposequences, local climate, lithology, soil association, vegetation type or sequence, and proportional occurrence and arrangement of land facets.  Speight (1988) considers its characteristic dimension to be about 600 m, and he recommends this diameter for a land-system site.

Note that these are definitions of conceptual land units.  Explicit reference can be made to land-unit individuals, types or tracts (e.g. land-facet individual, land-facet tract, land-facet type) but the context will usually convey the appropriate meaning. Particular mention should also be made of unique mapping areas – these are usually instances of land system tracts that are later grouped into land system types.

To reiterate, the concept of scale in the hierarchy of land-unit tracts is based not on the cartographic scale of mapping, but rather on:

the characteristic dimension; and

set of defining attributes.

If land facets and land systems are defined in terms of landform attributes alone, they are identical with the landform elements and landform patterns defined by McDonald et al. (1990).

Mapping land districts (L4) is usually achieved by grouping land systems. Mapping land units at higher levels can be achieved by grouping land districts but in reality, most mapping at the division (L1), province (L2), and zone (L3) level is undertaken using a divisive rather than an agglomerative approach. Furthermore, different criteria for mapping emerge at these more generalized levels and many of the criteria used at lower levels lose significance (and vice versa).

Table 3: The spatial hierarchy of land-unit tracts (after Speight 1988). Note that the database design for ASRIS allows intermediate Levels to be characterized (e.g., a System with a characteristic dimension significantly less that 100 m would be designated as Level 5.1 or 5.2 in the hierarchy)

| Level | Order of land-unit tract | Speight | Characteristic dimension | Descriptive or defining attributes | Appropriate map scale |
| --- | --- | --- | --- | --- | --- |
| 1.0 | Division | 300km | 30 km | Broad physiography (slope and relief) and geology | 1:10 million |
| 2.0 | Province | 100 km | 10 km | Physiography, water balance, dominant soil order and substrate | 1: 2.5 million |
| 3.0 | Zone | 30 km | 3 km | Physiography, regolith materials, age of land surface, water balance dominant soil suborder | 1:1 million |
| ASRIS Mapping Hiatus Levels above are based on subdivisions of the continent Levels below are aggregated from surveys. |
| 4.0 | District | 5 km | 1 km | Groupings of geomorphically related systems | 1:250 000 |
| 5.0 | System | 600 | 300 m | Local climate, relief, modal slope, single lithology or single complex of lithologies, similar drainage net throughout, related soil profile classes (soil-landscape*) | 1:100 000 |
| 5.1 |  |  | 100 m | As for Level 5 | 1:25 000 |
| 6.0 | Facet | 40 | 30 m | Slope, aspect, soil profile class | 1:10000 |
| 6.1 |  |  | 10 m |  | 1:2500 |
| 6.2 |  |  | 3 m |  | 1:1000 |
| 7.0 | Site | 20 | 10 m | Soil properties, surface condition, microrelief | rarely mapped in conventional survey |

*  Sensu Thompson and Moore (1984)

## Upper levels of the hierarchy

The upper levels of the land-unit hierarchy are described in Sections 6–8. There are many other maps of Australia’s natural resources at scales equivalent to the land zone, land province or land division. Some examples relevant to soils and landscapes include:

Northcote et al. (1960–1968) – Atlas of Australian soils

Löffler and Ruxton (1969) – Relief and landform map of Australia

Laut et al. (1980) – Provisional environmental regions of Australia

CSIRO (1983) – Soil landscape regions

Grant et al. (1984) – Geotechnical landscape map of Australia

Chan et al. (1986) – Regolith terrain map of Australia

Jennings and Mabbutt (1986) – Physiographic regions of Australia

Environment Australia (2000) – Interim biogeographic regions Version 5.1

Coram et al. (2001) – Groundwater flow systems

Williams et al. (2002) – Agro-ecological regions of Australia

ASRIS has the facility to substitute such stratifications above the level of the mapping hiatus. IBRA regions, groundwater flow systems, and catchment management boundaries are available and others will be added if required. The ability to substitute other stratifications allows summaries of soil and landscape properties to be generated in various formats. This promotes both integration of natural resource information and more widespread use of soil and land data by non soil-science based groups.

The linework and principles of Jennings and Mabbutt (1986) have been used to develop methods for Levels 1–3 in ASRIS. In particular:

Land-unit tracts at these levels are discrete entities and outliers are permitted only in exceptional cases (e.g. offshore islands, major plateau adjacent to extensive tablelands)

Tracts are hierarchical and have a single parent-tract

The conventions for geographic naming outlined by Jennings and Mabbutt (1986) are followed except where their existing terms fail to have a local resonance (e.g. Werriwa Tablelands for the northern section of the Southern Tablelands in New South Wales) – this judgement will be made by state and territory agency staff with reference local naming conventions.

### Data presentation

Apart from the online maps, data summaries (e.g., for soil properties such as pH, exchangeable cations, hydraulic conductivity) in the ASRIS land unit hierarchy are of two basic types:

Area-weighted means (only for attributes where this is appropriate)

Histograms of attributes based on percentage area

These two options, when combined with estimates of uncertainty, should form a sufficient basis for most queries of the system. The provision of histograms is to ensure compatibility with modeling systems such as those used in hydrology that use distributional information rather than simple measures of central tendency (e.g., mean, median). It is also an essential step towards providing better measures of uncertainty for all users of soil and land information.

## Relationships between the land unit hierarchy and continental grids

A theoretical ideal would be to have estimates for all relevant soil and land attributes at all locations with an acceptable level of uncertainty for all forms of decision-making. A grid-based representation of these attributes would be convenient and ASRIS 2001 generated such coverages for selected soil properties using environmental correlation (i.e., point data from field measurements are correlated with environmental variables that are measured everywhere to produce predictions of soil attributes for all locations – see McKenzie and Ryan 1999, Bui et al. 2004, McKenzie et al. 2004).  The land-unit hierarchy provides another method for providing predictions at locations. Estimates are based on field observations or interpretations of soil variation within land-unit tracts. While the mental models used to delineate and describe the land-unit tracts are rarely explicit and sampling is purposive, the resulting maps have been useful for many purposes and they contain considerable information.

The land-unit hierarchy has been prepared with this context and it is recognized that the predictions of individual attributes will often have a large uncertainty – we cannot estimate this uncertainty in an objective manner unless there is independent statistically based sampling (McKenzie and Ryan 2004).

The land-unit hierarchy has another very important role. It can be used to stratify landscapes to allow:

More precise interpretations relating to landscape processes,

Development of robust environmental correlation models for predicting individual soil attributes using a grid-based approach.

The hierarchy of land units and grid-based methods for predicting soil and landscape attributes are complementary both for the analysis and interpretation of data.

Database development within ASRIS will therefore include not only the construction of the soil profile database for fully characterized profiles (i.e., with comprehensive analytical data), but also the development of a much larger soil profile database for all locations characterized during agency survey programs. This comprehensive database will include other sources of data if quality control and privacy considerations can be resolved (e.g., soil-testing data).  However, the initial priority is on development of the land-unit hierarchy, interpretations of soil and land qualities, and the database of fully characterized representative profiles. The grid-based estimates from ASRIS 2001 (Johnston et al. 2003) are included for completeness.

## Description of Land Facet and Land System Tracts

This document concentrates on land facet and land system tracts. Land facets are usually described but not mapped in most Australian land resource surveys.  However, the precision of the mapping varies considerably.  For example, the Atlas of Australian Soils uses very general soil-landscapes (equivalent here to land systems) with un-mapped land facets. In contrast, the soil-landscape mapping undertaken in New South Wales is more precise although it still maps soil-landscapes and describes unmapped land facets.

The land-unit hierarchy in ASRIS requires description of individual land system tracts and their component land facets. In some cases, individual land system tracts (i.e. unique mapping areas) may be described according to a land system type (i.e. according to Christian and Stewart’s (1968) original definition of a land system where individual land system tracts belong to the same land system type with the tracts having the same descriptive attributes). It would be preferable to have access to descriptions of each land system tract prior to grouping into a land system type but in many cases these data were never recorded (e.g. in the earlier CSIRO land system surveys).

# Accuracy, precision and a basis for stating uncertainty

## Rationale

Estimates of uncertainty for each attribute in ASRIS are needed to encourage more appropriate use of soil and land resource data. Uncertainty estimates are essential for the tracking of error propagation in various forms of analysis, particularly simulation modeling (e.g., Heuvelink 1998, Moss and Schneider 2000, Minasny and Bishop 2004). In many instances, the information on uncertainty generated by a model is as important as the prediction itself.

As far as possible, we have followed guidelines from the National Institute of Standards and Technology for evaluating and expressing uncertainty (Taylor and Kuyatt 1994, http://physics.nist.gov.cuu/Uncertainty).

Type A evaluations of standard uncertainty are based on any valid statistical method for treating data. These are not common in Australian soil and land resource survey. An example would be estimation of uncertainties in carbon or pH based on stratified random sampling of a land-unit tract.

Type B evaluations of standard uncertainty are based on scientific judgement using all the relevant information available, which may include:

Previous measurement data on related soils

Experience with, or general knowledge of, the behaviour and properties of the relevant soils and measurement methods (e.g., accuracy of laboratory determinations and field description methods, reliability of pedotransfer functions)

Uncertainties published in reviews of soil spatial variability (e.g., Beckett and Webster 1971, Wilding and Drees 1983, McBratney and Pringle 1999)

## Estimating uncertainty

Most estimates of uncertainty in ASRIS rely on Type B evaluations. The form of the estimate depends on the measurement scale and assumed probability distribution for each attribute.

Continuous variables with an assumed Normal probability distribution have their uncertainty represented by an estimated standard deviation. This is denoted by ui and uj for Type A and B evaluations respectively. In most cases, an attribute’s uncertainty will arise from several sources and the combined standard uncertainty (uc) is reported. There are many issues to resolve in calculating uc, and it will often be appropriate to simply assume the component variances additive (i.e., uc = ((u12 + u22 + u32…) where u1, u2 and u3 are uncertainties attributable to different sources, for example, field estimation, a pedotransfer function, and spatial variability). Two components of uncertainty are recorded in ASRIS (see below) – Table 2 provides default values.

It is difficult to nominate the most appropriate error distribution for some variables. For example, some must be positive (e.g., CEC, layer thicknesses) so a Gamma distribution may be most appropriate but in practice it will be simpler to use a log-normal distribution. Other variables are bounded (e.g., clay content varies from 0–100%) and the assumptions of the Normal and Gamma distributions are violated so another approach is needed. We have adopted the following conventions.

Continuous variables that are not normally distributed are transformed to an approximately normal distribution and uncertainties are then estimated. Hydraulic conductivity and electrical conductivity are assumed to be distributed log-normally, unless there is evidence to the contrary. The mean is recorded in untransformed units to improve the ease of interpretation but the standard deviation is recorded as a transformed value. For example, the hydraulic conductivity may be estimated to be 100 mm/hr with a standard deviation of 0.5 log(mm/hr). The range of ± 1 standard deviation (i.e., 68% of the population) around the mean of 100 mm/hr would therefore be 32–320 mm/hr. The advantage of recording the transformed standard deviation is that that only one value is needed to represent dispersion of the asymmetric distribution.

Variables with fixed ranges (e.g., percentage coarse fragments) or coarse stepped scales are modeled with triangular probability distributions unless there is evidence to the contrary. The triangular probability distribution is assumed to be symmetric. The mean is estimated and dispersion is defined as (95% quantile – 5% quantile)/2. The distribution between the minimum value and the 5% quantile, and between the 95% quantile and the maximum, is assumed to be flat. The distribution is shown in Figure 3.

Uncertainties for nominal variables are represented by the probability that a class is correct (e.g., the uncertainty that a landform element type is a beach ridge is 0.8). Combined uncertainties are calculated by multiplying component probabilities.

Every soil attribute has an estimated uncertainty with two components.

The first component (u1) is associated with the measurement error for the given attribute at the profile or site – it will be significantly reduced if replicated sampling or bulking has been undertaken. If the attribute (e.g., water retention at –10 kPa) is being estimated using a pedotransfer function, then the uncertainty includes both the measurement error of the explanatory variables (e.g., texture, structure, and bulk density) and error due to model underlying the pedotransfer function.

The second component (u2) of uncertainty is due to spatial variability within the land-unit tract at the lowest level in the hierarchy for which data are available.

In most parts of Australia, there is limited information on both of these sources of uncertainty and it will require good judgment to provide estimates. However, the alternative of providing estimates of mean values without information on variability is potentially misleading.

In the absence of better information, we will use default values of uncertainty drawn from the published literature on spatial variability and our general knowledge (Table 4). The default values are conservative (i.e., most likely on the high side) and intended to encourage more attention to the estimation of uncertainty. The component of uncertainty due to measurement (u1) can be determined using the estimation method for each variable as a guide (e.g., Table 23 for bulk density). The component of uncertainty due to spatial variability (u2) can be determined using several lines of evidence including:

cartographic scale of the survey and intensity of sampling (this is expressed via the Order of Survey (Table 7, Soil Survey Staff 1993)), and

qualitative assessment of landscape complexity.

Figure 3: Examples of triangular probability distribution functions for coarse fragments. The mean, 5% and 95% quantiles are shown for the less variable layer.

Table 4: Default estimates of uncertainty for attributes of land-unit tracts in ASRIS – defaults for landform and land surface (relief, modal slope, element, pattern, microrelief, rock outcrop and surface coarse fragments) are yet to be determined.

| Attribute | Units (un-transformed) | Scale of measurement and probability distribution* | Attribute uncertainty due to measurement (u1) | Indicative Spatial Uncertainty (simple– complex landscape)** (u2) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Order 3 Survey | Order 4 Survey | Order 5 Survey |
| Landform pattern |  | Nominal |  |  |  |  |
| Rock outcrop (Level 5) | % |  |  |  |  |  |
| Surface coarse fragments | % |  |  |  |  |  |
| Morphologic type |  | Nominal |  |  |  |  |
| Landform element |  | Nominal |  |  |  |  |
| Slope class |  | Nominal |  |  |  |  |
| Site drainage |  | Nominal |  |  |  |  |
| Rock outcrop (element) | % |  |  |  |  |  |
| Surface coarse frag. | % |  |  |  |  |  |
| Microrelief type |  | Nominal |  |  |  |  |
| Gilgai component |  | Nominal |  |  |  |  |
| Microrelief biotic agent |  | Nominal |  |  |  |  |
| Biotic component |  | Nominal |  |  |  |  |
| Texture |  | Nominal | 0.8 – S, LS, CS, MC, MHC, HC. 0.7 – other classes | 0.4–0.7 | 0.2–0.8 | 0.1–0.9 |
| Clay content | % | Triangular | 10% | 10–20% | 20–30% | 30–40% |
| Coarse fragment abundance | % | Triangular | 20% | 20–30% | 30–40% | 40–50% |
| Coarse fragment porosity | m3/m3 | Triangular | 0.1 | 0.1–0.2 | 0.1–0.2 | 0.2–0.3 |
| Bulk density | Mg/ m3 | Normal | 0.1 | 0.1–0.2 | 0.2–0.3 | 0.3–0.4 |
| pH |  | Normal | 0.2 | 0.2–0.5 | 0.5–1.0 | 1.0–2.0 |
| Organic carbon | % | Normal | 0.2 | 0.4–0.8 | 0.8–1.2 | 1.2–2.0 |
| Depth A1 | m | Triangular | 0.05 | 0.1–0.2 | 0.2–0.3 | 0.3–0.4 |
| Depth to B2 | m | Normal | 0.1 | 0.1–0.2 | 0.2–0.3 | 0.3–0.4 |
| Depth of solum | m | Normal | 0.2 | 0.2–0.4 | 0.4–0.6 | 0.6–1.0 |
| Depth to impeding layer | m | Normal | 0.2 | 0.2–0.4 | 0.4–0.6 | 0.6–1.0 |
| Depth of regolith | m | Normal | 0.3 | 0.3–1.0 | 1.0–2.0 | 2.0–3.0 |
| Layer thicknesses 1-4 | m | Normal | 0.1 | 0.1–0.2 | 0.2–0.3 | 0.3–0.4 |
| Layer thickness 5 | m | Normal | 0.2 | 0.3–1.0 | 1.0–2.0 | 2.0–3.0 |
| (–10 kPa | % | Normal | 2 | 2–4 | 4–6 | 6–8 |
| (–1.5MPa | % | Normal | 1 | 1–3 | 3–5 | 5–7 |
| Ksat | mm/hr | Log10-normal | 0.5 | 1–2 | 1.5–3 | 2–4 |
| Electrical conductivity | dS/m | Log10-normal | -1 | -0.7–-0.4 | -0.4–-0.2 | -0.2–-0.1 |
| Aggregate stability |  | Nominal | 0.9 | 0.8–0.7 | 0.7–0.6 | 0.6–0.4 |
| Water repellence |  | Nominal | 0.8 | 0.6–0.4 | 0.5–0.3 | 0.4–0.2 |
| Sum of exchangeable bases | cmol(+)/kg | Normal | 0.5 | 0.5–1 | 1–4 | 4–8 |
| CEC | cmol(+)/kg | Normal | 0.5 | 0.5–1 | 1–4 | 4–8 |
| ESP | % | Normal | 1 | 1–2 | 2–4 | 4–8 |
| ASC (Great Group) |  | Nominal | 0.9 | 0.8–0.7 | 0.7–0.5 | 0.5–0.4 |
| WRB |  | Nominal | 0.8 | 0.7–0.6 | 0.6–0.4 | 0.4–0.1 |
| Substrate type |  | Nominal | 0.8 | 0.7–0.6 | 0.6–0.5 | 0.5–0.4 |
| Substrate permeability | mm/hr | Log10-normal | 0.5 | 1–2 | 1.5–3 | 2–4 |

* Uncertainty for Normally distributed attributes is estimated using the standard deviation (sd) – note 68% of observations are within ±1sd and 95% are within ±2sd.

** Spatial uncertainty includes the component due to measurement or estimation (i.e., u1) along with uncertainty arising from spatial variation within a land-unit tract. Spatial uncertainty increases with decreasing survey effort (e.g. less intensive field sampling and broader scale mapping) and with increasing landscape complexity. Survey effort has been classified according to the Survey Order while a range in uncertainty due to landscape complexity has been estimated.

# Level-1 descriptors (land division)

Level 1 distinguishes major physiographic divisions across the country. These tracts are defined primarily by slope and relief although the principles of mapping are essentially the same as those used for integrated survey (Gunn et al. 1988). Various strands of evidence are used to locate boundaries of these large land-unit tracts: for example, existing geology and landform maps at the same scale, Landsat imagery, and various terrain attributes (see the ASRIS website).

Two terrain attributes in particular are useful at the continental level to both help delineate and describe land-unit tracts. The Multi-resolution Valley Bottom Flatness (MrVBF) index (Gallant and Dowling 2003) identifies areas that are both relatively flat and low in the landscape at different scales – these are interpreted as valley bottom areas (Figure 4). MrVBF is interpreted as an index of deposition, based on the assumption that flat valley bottoms are flat because they are filled with sediment. The index separates upland terrain dominated by erosional processes from lowland depositional terrain, and further divides the depositional areas into different classes based on slope and areal extent. Values less than 0.5 are considered to be erosional, while values greater than 0.5 are considered to be depositional. The second terrain variable is relief (Figure 5). It is defined using departure of an individual cell from the average elevation in a 2 km diameter window centred on the cell. Investigations are underway to refine this relief measure (using sectoral relief or upslope/downslope relief, both within a multiscale scheme similar to MrVBF).

In the absence of a better stratification, Jennings and Mabbutt’s physiographic regions will be used as a first approximation in ASRIS. A level of generalization between their Division and Province is needed for Level 1 in ASRIS. As a guide, the hierarchy of land-unit tracts divides by a factor of approximately seven between each level (i.e., Level 1 has ~7 tracts, Level 2 has ~49, Level 3 has ~ 343 and so forth). Adjustments to the Jennings and Mabbutt linework will be made manually using the terrain variables and other sources of information (particularly the Landsat imagery) – the goal is to create units that minimize within-unit variation and maximize between-unit variation in the two terrain attributes. The possibility for a more explicit and repeatable method is being investigated.

Level 1 can be used to make interpretations about landscape processes at the broadest scale. These relate primarily to distinctions between erosional and depositional landscapes, and the potential energy of landscapes (e.g. high-energy areas have steep slopes and large relief so they will have correspondingly large rates of sediment movement)

Each land-unit tract will have a geographical name, statistical summaries of slope and relief (including histograms) and a generalized description of geology.

Figure 4: The Multi-resolution Valley Bottom Flatness index identifies erosional and depositional areas from continental to local scales.

# Figure 5: Relative relief

# Level-2 descriptors (land province)

Level 2 subdivides Level-1 units using physiographic distinctions at a finer level of detail. Again, relief and modal slope are used as the primary discriminants and in the absence of a better stratification, Jennings and Mabbutt’s physiographic regions will be used as a first approximation. Level-2 is between the Province and Section in that scheme. Adjustments to the linework will be made manually using the terrain variables – the goal is to create units that minimize within-unit variation and maximize between-unit variation in the two terrain attributes.

Primary descriptors at Level-2 are relief, modal slope, regolith materials, dominant soil order, and an estimate of water-balance. As with Level 1, each tract will have a geographic name and simple text description.

Regolith materials will be described using the first level of classification in Table 47 (unweathered bedrock (BU), evaporites (EVA), sediments (SDE), unconsolidated materials (UO) and weathered in-situ residuals (WIR)). Some of these categories may be split if necessary (e.g. to discriminate alluvial, colluvial and aeolian sediments). The relative area of up to three classes will be shown using the descriptors dominant (>50%), subdominant (20–50%) and minor (<20%). The same system is used to show the abundance of the dominant soil order.

Water-balance is estimated using outputs from the BIOS model (Raupach et al. 2001) calculated using a 5 km grid across the country. The model partitions precipitation into transpiration and evaporation with the remainder being allocated to drainage and runoff. This drainage and runoff (‘excess water’) provides an estimate of potential leaching. This acts as a guide to accumulations of soluble salts, organic matter dynamics, pH, and intensity of weathering (Figure 6).

There are limits to the degree to which contemporary climate can be used to infer current or past soil processes. However, spatial representation in ASRIS of Pleistocene and earlier Tertiary climates is not feasible at this stage.

Figure 6: Average annual excess water (mm deep drainage and runoff per annum) (Raupach et al. 2001)

# Level-3 descriptors (land zone)

Level 3 subdivides Level-2 units with finer distinctions based on physiography. The number and detail of descriptors are also increased.

Regolith materials are described using Table 48 and an estimate of areal proportion (dominant, subdominant, minor).  At this stage, the line work will most likely come from high level groups from land resource surveys or geologic and geomorphic mapping.

Relative age of the land surface is estimated (Holocene, Pleistocene, Tertiary, and pre-Tertiary)

Climate summaries are given for excess water (see Level 2), mean annual temperature and mean annual precipitation

Up to three soil sub-orders are listed with an estimate of abundance (dominant, subdominant and minor)

A geographic name and text description.

As noted earlier, between 200–300 land-unit tracts will be delineated.

# Level-4 descriptors (land district)

The descriptors for Level 4 in the ASRIS hierarchy of land units characterize groupings of geomorphically related systems. These units differ from Level 3 in both detail and concept. Level-4 tracts are not geographically contiguous and conformable boundaries with Level 3 are not mandatory. Level-4 tracts are aggregated from surveys and are below the ASRIS Mapping Hiatus whereas Levels 1–3 are based on subdivisions of the continent. Most descriptors for Level 4 are generated as weighted averages and histograms from Level-5 tracts. Additional descriptions provide:

Estimates of the resistance to weathering of the substrate

A text description of the tract

In many cases, the number of Level-4 tracts per Level-3 parent will be greater than seven.

# Level-5 descriptors (land system)

## Identifiers

Most field-based land resource surveys in Australia collect information at Levels 5 and 6. In this section and the next, descriptors are specified for land-unit tracts at the system and facet level. State and territory agencies will most commonly provide data at Level 5 (land system) with unmapped tracts at Level 6 (land facets). In some instances, land systems or land facets may be provided at two or more levels of detail (e.g., nested land systems with unmapped facets, or a land system with 2 levels of land facet). In some circumstances, the lowest level may only consist of land systems.

Most source data for ASRIS have been collected during particular projects that cover a specified area and defined period. Project and agency codes are provided with all data. In the case of soil profile data collected independently of survey projects, a miscellaneous code (MISC) is used along with the Agency Code. States and territories need to provide unique Level-5 identifiers for each land system tract. An extra identifier (proportion) is needed when the land-unit tract is described but not mapped. The identifiers are summarized in Table 5.

Table 5: Level-5 land-unit tract identifiers

| Variable | Definition | Example and explanation | Comments |
| --- | --- | --- | --- |
| Agency code | SITES agency code | 505 |  |
| Project code | Agency code for the source survey | ALP58 (Alpine survey, 1958) | See ASRIS Website for a full listing of codes |
| Feature identification | Agency defined and unique number for the tract | mtk00245 |  |
| Hierarchy level | Level in the ASRIS land-unit hierarchy | 5.0 |  |
| Component identification | Unique code for the unmapped component if present | 0001 |  |
| Feature name | Plain text description of the land unit | Mt Kosciuszko land system | Text can also include a broad description of the tract (<240 characters) |
| Proportion | Areal occupied by the tract within the parent land unit | 60% | Only applicable when the land-unit tract is described but not mapped |

## Mapping Intensity and Scale

#### Observations

The nature of observations within each land-unit tract at Level 5 and 6 is recorded according to Table 6. Note that a field observation involves, as a minimum, completion of a full site and profile description according to McDonald et al. (1990).

Table 6: Nature of observations for land-unit tract

| Class | Description |
| --- | --- |
| 1 | Multiple field observations recorded and extensive traverses |
| 2 | Single field observation and restricted traverses |
| 3 | Characterization relies on field observations made in similar units in the same District (if tract is L5) or System (if tract is L6) |
| 4 | Characterization relies on remotely sensed information only |
| 5 | Unknown |

#### Order of survey

The order of survey used to generate the interpretations for each land-unit tract is recorded according to Table 7 (for further details see Soil Survey Staff (1993, p48–49)).

Table 7: Orders of survey (modified from Soil Survey Staff (1993, p48–49))

| Order level | Intensity | Minimum size delineation (ha) | Cartographic scale for publication |
| --- | --- | --- | --- |
| 1 | Very intensive | <0.3 | More detailed than 1:10,000 |
| 2 | Intensive | 0.3 – 1 | 1:10,000 – 1:20,000 |
| 3 | Extensive | 1 – 5 | 1:20,000 – 1:50,000 |
| 4 | Extensive | 5 – 150 | 1:50,000 – 1:250,000 |
| 5 | Very Extensive | 150 – 4,000 | 1:250,000 – 1: million or less detailed |

#### Year of survey

The year of generation of the primary source of information used for the interpretations is recorded (the year of publication will usually be sufficient).

## Landform

#### Relief/modal slope

Relief and modal slope will be calculated for land-unit tracts above and including the level of land system. Relief and modal slope classes will also be generated according to Table 5 of Speight (1990). The ASRIS team will undertake these tasks using the continent-wide 9-second digital elevation model. It is acknowledged that slopes will be underestimated in some landscapes as a result. Codes are provided in Table 8.

Table 8: Relief and modal slope classes

| Code | Code desciption |
| --- | --- |
| B | Badlands <9m >32% |
| B1 | Badlands 9-30m >56% |
| B2 | Badlands 30-90m >100% |
| GP | Gently undulating plains <9m 1-3% |
| GR | Gently undulating rises 9-30m 1-3% |
| LP | Level plain <9m <1% |
| PH | Precipitous hills 90-300m >100% |
| PM | Precipitous mountains >300m >100% |
| RH | Rolling hills 90-300m 10-32% |
| RL | Rolling low hills 30-90m 10-32% |
| RM | Rolling mountains >300m 10-32% |
| RP | Rolling plains <9m 10-32% |
| RR | Rolling rises 9-30m 10-32% |
| SH | Steep hills 90-300m 32-56% |
| SL | Steep low hills 30-90m 32-56% |
| SM | Steep mountains >300m 32-56% |
| SR | Steep rises 9-30m 32-56% |
| UH | Undulating hills 90-300m 3-10% |
| UL | Undulating low hills 30-90m 3-10% |
| UP | Undulating plains <9m 3-10% |
| UR | Undulating rises 9-30m 3-10% |
| VH | Very steep hills 90-300m 56-100% |
| VL | Very steep low hills 30-90m 56-100% |
| VM | Very steep mountains >300m 56-100% |

#### Landform pattern

Landform pattern is recorded using the terms in the glossary provided by Speight (1990, p48-57, Table 9).

#### Rock outcrop

Rock outcrop is the percentage of the land-unit tract occupied by rock outcrop. This attribute is usually recorded using the classes on page 101 of McDonald et al. (1990) – use the mid-point of the class range if more accurate information is not available. Rock outcrop is only recorded at Level 5 if data are not available for Level 6. Care is needed to avoid double counting with surface coarse fragments.

#### Surface coarse fragments

The areal percentage of surface coarse fragments is recorded as a percentage for the land-unit tract but again only when Level-6 tracts are not described.  These variables are recorded for five size classes: gravelly (2–60mm) (i.e. grouping of the fine, medium and coarse gravelly categories in McDonald et al. (1990)), cobbles (60-200 mm), stones (200-600 mm), boulders (600 mm – 2m) and large boulders (>2 m).

Table 9: Codes for landform pattern

| Code | Landform pattern | Code | Landform pattern |
| --- | --- | --- | --- |
| ALF | Alluvial fan | MAD | Made land |
| ALP | Alluvial plain | MAR | Marine plain |
| ANA | Anastomatic plain | MEA | Meander plain |
| BAD | Badlands | MET | Meteor crater |
| BAR | Bar plain | MOU | Mountains |
| BEA | Beach ridge plain | PAR | Parabolic dunefield |
| CAL | Caldera | PED | Pediment |
| CHE | Chenier plain | PEP | Pediplain |
| COR | Coral reef | PLA | Plain |
| COV | Covered plain | PLT | Plateau |
| DEL | Delta | PLY | Playa plain |
| DUN | Dunefield | PNP | Peneplain |
| ESC | Escarpment | RIS | Rises |
| FLO | Flood plain | SAN | Sand plain |
| HIL | Hills | SHF | Sheet-flood fan |
| KAR | Karst | STA | Stagnant alluvial plain |
| LAC | Lacustrine plain | TEL | Terraced land (alluvial) |
| LAV | Lava plain | TER | Terrace (alluvial) |
| LON | Longitudinal dunefield | TID | Tidal flat |
| LOW | Low hills | VOL | Volcano |

# Level-6 descriptors (land facets)

## Identifiers

In the previous section it was noted that in most land resource surveys in Australia, Level-6 land facets are described but not mapped. The areal percentage of each unmapped tract within its parent tract must be recorded to allow the calculation of area-weighted statistics within ASRIS. The identifiers for Level-6 land facets are presented in Table 10 for completeness – they are the same as those for Level-5 tracts.

Table 10: Level-6 land-unit tract identifiers

| Variable | Definition | Example and explanation | Comments |
| --- | --- | --- | --- |
| Agency code | SITES agency code | 505 | See ASRIS Website for a full listing of valid codes |
| Project code | Agency code for the source survey | ALP58 (Alpine soil survey, 1958 – Bloggs et al. (1964)) | See ASRIS Website for a full listing of codes |
| Feature identification | Agency defined and unique code for the tract | mtk00245003 |  |
| Component identification | Unique code for the unmapped component if present | 0001 |  |
| Hierarchy level | Level in the ASRIS land-unit hierarchy | 6.0 |  |
| Feature name | Plain text description of the land unit | Feldmark on exposed slopes of Mt Kosciuszko | Text can also include a broad description of the tract (<240 characters) |
| Proportion | Areal percentage occupied by the tract within the parent land unit | 30% | Only applicable when the land-unit tract is described but not mapped |

## Landform

The observations method-code (Table 6) is recorded and it forms the basis for assessing the uncertainty of estimates for morphologic type, landform element type, slope class, site drainage, rock outcrop, surface coarse fragments and microrelief.

#### Morphological type

The land facet is described using one of the ten morphologic types defined by Speight (1990, p13) and listed in Table 11.

Table 11: Landform morphological type

| Code | Code desciption |
| --- | --- |
| C | Crest |
| D | Closed Depression |
| F | Flat |
| H | Hillock |
| L | Lower-slope |
| M | Mid-slope |
| R | Ridge |
| S | Simple-slope |
| U | Upper-slope |
| V | Open depression (vale) |

#### Landform element type

Landform element is recorded using the terms in the glossary provided by Speight (1990, p24-34) and listed in Table 13.

#### Slope class

The average slope of the land facet is recorded in percent.

#### Site drainage

Site drainage is recording using the six classes defined by McDonald and Isbell (1990, p151) and shown in Table 12.

Table 12: Drainage classes

| Code | Code description |
| --- | --- |
| 1 | Very poorly drained |
| 2 | Poorly drained |
| 3 | Imperfectly drained |
| 4 | Moderately well drained |
| 5 | Well drained |
| 6 | Rapidly drained |

Table 13: Landform elements (after Speight 1990)

| Code | Landform element | Code | Landform element |
| --- | --- | --- | --- |
| ALC | Alcove | LAK | Lake |
| BAN | Bank | LDS | Landslide |
| BAR | Bar | LEV | Levee |
| BEA | Beach | LUN | Lunette |
| BEN | Bench | MAA | Maar |
| BER | Berm | MOU | Mound |
| BKP | Backplain | OXB | Ox-bow |
| BOU | Blow out | PED | Pediment |
| BRI | Beach ridge | PIT | Pit |
| BRK | Breakaway | PLA | Plain |
| CBE | Channel bench | PLY | Playa |
| CFS | Cliff-foot slope | PST | Prior stream |
| CIR | Cirque | REF | Reef flat |
| CLI | Cliff | RFL | Rock flat |
| CON | Cone | RPL | Rock platform |
| COS | Cut-over surface | SCA | Scarp |
| CRA | Crater | SCD | Scald |
| CUT | Cutface | SCR | Scroll |
| DAM | Dam | SFS | Scarp-foot slope |
| DDE | Drainage depression | SRP | Scroll plain |
| DOL | Doline | STB | Stream bed |
| DUC | Dunecrest | STC | Stream channel |
| DUN | Dune | STF | Supratidal flat |
| DUS | Duneslope | SUS | Summit surface |
| EMB | Embankment | SWL | Swale |
| EST | Estuary | SWP | Swamp |
| FAN | Fan | TAL | Talus |
| FIL | Fill-top | TDC | Tidal creek |
| FLD | Flood-out | TDF | Tidal flat |
| FOO | Footslope | TEF | Terrace flat |
| FOR | Foredune | TEP | Terrace plain |
| GUL | Gully | TOR | Tor |
| HCR | Hillcrest | TRE | Trench |
| HSL | Hillslope | TUM | Tumulus |
| ITF | Intertidal flat | VLF | Valley flat |
| LAG | Lagoon |  |  |

## Land Surface

Descriptions of the land surface are defined by: microrelief type, the described gilgai component (if present), biotic agent, and biotic component. The descriptors follow the definitions of McDonald et al. (1990) and the codes are presented in Table 14, Table 15, Table 16, and Table 17 respectively.

#### Rock outcrop

Rock outcrop is the percentage of the land-unit tract (usually a land facet) occupied by rock outcrop. Care is needed to avoid double counting with surface coarse fragments.

#### Surface coarse fragments

The areal percentage of surface coarse fragments is recorded as a percentage for the land facet (Table 13) or land system if it is the lowest level recorded.  These variables are recorded for five size classes: gravelly (2–60mm), cobbles (60-200 mm), stones (200-600 mm), boulders (600 mm – 2m) and large boulders (>2 m).

Table 14: Microrelief type

| Code | Code desciption |
| --- | --- |
| Z | No microrelief |
| NR | Microrelief not recorded |
| A | Lattice gilgai |
| C | Crabhole gilgai |
| D | Debil-debil |
| G | Contour gilgai |
| H | Spring hollow |
| I | Sinkhole |
| K | Karst microrelief |
| L | Linear gilgai |
| M | Melonhole gilgai |
| N | Normal gilgai |
| O | Other |
| P | Spring mound |
| R | Terracettes |
| S | Mass movement microrelief |
| T | Contour trench |
| U | Mound/depression microrelief |
| W | Swamp hummock |

Table 15: Described gilgai component (if present)

| Code | Code desciption |
| --- | --- |
| D | Depression |
| M | Mound |
| S | Shelf |

Table 16: Biotic agent for microrelief (if present)

| Code | Code desciption |
| --- | --- |
| A | Ant |
| B | Bird |
| M | Man |
| N | Animal |
| O | Other |
| T | Termite |
| V | Vegetation |

Table 17: Biotic component of microrelief (if present)

| Code | Code desciption |
| --- | --- |
| D | Depression |
| H | Hole |
| M | Mound |
| O | Other |
| T | Terrace |

## Soil

Soil in the land-unit tract at the finest level of resolution (usually Level 6) is described using the descriptors outlined in the following sections (unless the land unit is composed entirely of bare rock). If a land-unit tract (e.g., Level-6 land facet) has several component soils, then the land unit description remains the same, with separate soil descriptions for each component.

The soil profile descriptions for a land unit refer to an idealized soil. Estimates for attributes are derived from various sources including field descriptions, detailed representative profiles, and general field knowledge – all estimates have an accompanying measure of uncertainty (page 24). Soil data relating to actual soils are presented in the representative soil profile data base (page 72).

### Control sections

Soil profiles vary greatly in the morphology, composition, dimensions, and arrangement of soil horizons and stratigraphic layers. Generalization and simplification are essential for land evaluation and spatial analysis. As a consequence, a simple but sufficient model is needed to describe idealized soils in the land-unit hierarchy.

Each idealized soil profile is represented by five contiguous soil layers (see Figure 7 for examples). The layers are intended to discriminate materials in terms of their function in relation to water and gas movement, nutrient supply, plant growth, and physical behaviour more generally. Numbers are used to denote the layers and attributes (e.g., Layer-1 texture, Layer-3 organic carbon), and they will often correspond with particular types of soil horizons. In general, terms, Layers 1 and 2 refer to the A horizon (often an A1 and A2 horizon respectively), Layers 3 and 4 refer to the subsoil (often a B21 and B22 horizon respectively), and Layer 5 refers to the profile base (often a C horizon at around 1.5-2.0 m). Judgement is needed to define the layers in complex profiles (e.g. buried soils with pans) where the simple A-B-C sequence of master horizons is not evident.

The first step in preparing soil estimates is to define the position of the five soil layers and record their thicknesses. It is important to ensure the five layers are contiguous and that layer thicknesses sum to equal the total profile depth – this is necessary for calculation of integral properties such as the profile and plant available water capacities.

The rules for defining the layers and estimating attributes are reasonably straightforward. In most cases, attribute values are averages for a specified layer (e.g. available water capacity, texture). In some instances, attribute values refer to a particular part of the layer. For example, Layer-1 hydraulic conductivity refers to the upper few centimetres of the layer, while Layer-3 bulk density refers to the densest part of the layer. The following sections provide guidance on defining and describing the five generalized layers. It is difficult to anticipate all possible cases and judgement will be needed when soils have many contrasting layers.

If the A horizon of the idealized soil is thin and the profile has only a few layers (i.e., two or three), then Layer 2 may be recorded as missing. If the A horizon is thin, but multiple and contrasting layers occur deeper in the profile, Layer 2 can refer to layers below the A horizon (e.g., B1, IIA, IIB).

As noted earlier, Layers 3 and 4 in most profiles refer to the upper and lower B horizon respectively. In stratigraphically complex profiles, Layers 3 and 4 are defined according to how the profile functions in relation to plant growth and water movement (e.g., Figure 7c).

The soil data include a cross-reference to the ASRIS Soil Profile Database. The cross-reference is a link to a representative soil profile for the land-unit tract along with a measure of its similarity (Table 18) – this measure will be possibly augmented with a multivariate statistical metric at a later date. Ideally, land-unit tracts should have representative soil profiles nominated with a similarity of 1–3: relying on profiles with a similarity of 4 or 5 will be problematic in most instances.

Figure 7: Examples of horizon sequences and allocation to the five-layer model used to describe idealized soil profiles in the land-unit hierarchy.  Example (a) is a common sequence. In example (b), Layers 2 and 4 are recorded as missing because the profile is shallow and has only a few horizons. Example (c) is a complex profile and Layers are specified according to their influence on plant growth and water movement.

Table 18: Representativeness of the most similar soil profile in the ASRIS Soil Profile Database

| Similarity | Description |
| --- | --- |
| 1 | Representative profile sampled within the land-unit tract |
| 2 | Representative profile sampled from the same land unit type |
| 3 | Representative profile for the soil profile class, and sampled within the region. |
| 4 | Representative profile from another district but allocated to the same taxon within the Australian Soil Classification at the Great Group level or more detailed |
| 5 | Most similar profile from the ASRIS soil profile database based on expert judgement |

#### Texture

Texture class and clay content (%) are estimated for the five layers. In Australia, field texture is not synonymous with the particle size distribution. The former integrates particle size information with extra aspects relating to soil mechanical behaviour – the latter is affected by mineralogy, sodicity, organic matter content and cation composition. Estimates of clay content based on field texturing should therefore take these factors into account. For example, a Red Ferrosol with 80% clay that is very strongly aggregated can have a clay-loam texture, while another soil with a clay content of only 35%, but strong sodicity and abundant fine sand, may have a heavy-clay texture.

Estimation methods for texture and clay content are recorded (Table 19 and Table 20). Field-texture follows the definitions in McDonald and Isbell (1990) – the codes are shown in Table 21. Use of the modifiers and qualifiers is optional.

Table 19: Estimation method for field texture

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of field texture for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of field texture in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

Table 20: Estimation method for clay content

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated laboratory measurements of particle size from representative soil profiles in the land-unit tract |
| 2 | Estimate based on laboratory measurement of particle size from a representative soil profile in the land-unit tract |
| 3 | Estimate based on particle size analysis on similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate is based on field textures from representative soil profiles in the land-unit tract |
| 5 | Estimate based on particle size analysis of similar soils in the region or project area |
| 6 | Estimate is based on field textures from soil profiles in the land-unit tract |
| 7 | Estimate is based on field textures from similar soils in the project area |
| 8 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-1 Texture and clay content

The control section and convention for recording Layer-1 Texture and Layer-1 Clay Content are as follows.

If there is a single A1 horizon without subdivisions (e.g. A11, A12 etc.), then Layer-1 Texture and Layer-1 Clay Content are the texture and clay content of the A1 horizon.

If there are subdivisions within the A1 horizon, the Layer-1 Texture and Layer-1 Clay Content are taken from the thickest A horizon layer within the top 0.20 m of the soil profile (the upper layer is used if thicknesses are equal).

If the surface layer is an O horizon, the texture of the underlying A1 horizon is used in accord with the above criteria.  If there is no underlying A1 horizon, the Layer-1 Texture and Layer-1 Clay Content are taken from the thickest layer in the 0.20 m directly beneath the O horizon.

If the surface layer is a peat, Layer-1 Texture and Layer-1 Clay Content are recorded using the 7 classes of organic materials defined by McDonald and Isbell (1990) and shown in Table 21.

##### Layer-2 Texture and clay content

The Layer-2 Texture and Layer-2 Clay Content usually refer to the average texture and clay content of the lower portion of the A horizon.  The A horizon at this depth may be an A1, A2, A3, AB or subdivision thereof.

If the surface layer is not an A1 horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing (NA for texture, -9999 for clay content –see page 73)

If the A horizon is thin and the profile only has a few layers, Layer-2 Texture and Layer-2 Clay Content may be recorded as missing.

If the A horizon is thin and multiple contrasting layers occur deeper in the profile, Layer-2 Texture and Layer-2 Clay Content  can refer to layers below the A (e.g. B1, 2A, 2B, 2D).

##### Layer-3 Texture and clay content

The B-horizon definition below follows the Field Handbook with the modification suggested by Isbell (1996) (the criteria in part being “…an illuvial concentration of silicate clay, iron, aluminium, humus, carbonates, gypsum, or silica, alone or in combination”). The Layer-3 Texture and Layer-3 Clay Content are defined in most cases as follows.

- If a B horizon is present, the Layer-3 Texture and Layer-3 Clay Content are the texture encountered in the upper B (usually B1 and B21).

- If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Texture and Layer-3 Clay Content generally refers to the materials directly below the A horizon (usually the upper 0.20 m).

- In more complex profiles, Layer-3 Texture and Layer-3 Clay Content refer to the third functional layer in the profile.

##### Layer-4 Texture and clay content

In most profiles, Layer-4 Texture and Layer-4 Clay Content refer to the lower part of the B horizon – this is usually a B22 or B3 and it often starts at around 0.80 m. If the profile and B horizon are thin (<1.0 m and <0.20 m respectively) and overlie an R horizon, Layer 4 may be recorded as missing.

##### Layer-5 Texture and clay content

The Layer-5 Texture and Layer-5 Clay Content are normally estimated at a depth between 1.5–2.0 m. The intention is to characterize the material in the lower portion or base of the potential root zone. If an R horizon or hard materials (including a continuous calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer-4 estimate, then the Layer-5 Texture and Layer-5 Clay Content applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing (NA for texture, -9999 for clay content – see page 73).

Table 21: Field-texture grades, modifiers and qualifiers

| Code | Grade | Code | Modifiers and qualifiers |
| --- | --- | --- | --- |
| S | Sand | FS | Fine sand |
|  |  | MS | Medium sand |
|  |  | KS | Coarse sand |
|  |  | SA | Sapric sand |
|  |  | SI | Fibric sand |
| LS | Loamy sand | LFS | Loamy fine sand |
|  |  | LMS | Loamy medium sand |
|  |  | LKS | Loamy coarse sand |
|  |  | LSA | Sapric loamy sand |
|  |  | LSI | Fibric loamy sand |
| CS | Clayey sand | CFS | Clayey fine sand |
|  |  | CMS | Clayey medium sand |
|  |  | CKS | Clayey coarse sand |
|  |  | CSA | Sapric clayey sand |
|  |  | CSI | Fibric clayey sand |
| SL | Sandy loam | FSL | Fine sandy loam |
|  |  | MSL | Medium sandy loam |
|  |  | KSL | Coarse sandy loam |
|  |  | SLA | Sapric sandy loam |
|  |  | SLI | Fibric sandy loam |
| L | Loam | LA | Sapric loam |
|  |  | LI | Fibric loam |
| ZL | Silty loam | ZLA | Sapric silty loam |
|  |  | ZLI | Fibric silty loam |
| SCL | Sandy clay loam | SCLFS | Sandy clay loam, fine sand |
|  |  | SCLA | Sapric sandy clay loam |
|  |  | SCLI | Fibric sandy clay loam |
| CL | Clay loam | FSCL | Fine sandy clay loam |
|  |  | MSCL | Medium sandy clay loam |
|  |  | KSCL | Coarse sandy clay loam |
|  |  | CLA | Sapric clay loam |
|  |  | CLI | Fibric clay loam |
| CLS | Clay loam, sandy | CLFS | Clay loam, fine sandy |
|  |  | CLMS | Clay loam, medium sandy |
|  |  | CLKS | Clay loam, coarse sandy |
|  |  | CLSA | Sapric clay loam, sandy |
|  |  | CLSI | Fibric clay loam, sandy |
| ZCL | Silty clay loam | ZCLA | Sapric silty clay loam |
|  |  | ZCLI | Fibric silty clay loam |
| LC | Light clay | SLC | Sandy light clay |
|  |  | FSLC | Fine sandy light clay |
|  |  | MSLC | Medium sandy light clay |
|  |  | KSLC | Coarse sandy light clay |
|  |  | ZLC | Silty light clay |
|  |  | LCA | Sapric light clay |
|  |  | LCI | Fibric light clay |
| LMC | Light medium clay | ZLMC | Silty light medium clay |
|  |  | SLMC | Sandy light medium clay |
|  |  | FSLMC | Fine sandy light medium clay |
|  |  | MSLMC | Medium sandy light medium clay |
|  |  | KSLMC | Coarse sandy light medium clay |
|  |  | LMCA | Sapric light medium clay |
|  |  | LMCI | Fibric light medium clay |
| MC | Medium clay | ZMC | Silty medium clay |
|  |  | SMC | Sandy medium clay |
|  |  | FSMC | Fine sandy medium clay |
|  |  | MSMC | Medium sandy medium clay |
|  |  | KSMC | Coarse sandy medium clay |
|  |  | MCA | Sapric medium clay |
|  |  | MCI | Fibric medium clay |
| MHC | Medium heavy clay | ZMHC | Silty medium heavy clay |
|  |  | SMHC | Sandy medium heavy clay |
|  |  | FSMHC | Fine sandy medium heavy clay |
|  |  | MSMHC | Medium sandy medium heavy clay |
|  |  | KSMHC | Coarse sandy medium heavy clay |
|  |  | MHCA | Sapric medium heavy clay |
|  |  | MHCI | Fibric medium heavy clay |
| HC | Heavy clay | SHC | Sandy heavy clay |
|  |  | FSHC | Fine sandy heavy clay |
|  |  | MSHC | Medium sandy heavy clay |
|  |  | KSHC | Coarse sandy heavy clay |
|  |  | ZHC | Silty heavy clay |
|  |  | HCA | Sapric heavy clay |
|  |  | HCI | Fibric heavy clay |
| AP | Sapric peat |  |  |
| SP | Sandy peat |  |  |
| LP | Loamy peat |  |  |
| CP | Clayey peat |  |  |
| GP | Granular peat |  |  |
| HP | Hemic peat |  |  |
| IP | Fibric peat |  |  |

#### Coarse fragments

Coarse fragments are estimated using the conventions in McDonald et al. (1990). The main purpose for the variable is to allow calculation of available water capacity. In ASRIS, hard segregations are included in the estimate of coarse fragments. Judgment is needed with porous segregations that store water or provide surfaces for ion-exchange. If these are present, then the porosity of coarse fragments needs to be estimated. In most regions, porosity of coarse fragments will be 0.00 m3/m3 (see page 55). Use Table 22 for the estimation method.

The abundance of coarse fragments is estimated as an average percentage for each of the five layers (if source data rely on the classes listed by McDonald et al. (1990, p97), then use midpoints of each class). The guidelines for texture apply to coarse fragments.

Table 22: Estimation method for coarse fragments

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on replicated measurements of coarse fragments in an exposure or soil pits within the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of coarse fragments in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils |

#### Bulk density

The bulk density estimation method is recorded (Table 23) along with the bulk density for each layer.  Apart from Layer-3, the bulk density is the average for each Layer. The guidelines on control sections used for Texture apply generally for bulk density.

The Layer-3 Bulk Density is estimated as follows.

In soils with a B2 horizon, the estimate is for the densest portion of the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Bulk Density is taken from the densest layer in the 0.20 m directly below the A horizon.

The Layer-5 bulk density is normally estimated at a depth between 1.5–2.0 m. The intention is to characterize the material in the lower portion or base of the potential root zone. If an R horizon or hard materials (including a continuous calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer-4 estimate, then the Layer-5 Bulk density applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing (NA for texture, -9999 for clay content – see Section 13.1).

Table 23: Estimation method for bulk density

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of bulk density for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of bulk density in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

#### pH profile

The pH in a 1:5 CaCl2 solution is estimated for the five layers in the soil profile. If measurements have been performed using 1:5 soil-to-water, then use the conversion table in Appendix 1 taken from Henderson and Bui (2003). The estimation method is shown in Table 24.

##### Layer-1 pH

The Layer-1 pH is recorded as follows.

In most instances, the estimate applies to the upper 50 mm of the A1 horizon.

If the surface layer is an O horizon, the estimate applies to the upper 50 mm of the underlying A horizon.  If there is no underlying A horizon, the Layer-1 pH refers to the 50 mm thick layer directly beneath the O horizon.

If the surface layer is a peat, the estimate applies to the upper 50 mm of the surface horizon.

If the A1 horizon is thinner than 50 mm, then the estimate is for the horizon.

Table 24: Estimation method for pH

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of pH for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of pH in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### pH in Layers 2–5

The pH for these layers is an average rather than an estimate for the upper portion. The guidelines on the definition of layers used for texture apply to Layers 2–5. If no B horizon is present and the sequence consists of an AC profile, the Layer-3 pH is taken from the layer 0.20 m directly below the A horizon. Again, the Layer-5 estimate refers to a depth between 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below Layer 4, then the Layer-5 pH applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

#### Organic carbon

Organic carbon is estimated for the five layers using the same guidelines presented for pH. The estimation methods are shown in Table 25.

Table 25: Estimation method for organic carbon.

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of organic carbon for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of organic carbon in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

#### Diagnostic Depths

Several diagnostic depths are recorded (m) apart from the thickness of each of the five layers to allow flexible analysis including the calculation of  plant available water capacity (page 54). The estimation method is also recorded (Table 26).

Table 26: Estimation method for depths and layer thicknesses

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of depth for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of depth supplemented by opportunistic sampling (e.g. road cuttings) |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils and landscapes from other regions |

##### Depth of A1

The depth of A1 horizon is recorded in meters. If an A1 is not present (e.g. OB profile), then the attribute is recorded as missing.

##### Total thickness of A horizon

The total thickness of A horizon is recorded in meters. If an A is not present (e.g. OB profile), then the attribute is recorded as missing.

##### Depth to B2 horizon

The depth from the landsurface to the top of the B2 is recorded in meters.  If there is no B horizon (e.g. AC profile), then the attribute is recorded as missing.

##### Depth to impeding layer

The depth to impeding layer will in many cases be difficult to estimate.  An impeding layer prevents root growth beyond the layer. If sufficient information is available, the depth to impeding layer is estimated for:

Annual crops and pastures – ACP (e.g., wheat, barley, canola)

Perennial pastures – PP (e.g., lucerne), and

Perennial native vegetation – PNV (e.g., trees and shrubs).

##### Impeding layer type

Impeding layer type is recorded for each vegetation type (Table 27, Table 28). Peverill et al. (1999) provide a basic reference on chemical toxicities and deficiencies.

##### Depth to base of regolith

Regolith refers to the “mantle of earth and rock, including weathered rocks and sediments, altered or formed by land surface processes” (Speight and Isbell 1990). Depth to the base of regolith is estimated in meters.  It will be difficult to estimate in many instances, particularly in deeply weathered landscapes where depths greater than 100 m are not uncommon.

Table 27: Type of impeding layer

| Code | Type of impeding layer |
| --- | --- |
| CT | chemical toxicity (e.g., boron) |
| CD | chemical deficiency (e.g., very low or zero available P) |
| PI | direct physical impedance (e.g., moist soil strength > 4 MPa or R horizon) |
| HY | hydrologic (e.g., permanent water table) |

Table 28: Estimation method for the type of impeding layer

| Code | Estimation method |
| --- | --- |
| 1 | Direct field observation of root patterns for the plant type (ACP, PP, PNV) with supporting soil analytical data within the land-unit tract |
| 2 | Interpretation of analytical data (relying on published limits for plants in question) |
| 3 | Direct field observation of root patterns for the plant type (ACP, PP, PNV) with supporting soil analytical data for similar soils in the region |
| 4 | Interpretation of analytical data (relying on published limits for plants in question) for similar soils in the region |
| 5 | General experience with morphologically similar soils |

#### Water retention and available water capacity

An estimate is made of the volumetric water content at –10 kPa (notional field capacity) and –1.5 MPa (notional wilting point) of the fine earth fraction for the five layers (see below for the procedure for discounting the effect of coarse fragments).  An accompanying method code is also recorded (Table 29). The estimates of volumetric water content are averages for each layer and they are used with the layer thicknesses to calculate an approximate profile available water capacity.  Note that water contents at –10 kPa and –1.5 MPa can be estimated using Williams et al. (1992) on the basis of field texture, bulk density and structure grade (see ASRIS website for a downloadable spreadsheet to perform the estimation).

The guidelines for estimating volumetric water contents at –10 kPa and –1.5 MPa are similar to those used for texture, coarse fragments and bulk density.

Layer-5 thickness will often be problematic. In landscapes with deep regolith, an arbitrary maximum corresponding to the likely maximum depth of rooting by perennial native plants may be sufficient. Note that the estimates of water retention ((–10kPa and (–1.5MPa) for Layer 5 usually relate to a depth of 1.0–1.5 m, and that application of the discounting method for water extraction (see below) means that the contribution of materials at depth is heavily discounted in the calculation of plant available water capacity.

Plant available water capacity can be estimated for the three generalized types of vegetation noted above (viz. annual crops and pastures, perennial pastures, and native trees and shrubs) by discounting the available water capacity for each layer. This discounting can be based on generalized models of root distribution and likely water extraction patterns (e.g., McKenzie et al. 2003) or through estimation of the non-limiting water range for each layer (e.g., using information on bulk density and nutrient availability).

If the surface layer is a peat, Layer-1 (–10 kPa and (–1.5MPa is recorded only if direct measurements are available. Reliable pedotransfer functions for Australian conditions are not yet available and very few such soils have been characterized.

Table 29: Estimation method for the estimation of water retention parameters

| Method | Description |
| --- | --- |
| 1 | Estimate derived from direct measurements of water retention in the land-unit tract |
| 2 | Water retention data estimated from direct measurements (e.g. Cresswell and Paydar (1996)) |
| 3 | Water retention data estimated using pedotransfer functions such as Williams et al. (1992) and with predictor variables derived from measurements in the land-unit type |
| 4 | Estimate based on direct measurements of similar soils |
| 5 | Estimate based on experience with similar soils |

##### Discounting estimates of available water capacity

The estimates of water retention listed above refer to the fine-earth fraction (e.g. AWCfe). They need to be adjusted to take account of coarse fragments, both their volumetric percentage and porosity, to estimate available water capacity of the whole soil (AWCws).

In most cases, coarse fragments will be non-porous and the right-hand term will be zero (i.e. AWCcf = 0). Estimation of water retention properties for porous coarse fragments (e.g. AWCcf) is difficult because reliable data are rarely available. Cresswell and Hamilton (2002) outline how to calculate total porosity in the presence of porous coarse fragments. However, information is needed on the water retention properties of the coarse fragments before a reliable estimate can be made on a whole-soil basis. If coarse fragments have the same water retention properties as the fine earth, then the AWCws and AWCfe will be equivalent. It is feasible for AWC of the coarse fragments to be greater than AWCfe (i.e. AWCws and coarse fragment content will be positively correlated). The procedure for estimation will vary depending on the availability of information.

The estimate of coarse fragment percentage for the layers (see page 49) are averages and care is needed when bands of coarse fragments are present. Porous coarse fragments are common in some parts of Australia (e.g., southwest Western Australia).

#### Calculating Profile and Plant Available Water Capacity

Five variables are used to calculate profile available water capacity ((–10 kPa, (–1.5MPa, layer thickness, and the percentage and porosity of coarse fragments) and a sixth is needed for plant available water capacity to express the degree to which plants can extract the water. The water retention and layer thickness variables are described above. A simple estimate of Plant Available Water Capacity can be generated by summing the available water capacities over the depth of the root zone – the depth to impeding layer along with a maximum rooting depth for the vegetation type in question can be used. An improved approximation can be made by applying a scaling term that discounts the available water capacity according to the capacity for roots to extract water. One such method is described by McKenzie et al. (2003) and shown in Figure 8 and Figure 9. While largely untested, their proposed discounting function uses a single parameter to summarize the effectiveness of water extraction – it can be estimated using soil attributes within ASRIS (e.g., bulk density, ESP, taxonomic class) along with the vegetation type.

Figure 8: Scaling term for water storage. The curves range from those likely for a soil with severe root constraints (e.g. Sodosols, Xi=0.2–0.4 m) to a deep soil without constraints (e.g. Red Ferrosol, Xi=2.0 m).

Figure 9: Calculation procedure for plant available water capacity

#### Permeability

The permeability of each layer is recorded using estimates of saturated hydraulic conductivity. A coarse stepped scale is presented in Table 30, the median values for each class are equidistant on a logarithmic scale because Ks data are generally log-normally distributed. The descriptive names are approximately the same as McDonald and Isbell (1990).  The accompanying method codes are presented in Table 31.

##### Layer-1 Ks

The Layer-1 Ks is for the soil surface.

If the soil has a surface crust or surface flake (McDonald et al. 1990), the estimate is for the upper 10 mm of the surface horizon.

If there is no surface crust or flake, the estimate applies to the upper 0.20 m of the A1 horizon if present. If the Layer-3 Ks control section upper boundary is within 0.20 m of the surface, Layer-1 Ks applies to the layer above the upper boundary of the Layer-3 Ks control section.

If the surface layer is an O horizon, the estimate applies to the upper 50 mm of the underlying A horizon.  If there is no underlying A horizon, the Layer-1 Ks refers to the 50 mm thick layer directly beneath the O horizon.

If the surface layer is a peat, the estimate applies to the upper 50 mm of the surface horizon.

If the A1 horizon is thinner than 50 mm, then the estimate is for the horizon.

##### Layer-2 Ks

The Layer-2 Ks is usually the average saturated hydraulic conductivity of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded is usually recorded as missing.

If the A horizon is thin and multiple contrasting layers occur deeper in the profile, Layer-2 Ks can refer to layers below the A (e.g. B1, 2A, 2B, 2D).

##### Layer-3 Ks

In soils with a B2 horizon, the estimate generally is for the least permeable portion of the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

If no B horizon is present and the sequence consists of an AC profile, the Layer-3 Ks is usually taken from the least permeable layer in the 0.20 m directly below the A horizon.

##### Layer-4 Ks

In soils with a thick B horizon, the estimate generally is for the least permeable portion of the lower B2 or B3 horizon.

If no B horizon is present or the sequence consists of multiple contrasting layers, the Layer-4 Ks is usually taken from the least permeable layer from 0.8–1.5 m.

##### Layer-5 Ks

The Layer-5 Ks is estimated as the least permeable layer between 1.5–3.0 m.  If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer 4 estimate, then the Layer-5 Ks applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

Table 30: Permeability classes

| Class | Median Ks (mm/hr) | Class boundaries (mm/hr) |
| --- | --- | --- |
|  |  | 0 |
| Impermeable | 0.01 |  |
|  |  | 0.03 |
| Very slowly permeable | 0.1 |  |
|  |  | 0.3 |
| Slowly permeable | 1 |  |
|  |  | 3 |
| Moderately permeable | 10 |  |
|  |  | 30 |
| Highly permeable | 100 |  |
|  |  | 300 |
| Extremely permeable | 1000 |  |
|  |  | >>1000 |

Table 31: Estimation method for saturated hydraulic conductivity

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on direct laboratory measurements of saturated hydraulic conductivity using undisturbed soil cores within the land-unit type |
| 2 | Estimate based on direct field measurements of saturated hydraulic conductivity using permeameters within the land-unit type |
| 3 | Estimate based on pedotransfer functions using predictor variables from the land-unit tract |
| 4 | Estimate based on direct measurements on similar soils |
| 5 | Estimate based on experience with similar soils |

#### Electrical conductivity

The electrical conductivity (EC) is estimated for the five layers. The estimation method is recorded according to Table 32. The electrical conductivity refers to a 1:5 soil:water extract and the units are dS/m.

##### Layer-1 EC

If there is a single A1 horizon without subdivisions (e.g. A11, A12 etc.), then estimate the Layer-1 EC using the A1 horizon.

If there are subdivisions within the A1 horizon, the Layer-1 EC is generally taken from the thickest A horizon layer within the top 0.20 m of the soil profile (the upper layer is used if thicknesses are equal).

If the surface layer is an O horizon, the underlying A horizon is used in accord with the above criteria.

If the surface layer is a peat, the estimate applies to the upper 0.20 m of the surface horizon.

##### Layer-2  EC

The Layer-2 EC is generally the average electrical conductivity of the lower 100 mm of the A horizon.  The A horizon at this depth may be an A1, A2, A3 or subdivision thereof.

If the surface layer is not an A horizon (e.g. O horizon) and there is no underlying A horizon, the attribute is recorded as missing.

If the A horizon is thin and the profile only has a few layers, Layer-2 EC may be recorded as missing.

If the A horizon is thin and multiple contrasting layers occur deeper in the profile, Layer-2 EC can refer to layers below the A (e.g. B1, 2A, 2B, 2D).

##### Layer-3 EC

In soils with a B2 horizon, the estimate is for the upper 0.20 m of the B2 horizon (or for the major part of the B2 horizon if it is less than 0.20 m thick).

In more complex profiles, Layer-3 EC refers to the third functional layer in the profile.

##### Layer-4 EC

In most profiles, Layer-4 EC refers to the lower part of the B horizon – this is usually a B22 or B3 and it often starts at around 0.80 m. If the profile and B horizon are thin (<1.0 m and <0.20 m respectively) and overlie an R horizon, Layer 4 may be recorded as missing.

##### Layer-5 EC

The Layer-5 EC is estimated at a depth of approximately 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below the control section used for the Layer-4 estimate, then the Layer-5 EC applies to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

Table 32: Estimation method for electrical conductivity

| Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of electrical conductivity for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of electrical conductivity in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

#### Aggregate stability

Aggregate stability is estimated using a three-class system based on Emerson (2002) (Table 33) using the same control sections as for electrical conductivity. The method code is also recorded (Table 34).

Table 33: Aggregate stability classes based on Emerson (2002)

| Code | Class | Description |
| --- | --- | --- |
| S | Stable | Aggregates are stable in distilled water (e.g., Emerson Classes 1 and 2) |
| M | Moderately stable | Dispersion occurs after re-moulding when wet (e.g., Emerson Classes 3a and 3b ) |
| U | Unstable | Aggregates disperse spontaneously in distilled water (e.g., Emerson Classes 5 to 7) |

#### Water repellence

Water Repellence of the dry surface-soil layer is allocated to one of three levels according to Table 35. The estimation method is also recorded (Table 36). The Molarity of Ethanol Drop (MED) test has been used by some survey agencies during recent years (see Carter 2002). The attribute is not mandatory but is recorded in regions where water repellence is significant for hydrology and plant growth.

Table 34: Estimation method for aggregate stability

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of aggregate stability for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of aggregate stability in the land-unit tract |
| 3 | As for 2 but rapid measurement, often in the field (e.g. 1-hour dispersion) |
| 4 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 5 | Estimate based on direct measurements of similar soils in the region or project area |
| 6 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

Table 35: Water repellence (after Moore 1998).

| Code | Severity | Description |
| --- | --- | --- |
| N | None | Not significant (MED <1) |
| M | Moderate | Observed in most years and a strong manifestation 1 year in 3 (MED 1-2) |
| S | Severe | Strong manifestation in most years (MED >2) |

Table 36: Method for estimating water repellence of the land surface

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of water repellence for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of water repellence in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type and under a similar land management system |
| 4 | Estimate based on direct measurements of similar soils and land-use systems in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

#### Exchangeable bases, CEC, and ESP

Estimates of exchangeable bases (ie ((Ca+Mg+Na+K) in cmol/kg), CEC (cmol/kg), and Exchangeable Sodium Percentage (ESP) are made for the five layers using the same guidelines for pH. Estimates of Layers 2–5 are averages for the complete layer. Method codes describe both the estimation procedure (Table 37) and laboratory procedure – the latter is needed to distinguish between buffered and un-buffered methods (Table 38).

Table 37: Estimation method for exchangeable bases, CEC and ESP

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on measurements of exchangeable bases, CEC and ESP for replicated soil profiles in the land-unit tract |
| 2 | Estimate based on an un-replicated measurement of exchangeable bases, CEC and ESP in the land-unit tract |
| 3 | Estimate based on direct measurements of similar soils in the same land unit type (e.g., modal profiles) |
| 4 | Estimate based on direct measurements of similar soils in the region or project area |
| 5 | Estimate based on experience with similar soils (e.g., same taxa in the Australian Soil Classification but from other regions) |

##### Layer-1 Exchangeable bases, CEC, and ESP

In most instances, the estimate applies to the upper 50 mm of the A1 horizon.

If the surface layer is an O horizon, the estimate applies to the upper 50 mm of the underlying A horizon.  If there is no underlying A horizon, the estimates refer to the 50 mm thick layer directly beneath the O horizon.

If the surface layer is a peat, the estimate applies to the upper 50 mm of the surface horizon.

If the A1 horizon is thinner than 50 mm, then the estimate is for the horizon.

##### Exchangeable Bases, CEC, and ESP in Layers 2–5

The Exchangeable Bases, CEC, and ESP for these layers is an average rather than an estimate for the upper portion. The guidelines on the definition of layers used for texture apply to Layers 2–5. If no B horizon is present and the sequence consists of an AC profile, the Layer-3 estimates are taken from the layer 0.20 m directly below the A horizon. Again, the Layer-5 estimate refers to a depth between 1.5–2.0 m. If an R horizon or hard materials (including a calcrete pan, partially weathered rock or saprolite, or other hard materials) occurs at a shallower depth, and this is still below Layer 4, then the Layer-5 estimates apply to the lowest 100 mm in the profile. Otherwise the variable is recorded as missing.

Table 38: Method codes for Sum Exchangeable Bases, CEC, and ESP (These are currently under review by the Working Group on Land Resource Assessment)

| Code | Code description |  |
| --- | --- | --- |
| 15A1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, no pretreatment for soluble salts |  |
| 15A2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, pretreatment for soluble salts |  |
| 15A3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, adjusted for soluble sodium |  |
| 15B1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, no pretreatment for soluble salts |  |
| 15B2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, pretreatment for soluble salts |  |
| 15B3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium chloride at pH 7.0, adjusted for soluble sodium |  |
| 15C1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) - alcoholic 1M ammonium chloride at pH 8.5, pretreatment for soluble salts |  |
| 15D1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; manual leach |  |
| 15D2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; automatic extractor |  |
| 15D3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) – 1M ammonium acetate at pH 7.0, rapid method with no pretreatment for soluble salts |  |
| 15E1_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) by compulsive exchange, no pretreatment for soluble salts |  |
| 15E2_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) by compulsive exchange, pretreatment for soluble salts |  |
| 15E3_BASES | Exchangeable bases (Ca2+,Mg2+,Na+,K+) by compulsive exchange, adjusted for soluble sodium |  |
| 15F1_BASES | Exchangeable bases by 0.01M silver-thiourea (AgTU)+, no pretreatment for soluble salts |  |
| Cation Exchange Capacity |  |
| 15B1_CEC | CEC – 1M ammonium chloride at pH 7.0, no pretreatment for soluble salts |  |
| 15B2_CEC | CEC – 1M ammonium chloride at pH 7.0, pretreatment for soluble salts |  |
| 15B3_CEC | CEC – 1M ammonium chloride at pH 7.0, adjusted for soluble sodium |  |
| 15C1_CEC | CEC - alcoholic 1M ammonium chloride at pH 8.5, pretreatment for soluble salts |  |
| 15D1_CEC | CEC – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; manual leach |  |
| 15D2_CEC | CEC – 1M ammonium acetate at pH 7.0, pretreatment for soluble salts; automatic extractor |  |
| 15E1_CEC | CEC by compulsive exchange, no pretreatment for soluble salts |  |
| 15E2_CEC | CEC by compulsive exchange, pretreatment for soluble salts |  |
| 15E3_CEC | CEC by compulsive exchange, adjusted for soluble sodium |  |
| 15F3_CEC | CEC by 0.01M silver-thiourea (AgTU)+ |  |
| 15I1_CEC | CEC measurement - distillation of ammonium ions |  |
| 15I2_CEC | CEC measurement - automated determination of ammonium ions |  |
| 15I3_CEC | CEC measurement - automated determination of ammonium and chloride ions |  |
| 15I4_CEC | CEC measurement - titration of ammonium and chloride ions |  |
| 15JG_CEC | Effective CEC using 15G1 for exchangeable acidity |  |
| 15JH_CEC | Effective CEC using 15H1 for exchangeable acidity |  |
| 15K1_CEC | CEC – pH 8.2 |  |

#### Australian Soil Classification

The Australian Soil Classification (Isbell 1996) is recorded at the Soil Order level as a minimum.  Recording at the Sub-Order or Great Group level along with the Family level is preferred but in some areas will not be feasible. The confidence levels, version and method for allocation are also recorded (Table 39, Table 40, and Table 42)

Table 39: Confidence level for the allocation to the Australian Soil Classification

| Code | Code description |
| --- | --- |
| - | No confidence level recorded. |
| 1 | All necessary analytical data are available. |
| 2 | Analytical data are incomplete but reasonable confidence. |
| 3 | No analytical data are available but confidence is fair. |
| 4 | No analytical data and little or no knowledge of this soil. |

Table 40: Version of the Australian Soil Classification used for allocation

| Code | Code description |
| --- | --- |
| 2 | A Classification System for Australian Soils 2nd approximation |
| 3 | A Classification System for Australian Soils 3rd approximation |
| 4 | Australian Soil Classification 1st Edition |
| 5 | Australian Soil Classification Revised Edition |

Table 41: Codes for Soil Orders in the Australian Soil Classification

| Code | Soil Order | Code | Soil Order |
| --- | --- | --- | --- |
| AN | Anthroposol | KU | Kurosol |
| CA | Calcarosol | OR | Organosol |
| CH | Chromosol | PO | Podosol |
| DE | Dermosol | RU | Rudosol |
| FE | Ferrosol | SO | Sodosol |
| HY | Hydrosol | TE | Tenosol |
| KA | Kandosol | VE | Vertosol |

Table 42: Codes for Suborders, Great Groups and Subgroups in the Australian Soil Classification

| Code | Code description |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| AA | Red | BR | Epihypersodic | DL | Melanic-Bleached |
| AB | Brown | BS | Epic-Pedal | DM | Melanic-Mottled |
| AC | Yellow | BT | Extratidal | DN | Melanic-Vertic |
| AD | Grey | BU | Ferric | DO | Mellic |
| AE | Black | BV | Arenaceous | DP | Mesonatric |
| AF | Dystrophic | BW | Fibric | DQ | Mottled |
| AG | Mesotrophic | BX | Fluvic | DR | Subhumose |
| AH | Eutrophic | BY | Fragic | DS | Orthic |
| AI | Acidic | BZ | Gypsic | DT | Oxyaquic |
| AJ | Acidic-Mottled | CB | Calcarosolic | DU | Paralithic |
| AK | Andic | CC | Halic | DV | Parapanic |
| AL | Aeric | CD | Haplic | DW | Peaty |
| AM | Aquic | CE | Hemic | DX | Peaty-Parapanic |
| AN | Anthroposols | CF | Histic | DY | Pedal |
| AO | Arenic | CG | Humic | DZ | Petrocalcic |
| AP | Argic | CH | Chromosol | EA | Petroferric |
| AQ | Argillaceous | CI | Humic/Humosesquic | EB | Pipey |
| AR | Basic | CJ | Humic/Sesquic | EC | Placic |
| AS | Bauxitic | CK | Humose | ED | Redoxic |
| AT | Bleached | CL | Humose-Magnesic | EE | Rendic |
| AU | Bleached-Acidic | CM | Humose-Mottled | EF | Reticulate |
| AV | Bleached-Ferric | CN | Humose-Parapanic | EG | Salic |
| AW | Bleached-Leptic | CO | Humosesquic | EH | Sapric |
| AX | Bleached-Magnesic | CP | Hypervescent | EI | Self-Mulching |
| AY | Bleached-Manganic | CQ | Hypercalcic | EJ | Semiaquic |
| AZ | Bleached-Mottled | CR | Hypernatric | EK | Sesquic |
| BA | Bleached-Sodic | CS | Hypersalic | EL | Shelly |
| BB | Bleached-Vertic | CU | Epihypersodic-Epiacidic | EM | Silpanic |
| BC | Calcareous | CV | Hypocalcic | EN | Snuffy |
| BD | Calcic | CW | Intertidal | EO | Sodic |
| BE | Chernic | CX | Kurosolic | EP | Episodic-Epiacidic |
| BF | Chernic-Leptic | CY | Leptic | EQ | Sodosolic |
| BG | Chromosolic | CZ | Lithic | ER | Stratic |
| BH | Crusty | DA | Lithocalcic | ES | Subnatric |
| BI | Densic | DB | Magnesic | ET | Subplastic |
| BJ | Duric | DC | Manganic | EU | Sulfidic |
| BK | Pedaric | DD | Marly | EV | Sulfuric |
| BL | Endoacidic | DF | Massive | EW | Supratidal |
| BM | Endic | DG | Melacic | EX | Vertic |
| BN | Episodic | DH | Melacic-Magnesic | EY | Humose-Bleached |
| BO | Endic-Pedal | DI | Melacic-Mottled | EZ | Melacic-Bleached |
| BP | Endohypersodic | DJ | Melacic-Parapanic | FA | Siliceous |
| BQ | Epic | DK | Melanic | FB | Supracalcic |
| FC | Melanic-Calcareous | GU | Humose-Calcareous | IO | Brown-Orthic |
| FD | Natric | GV | Lutic | IP | Yellow-Orthic |
| FF | Submelacic | GX | Manganic-Acidic | IQ | Grey-Orthic |
| FG | Submelanic | GY | Humose-Acidic | IR | Black-Orthic |
| FH | Palic | GZ | Bleached-Orthic | IS | Ferric-Reticulate |
| FI | Ochric | HA | Melanic-Sodic | XX | Available Class Inappropriate |
| FJ | Hypergypsic | HB | Mottled-Sodic | YY | Class Undetermined |
| FK | Ferric-Duric | HC | Ferric-Sodic | ZZ | No Available Class |
| FL | Gypsic-Subplastic | HD | Rudaceous |  |  |
| FM | Epicalcareous-Epihypersodic | HE | Endocalcareous-Mottled |  |  |
| FN | Mottled-Subnatric | HF | Tephric |  |  |
| FO | Mottled-Mesonatric | HG | Carbic |  |  |
| FP | Mottled-Hypernatric | HH | Clastic |  |  |
| FQ | Dermosolic | HI | Colluvic |  |  |
| FR | Kandosolic | HJ | Lithosolic |  |  |
| FS | Terric | HK | Supravescent |  |  |
| FT | Humose-Basic | HL | Episulfidic |  |  |
| FU | Melacic-Basic | HM | Episulfidic-Petrocalcic |  |  |
| FV | Melanic-Acidic | HN | Densic-Placic |  |  |
| FW | Faunic | HO | Acidic-Sodic |  |  |
| FX | Lutaceous | HP | Palic-Acidic |  |  |
| FY | Epicalcareous | HQ | Ochric-Acidic |  |  |
| FZ | Endocalcareous | HR | Cumulic |  |  |
| GA | Epiacidic | HS | Hortic |  |  |
| GB | Epicalcareous-Endohypersodic | HT | Garbic |  |  |
| GC | Melacic-Reticulate | HU | Urbic |  |  |
| GD | Peaty-Placic | HV | Dredgic |  |  |
| GE | Ferric-Petroferric | HW | Spolic |  |  |
| GF | Regolithic | HX | Scalpic |  |  |
| GG | Episodic-Endoacidic | HZ | Ashy |  |  |
| GH | Episodic-Epicalcareous | IA | Inceptic |  |  |
| GI | Episodic-Endocalcareous | IB | Epibasic |  |  |
| GJ | Epicalcareous-Endoacidic | IC | Ceteric |  |  |
| GK | Epiacidic-Mottled | ID | Subpeaty |  |  |
| GL | Endoacidic-Mottled | IE | Effervescent |  |  |
| GM | Endocalcareous-Endohypersodic | IF | Folic |  |  |
| GN | Epihypersodic-Endoacidic | IG | Humosesquic/Sesquic |  |  |
| GO | Epihypersodic-Endocalcareous | IH | Humic/Alsilic |  |  |
| GP | Magnesic-Natric | IJ | Modic |  |  |
| GQ | Episodic-Gypsic | IK | Histic-Sulfidic |  |  |
| GR | Rudosolic | IL | Sequi-Nodular |  |  |
| GS | Epipedal | IM | Calcenic |  |  |
| GT | Tenosolic | IN | Red-Orthic |  |  |

Table 43: Codes for Family criteria in the Australian Soil Classification

| Code | Code description |  |  |
| --- | --- | --- | --- |
| - | Not recorded | M | Clay-loamy |
| A | Thin | N | Silty |
| B | Medium | O | Clayey |
| C | Thick | P | Granular |
| D | Very thick | Q | Fine |
| E | Non-gravelly | R | Medium fine |
| F | Slightly gravely | S | Very fine |
| G | Gravelly | T | Very shallow |
| H | Moderately gravelly | U | Shallow |
| I | Very gravely | V | Moderately deep |
| J | Peaty | W | Deep |
| K | Sandy | X | Very deep |
| L | Loamy | Y | Giant |

Table 44: Method for allocating profile to the classification system (either ASC or WRB)

| Method | Description based on: |
| --- | --- |
| 1 | Morphology and analytical data from the land-unit tract |
| 2 | Morphology data from the land-unit tract |
| 3 | Morphology and analytical data from similar soils in the same land unit type |
| 4 | Morphology data for similar soils in the region or project area |
| 5 | Experience with morphologically similar soils in other regions |

#### World Reference Base

Allocation to the World Reference Base to the level of the Reference Group with one or two qualifiers is preferred but conversion of historic data sets may not be possible in the short term. This attribute is required to ensure compatibility with SOTER.

Experience with the World Reference Base in Australia is limited and few allocations have been recorded in agency databases. The time needed to allocate soils within ASRIS is not available. As an interim measure, dominant soils will be identified at approximately Level 3 within ASRIS – the most common three will be allocated to the World Reference Base.

Table 45: Reference Soil Group codes for the World Reference Base

| Code | Code description |  |  |
| --- | --- | --- | --- |
| AB | Albeluvisol | HS | Histosol |
| AC | Acrisol | KS | Kastanozem |
| AL | Alisol | LP | Leptosol |
| AN | Andosol | LV | Luvisol |
| AR | Arenosol | LX | Lixisol |
| AT | Anthrosol | NT | Nitisol |
| CH | Chernozem | PH | Phaeozem |
| CL | Calcisol | PL | Planosol |
| CM | Cambisol | PT | Plinthosol |
| CR | Cryosol | PZ | Podzol |
| DU | Durisol | RG | Regosol |
| FL | Fluvisol | SC | Solonchak |
| FR | Ferralsol | SN | Solonetz |
| GL | Gleysol | UM | Umbrisol |
| GY | Gypsisol | VR | Vertisol |

Table 46: Qualifiers for Reference Soil Groups in the World Reference Base

| Code | Qualifier | Code | Qualifier | Code | Qualifier |
| --- | --- | --- | --- | --- | --- |
| AB | Albic | FI | Fibric | LEN | Endoleptic |
| ABG | Glossalbic | FL | Ferralic | LEP | Epileptic |
| ABH | Hyperalbic | FLH | Hyperferralic | LI | Lithic |
| AC | Acric | FLW | Hypoferralic | LIP | Paralithic |
| AD | Aridic | FO | Folic | ME | Melanic |
| AE | Aceric | FR | Ferric | MG | Magnesic |
| AH | Anthropic | FRH | Hyperferric | MO | Mollic |
| AI | Aric | FU | Fulvic | MS | Mesotrophic |
| AL | Alic | FV | Fluvic | MZ | Mazic |
| AM | Anthric | GA | Garbic | NA | Natric |
| AN | Andic | GC | Glacic | NI | Nitic |
| ANA | Aluandic | GE | Gelic | OA | Oxyaquic |
| ANS | Silandic | GI | Gibbsic | OH | Ochric |
| AO | Acroxic | GL | Gleyic | OHH | Hyperochric |
| AP | Abruptic | GLN | Endogleyic | OM | Ombric |
| AQ | Anthraquic | GLP | Epigleyic | OR | Orthic |
| AR | Arenic | GM | Grumic | PA | Plaggic |
| AU | Alumic | GP | Gypsiric | PC | Petrocalcic |
| AX | Alcalic | GR | Geric | PD | Petroduric |
| AZ | Arzic | GS | Glossic | PE | Pellic |
| CA | Calcaric | GSM | Molliglossic | PF | Profondic |
| CB | Carbic | GSU | Umbriglossic | PG | Petrogypsic |
| CC | Calcic | GT | Gelistagnic | PH | Pachic |
| CCH | Hypercalcic | GY | Gypsic | PI | Placic |
| CCO | Orthicalcic | GYH | Hypergypsic | PL | Plinthic |
| CCW | Hypocalcic | GYW | Hypogypsic | PLH | Hyperplinthic |
| CH | Chernic | GZ | Greyic | PLO | Orthiplinthic |
| CL | Chloridic | HA | Haplic | PLP | Epiplinthic |
| CN | Carbonatic | HG | Hydragric | PLR | Paraplinthic |
| CR | Chromic | HI | Histic | PN | Planic |
| CT | Cutanic | HIB | Thaptohistic | PO | Posic |
| CY | Cryic | HIF | Fibrihistic | PP | Petroplinthic |
| DN | Densic | HIS | Saprihistic | PR | Protic |
| DU | Duric | HK | Hyperskeletic | PS | Petrosalic |
| DY | Dystric | HT | Hortic | PT | Petric |
| DYE | Epidystric | HU | Humic | PTP | Epipetric |
| DYH | Hyperdystric | HUM | Mollihumic | RD | Reductic |
| DYO | Orthidystric | HUU | Umbrihumic | RG | Regic |
| ES | Eutrisilic | HY | Hydric | RH | Rheic |
| ET | Entic | II | Lamellic | RO | Rhodic |
| EU | Eutric | IR | Irragric | RP | Ruptic |
| EUH | Hypereutric | IV | Luvic | RS | Rustic |
| EUN | Endoeutric | IVW | Hypoluvic | RU | Rubic |
| EUO | Orthieutric | IX | Lixic | RZ | Rendzic |
| FG | Fragic | LE | Leptic | SA | Sapric |
| SD | Spodic | SU | Sulphatic | TY | Takyric |
| SI | Silic | SZ | Salic | UB | Urbic |
| SK | Skeletic | SZN | Endosalic | UM | Umbric |
| SKN | Endoskeletic | SZP | Episalic | VI | Vitric |
| SKP | Episkeletic | SZW | Hyposalic | VM | Vermic |
| SL | Siltic | TF | Tephric | VR | Vertic |
| SO | Sodic | TI | Thionic | VT | Vetic |
| SON | Endosodic | TIO | Orthithionic | XA | Xanthic |
| SOW | Hyposodic | TIT | Protothionic | YE | Yermic |
| SP | Spolic | TR | Terric | YES | Nudiyermic |
| ST | Stagnic | TU | Turbic |  |  |
| STN | Endostagnic | TX | Toxic |  |  |

#### Local taxonomic class

If available, the local taxonomic class, established by soil and land resource survey, is recorded.  The local class will most commonly be a Soil Profile Class (Isbell 1988).

## Substrate

#### Substrate type

The substrate (as defined by Speight and Isbell 1990) is characterized using the codes and descriptions for regolith published in the ‘RTMAP database field guide and users guide’ (Pain et al. in press) and shown in Table 47 and Table 48.

Table 47: Regolith material descriptions used for the characterization of substrate (after Pain et al. 2004)

| Code | Regolith | Code | Regolith |
| --- | --- | --- | --- |
| BU00 | unweathered bedrock | SDS00 | coastal sediments |
| EVA00 | evaporite | SDS01 | beach sediments |
| EVA01 | halite | SDS02 | estuarine sediments |
| EVA02 | gypsum | SDS03 | coral |
| EVA03 | Calcrete | SDT00 | terrestrial sediments |
| SDA00 | alluvial sediments | UOC00 | clay (unknown origin) |
| SDA10 | channel deposits | UOM00 | weathered material (unknown origin) |
| SDA20 | overbank deposits | UOS00 | sand (unknown origin) |
| SDC00 | colluvial sediments | VOL00 | Volcanic sediments |
| SDC01 | scree | VOL01 | lava flow |
| SDC02 | landslide deposit | VOL02 | tephra |
| SDC03 | mudflow deposit | WIR10 | Saprolith |
| SDC04 | creep deposit | WIR11 | saprock |
| SDC05 | sheet flow deposit | WIR12 | moderately weathered bedrock |
| SDC06 | fanglomerate | WIR13 | highly weathered bedrock |
| SDE00 | aeolian sediments | WIR14 | very highly weathered bedrock |
| SDE01 | aeolian sand | WIR15 | completely weathered bedrock |
| SDE02 | loess | WIR15.1 | mottled zone |
| SDE03 | parna | WIR15.2 | pallid zone |
| SDF00 | fill | WIR16 | saprolite |
| SDG00 | glacial sediments | WIR20 | residual material |
| SDL00 | lacustrine sediments | WIR21 | lag |
| SDM00 | marine sediments | WIR22 | residual sand |
| SDP00 | swamp (paludal) sediments | WIR23 | residual clay |
| SDP01 | peat | WIR24 | soil on bedrock |

Table 48: Estimation method for substrate type

| Estimation Method | Description |
| --- | --- |
| 1 | Estimate based on direct observation of substrate at the observation site(s) used for soil description |
| 2 | Estimate based on direct observations of substrate in the land-unit tract |
| 3 | Estimate based on direct observations of substrate in the same land-unit type within the region or project area |
| 4 | Estimate based on broad-scale regolith mapping for the area |
| 5 | Estimate based on geological mapping for the area |

#### Substrate permeability

The permeability of the substrate is estimated using the classes in Table 30. The estimate refers to the least permeable layer. Note that the substrate permeability may be the same as the Layer-5 Ks. Estimates are restricted to the upper 10 m.

Table 49: Estimation method for substrate permeability

| Method | Description |
| --- | --- |
| 1 | Estimate based on direct measurement of saturated hydraulic conductivity within the land-unit type |
| 2 | Estimate based on pedotransfer functions using predictor variables from the land-unit tract |
| 3 | Estimate based on direct measurements on similar substrate materials |
| 4 | Estimate based on general knowledge of groundwater movement |
| 5 | Estimate based on experience with similar substrate materials |

# Soil Profile Database

As noted earlier, ASRIS contains the database of polygon descriptors (described in the previous sections) along with separate soil profile database that contains primary data that describe the site, soil morphology, soil chemistry and soil physical properties from fully characterized sites that are known to be representative of significant areas and environments. The minimum data set is listed in Table 50. Data transfer for the Representative Soil Profile Database within ASRIS should follow the SITES protocol (Kidston and McDonald 1995). Further details on the ASRIS soil profile database will be included in the next version of this document.

Table 50: Recommended minimum data set for the ASRIS soil profile database

| Attribute | Method | Attribute | Method |
| --- | --- | --- | --- |
| Site | Soil chemical properties (major horizons) |
| Location |  | pH(1:5 CaCl2) |  |
| Type of observation |  | EC1:5 |  |
| Landform element |  | Organic carbon |  |
| Land use |  | Exch. Ca |  |
| Microrelief type |  | Exch. Mg |  |
| Surface coarse fragments |  | Exch. K |  |
| Rock outcrop |  | Exch. Na |  |
| Surface condition |  | CEC |  |
|  |  | Total P |  |
| Morphology (horizon/depth basis) | Available P |  |
| Horizon type |  | Total N |  |
| Depth |  | Total K |  |
| Boundary shape |  |  |  |
| Boundary distinctness |  | Soil Physical Properties (major horizons) |
| Colour hue, value, chroma |  | Bulk density |  |
| Mottle abundance |  | Particle size |  |
| Coarse fragment abundance |  | –10 kPa (v |  |
| Field pH |  | –1.5 MPa (v |  |
| Texture |  | Soil shrinkage |  |
| Structure grade |  | Dispersion class |  |
| Structure size |  | Saturated K |  |
| Structure type |  | Unsaturated K (–50mm) |  |
| Segregation abundance |  |  |  |
| Segregation type |  | Taxonomy |  |
| Carbonate effervescence |  | ASC (to Family level) |  |
|  |  | World Reference Base |  |

# Data conventions, transfer procedures and database design

## Missing data, explicit zeros and explanatory notes

Blank entries are ambiguous because they can be interpreted to be a real zero (e.g., 0%), absence of a nominal variable (e.g., no redoximorphic mottles), missing data (e.g. through an oversight or deliberate decision), or a logical impossibility (e.g., mottle colour when mottle abundance is 0%). To avoid ambiguity, the following conventions are used throughout ASRIS – absences or zeros must be explicit.

Real zeros and absences: Use 0 for numeric fields. For alphanumeric fields, use Z to denote the attribute is absent unless the code table already has an assigned code.

Not known: Use -1234 for numeric fields. For alphanumeric fields, use NR unless the code table has an assigned code.

Logically impossible: Use -9999 for numeric fields. For alphanumeric fields, use NA unless the code table has an assigned code.

Finally, a free text field can be used to note any difficulties encountered with the data model and definitions. For example, it may be difficult to reliably represent a soil profile using the four layer model adopted by ASRIS. The note should outline the problem and method used to for estimating soil attributes.

## Database design

The database design for ASRIS is presented in Figure 10. Definitions and formats used for the variables in each component database table are listed in the following tables. The full list of method codes, including those for the profile data, is available from the ASRIS team. When providing data to ASRIS, it is necessary to supply the necessary decode data and tables (e.g., the codes used for identifying officers responsible for soil descriptions). Identify instances where codes from McDonald et al. (1990) have not been used.

Figure 10: Database design for ASRIS. Definitions of variables are provided in the Tables below.

The method to be used by state and territory agencies for transferring data to ASRIS depends heavily on the information systems and support staff available in each contributing organization. The most technically demanding but best approach is to generate ASRIS data through a series of formal queries to the agency information system. This requires a very well organized agency database and significant investment in computer coding. Another approach is to use the ASRIS Data Entry Spreadsheet available from the ASRIS website. This EXCEL spreadsheet allows for manual or semi-automated data-entry (e.g. cutting and pasting from agency spreadsheets).

While it would be advantageous for agencies to provide data using the ASRIS database design, it is recognized that many field operators have difficulty with the principles guiding relational database design and that most prefer the flat file format provided by the spreadsheet. The key requirement is for each agency to select a procedure that encourages efficient updating when new information becomes available.

Referential integrity is necessary within the ASRIS database so ensure that unique identifiers are used for land-unit tracts. Avoid using upper or lower case letters as a means of creating unique keys. Also avoid including the letters o or i in unique keys wherever possible.

ASRIS is provided via the Internet using SQL Server, the ARC Spatial Data Engine, and ARC Internet Map Server. As a result, the spatial data should be supplied to ASRIS with a defined topology and in a format that can be imported to ARC Info. These data need a nominated projection and datum along with metadata conforming at least to ANZLIC standards. All spatial data in ASRIS are based on the Geodetic Datum of Australia (GDA94). It would be advantageous for the polygon coverages to conform to the vector baseline GEODATA COAST 100K 2004.  This dataset contains boundaries for the coastline, states and territories. It is available as a free download from the Geoscience Australia website.

Table 51: The agencies table.

| Column Name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| state_code | nvarchar | 3 | no | State code i.e. NSW=1, VIC=2, QLD=3, SA=4, WA=5, TAS=6, NT=7, ACT=8 |
| agency_name | nvarchar | 240 | no | Name of agency |
| agency_acronym | nvarchar | 10 | yes | Agency acronym, e.g. WADA |

Table 52: The projects table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| project_name | nvarchar | 240 | no | Project name |
| project_contact | nvarchar | 4 | no | Project contact officer |
| project_biblio_ref | nvarchar | 240 | yes | Bibliographic reference |

Table 53: The site_location table.

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 30 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| site_lat | numeric | 9 | yes | Latitude decimal degrees |
| site_long | numeric | 9 | yes | Longitude decimal degrees |
| site_east | numeric | 9 | yes | Australian Map Grid Easting |
| site_north | numeric | 9 | yes | Australian Map Grid Northing |
| site_zone | nvarchar | 3 | yes | Australian Map Grid Zone |
| site_datum | nvarchar | 10 | yes | Datum |
| site_spheroid | nvarchar | 10 | yes | Spheroid |
| loc_method | nvarchar | 15 | yes | Location method (e.g. hand held GPS, 1:100,000 mapsheet) |

Table 54: The features table.

| Column Name | Data type | Length | Nullable | Description |  |
| --- | --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 30 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| feature_id_orig | nvarchar | 10 | no | Feature identifier from originating agency |
| proportion | decimal | 5 | no | Feature proportion if component_id=0 otherwise component proportion |
| feature_type | nvarchar | 2 | no | Feature type, e.g. point, tract |
| hierarchy | nvarchar | 3 | no | Level of ASRIS hierarchy |
| feature_name | nvarchar | 30 | yes | Name of the feature |
| ref_agency_code | nvarchar | 3 | yes | Parent feature's agency code |
| ref_project_code | nvarchar | 10 | yes | Parent feature's project code |
| ref_feature_id | nvarchar | 10 | yes | Parent feature's feature code |
| ref_component_id | nvarchar | 30 | no | Parent feature's component identifier |

Table 55: The feature notes table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 30 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| notes_type | nvarchar | 30 | yes | Feature notes type if component_id = 0 otherwise notes refers to the component |
| notes | nvarchar | 240 | yes | Feature notes if component_id = 0 otherwise notes refers to the component |

Table 56: The samples table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 30 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| samp_no | int | 4 | no | Sample number |
| samp_type | nvarchar | 15 | yes | Type of sample (e.g. fine earth, whole soil) |
| samp_method | nvarchar | 15 | yes | Sampling method |
| samp_upper_depth | numeric | 5 | yes | Sample upper depth (m) |
| samp_lower_depth | numeric | 5 | yes | Sample lower depth (m) |
| samp_desc | nvarchar | 240 | yes | Sample description |

Table 57: The sample notes table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 30 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| samp_no | int | 4 | no | Sample number |
| samp_notes | nvarchar | 240 | yes | Sample notes |

Table 58: The results table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| project_code | nvarchar | 10 | no | Project identifier |
| feature_id | nvarchar | 30 | no | Feature identifier |
| component_id | nvarchar | 30 | no | Unmapped component identifier |
| samp_no | int | 4 | no | Sample number |
| res_no | int | 4 | no | Result number |
| param_char_id | nvarchar | 20 | no | Parameter method identifier (categorical data) |
| param_num_id | nvarchar | 20 | no | Parameter method identifier (continuous data) |
| res_value_type | nvarchar | 1 | yes | (Value type, e.g. maximum, minimum, mean) |
| res_value_pref | nvarchar | 1 | yes | Value prefix (e.g. –, <, >) |
| res_char_value | nvarchar | 25 | yes | Character value |
| res_num_value | numeric | 5 | no | Numerical value |
| res_proportion | int | 4 | yes | Percentage of area the value represents |
| res_est_method | int | 4 | yes | Estimation method for polygon attributes |
| res_uc1 | numeric | 5 | yes | Result uncertainty1 |
| res_uc2 | numeric | 5 | yes | Result uncertainty2 |

Table 59: The param_num_method table.

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| param_num_id | nvarchar | 20 | no | Parameter method identifier |
| parameter | nvarchar | 20 | no | Parameter measured (e.g. pH, organic carbon) |
| parameter_desc | nvarchar | 240 | yes | Method description |
| param_method_units | nvarchar | 10 | yes | Units of measurement |
| param_method_ref | nvarchar | 20 | yes | Technical reference for the method |
| error | numeric | 5 | yes | Error of measurement |
| min_detect | numeric | 5 | yes | Minimum detection limit |
| max_detect | numeric | 5 | yes | Maximum detection limit |
| correction | numeric | 5 | yes | Required corrections |

Table 60: The param_char_method table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| param_char_id | nvarchar | 20 | no | Parameter method identifier e.g. texture, mottle abundance, segregation form |
| code_value | nvarchar | 25 | no | Code value (e.g. LC, 2, N) |
| parameter | nvarchar | 20 | no | Parameter measured (e.g. pH, texture, depth, mottles) |
| code_desciption | nvarchar | 128 | yes | Code description (e.g. light clay, few 2-10%, nodules) |

Table 61: The param_ char_refs table

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| param_char_id | nvarchar | 20 | no | Parameter method identifier (e.g. texture, mottle abundance, segregation form) |
| code_reference | nvarchar | 50 | yes | Page of reference from McDonald et al. (1990) unless otherwise stated |

Table 62: The codes table.

| Column name | Data type | Length | Nullable | Description |
| --- | --- | --- | --- | --- |
| agency_code | nvarchar | 3 | no | Agency identifier |
| code_domain | nvarchar | 20 | no | Code domain |
| code_value | nvarchar | 20 | no | Code value |
| code_parameter | nvarchar | 20 | no | Parameter measured (e.g. officers, feature type) |
| code_desciption | nvarchar | 128 | yes | Code description |

# Relationship to SOTER

ASRIS has been designed to facilitate the Australian contribution to SOTER – this is the new global soil and land resource information system. Details on the conversion protocols will be provided in the next version of this document.

# References

Austin, MP, Basinski JJ (1978) Bio-physical survey techniques. In ‘Land use on the South Coast of New South Wales.  A study in methods of acquiring and using information to analyse regional land use options. Volume 1. General report.’ (General Eds. MP Austin and KD Cocks).

Beckett PHT (1968) Method and scale of land resource srveys, in relation to precision and cost.  In Land evaluation. (Ed. GA Stewart). (MacMillan: Melbourne).

Beckett PHT, Webster R (1971) Soil variability: a review. Soils and Fertilizers 34, 1–15.

Beckett PHT, Bie, SW (1978) Use of soil and land system maps to provide soil information in Australia.  CSIRO Aust. Div Soils Tech. Paper No. 33.

Bui EN, Moran CJ (2004) Synthesis studies. In ‘Guidelines for surveys 2nd edition.’ Australian Soil and Land Survey Handbook Series Volume 2 (Eds NJ McKenzie, MJ Grundy, AJ Ringrose-Voase) (CSIRO Publishing: Melbourne).

Carter DJ (2002) Water repellence. In Soil physical measurement and interpretation for land evaluation.  Australian Soil and Land Survey Handbook Series Vol. 5. (Eds McKenzie NJ, Coughlan K, Cresswell HP) (CSIRO Publishing: Melbourne).

Chan RA (1986) Regolith terrain map of Australia 1:5 000 000. Record 1986/27. Bureau of Mineral Resources, Geology and Geophysics, Canberra.

Christian CS Stewart GA (1968).  Methodology of integrated surveys. In Aerial surveys and integrated studies. Proceedings of the Tolouse Conference of 1964. (UNESCO: Paris).

Coram J, Dyson P, Evans R (2001). An evaluation framework for dryland salinity. Bureau of Rural Sciences, Canberra.

Cresswell HP, Paydar Z (1996) Water retention in Australian soils. I. Description and prediction using parametric functions. Australian. Journal of Soil Research 34, 195–212.

CSIRO (1983) ‘Soils: an Australian viewpoint.’ (CSIRO: Melbourne/Academic Press: London).

Dalal-Clayton B, Dent D (2001) ‘Knowledge of the land.’ (Oxford University Press: Oxford).

Dent D, Young A (1981). Soil survey and land evaluation. (George Allen and Unwin: London).

Emerson WW (2002) Emerson dispersion test. In Soil physical measurement and interpretation for land evaluation.  Australian Soil and Land Survey Handbook Series Vol. 5. (Eds McKenzie NJ, Coughlan K, Cresswell HP) (CSIRO Publishing: Melbourne).

Environment Australia (2000) Revision of the Interim Biogeographic Regionalisation for Australia (IBRA) and Development of Version 5.1 – Summary Report. Department of Environment and Heritage, Canberra.

Gallant JC, Dowling TD (2003) A multi-resolution index of valley bottom flatness for mapping depositional areas. Water Resources Research 39, 1347–1360.

Gibbons FR (1983) Soil mapping in Australia. In Soils: an Australian viewpoint. CSIRO Aust. Div. Soils. (CSIRO: Melbourne\Academic Press: London).

Grant K, Davis JR, de Visser C (1984) A geotechnical landscape map of Australia. CSIRO Division of Water and Land Resources Divisional Report 84/1, Canberra.

Gunn RH, Beattie JA, Reid RE, van de Graaff RHM (1988) Australian soil and land survey handbook:  guidelines for conducting surveys. (Inkata Press: Melbourne).

Henderson BL, Bui EN, Moran CJ, Simon DAP, Carlile P (2001). ‘ASRIS: Continental-scale soil property predictions from point data’ (Technical Report 28/01, CSIRO Land and Water, Canberra).

Henderson BL, Bui EN (2002). An improved calibration curve between soil pH measured in waterand CaCl2 . Australian Journal of Soil Research 40, 1399–1405.

Heuvelink GBM (1998) Error propagation in environmental modelling with GIS. (Taylor and Francis: London).

Isbell RF (1988) Soil classification. In ‘Australian Soil and Land Survey Handbook – Guidelines for Conducting Surveys.’ (Eds RH Gunn, JA Beattie, RE Reid and RHM van de Graaff) pp 20-36. (Inkata Press: Melbourne)

Isbell RF (1996) ‘The Australian soil classification.’ (CSIRO Publishing: Melbourne).

Isbell RF (2002) ‘The Australian soil classification (Revised first edition).’ (CSIRO Publishing: Melbourne).

Jennings JN, Mabbutt JA (1986) Physiographic outlines and regions. In ‘Australia, a geography. Volume 1. The natural environment.’ (Ed. DN Jeans) (Sydney University Press: Sydney)

Johnston RM, Barry SJ, Bleys E, Bui EN, Moran CJ, Simon DAP, Carlile P, McKenzie NJ, Henderson BL, Chapman G, Imhoff M. Maschmedt D, Howe D, Grose C, Schoknecht N, Powell B, Grundy M (2003) ASRIS – the database. Australian Journal of Soil Research 41, 1021–1036.

Kidston L, McDonald WS (1995) Soil information transfer and evaluation system user manual. ACLEP Technical Report No. 5, (CSIRO Division of Soils: Canberra).

King, PM (1981). Comparison of methods for measuring severity of water repellence of sandy soils and assessment of some factors that affect its measurement. Australian Journal of Soil Research 19, 275–285.

Laut P, Firth D, Paine TA (1980). Provisional environmental regions of Australia: a working document towards a framework for Australian environmental statistics. (CSIRO: Melbourne) Löffler and Ruxton (1969)

Mabbutt JA (1968) Review of concepts of land evaluation. In Land evaluation. (Ed. GA Stewart). (MacMillan: Melbourne).

Minasny B, Bishop T (2004) Uncertainty analysis. In Guidelines for conducting surveys 2nd edition. Australian Soil and Land Survey Handbook Series Volume 2. (CSIRO Publishing: Melbourne) (in press).

McBratney AB, Pringle MJ (1999) Estimating proportional and average variograms of soil properties and their potential use in precision agriculture. Precision Agriculture, 1, 125–152.

McDonald RC, Isbell RF (1990). Soil profile. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS (1990). Australian soil and land survey field handbook. 2nd Edn.  (Inkata Press:  Melbourne).

McKenzie NJ (1991) A strategy for coordinating soil survey and land evaluation in Australia.  CSIRO Division of Soils, Divisional Report No. 114.

McKenzie NJ, Ryan PJ (1999) Spatial prediction of soil properties using environmental correlation. Geoderma 89, 67-94.

McKenzie NJ, Henderson B, McDonald WS (2002) Monitoring soil change. Principles and practices for Australian conditions. CSIRO Land & Water Technical Report 18/02, Canberra.

McKenzie NJ, Gallant JC, Gregory LJ (2003) Estimating water storage capacities in soil at catchment scales. Technical Report 03/3, Cooperative Research Centre for Catchment Hydrology, Canberra.

McKenzie NJ, Grundy MJ, Ringrose-Voase AJ (Eds) (2004) ‘Guidelines for surveys 2nd edition.’ Australian Soil and Land Survey Handbook Series Volume 2 (CSIRO Publishing: Melbourne).

Moore G (1998) Soilguide: A handbook for understanding and managing agricultural soils. Agriculture Western Australia, Bulletin 4343.

Moss RH, Schneider SH (2000) Uncertainties in the IPCC Third Assessment Report. Recommendations to lead authors for more consistent assessment and reporting. In Guidance Papers on the Cross Cutting Issues of the Third Assessment Report of the IPCC (Eds R Pachauri, T Taniguchi, K Tanaka) (World Meteorological Organization: Geneva).

NLWRA (2001) ‘Australian agricultural assessment 2001.’ National Land and Water Resources Audit, Canberra.

NLWRA (2002) ‘Natural resource economics.’ National Land and Water Resources Audit, Canberra.

Northcote KH with Beckmann GG, Bettenay E, Churchward HM, Van Dijk DC, Dimmock GM, Hubble GD, Isbell RF, McArthur WM, Murtha GG, Nicolls KD, Paton TR, Thompson CH, Webb AA, Wright MJ (1960-1968) ‘Atlas of Australian Soils, Sheets 1 to 10.  With explanatory data (CSIRO Aust. and Melbourne University Press:  Melbourne).

Northcote KH (1984) Soil-landscapes, taxonomic units and soil profiles.  A personal perspective on some unresolved problems of soil survey.  Soil Survey and Land Evaluation, 4, 1–7.

Pain C, Chan R, Craig M, Gibson D, Kilgour P, Wilford J (in press) RTMAP regolith database field book and users guide (second edition). CRC LEME Report 138.

Peverill KI, Sparrow LA, Reuter (1999) ‘Soil analysis: an interpretation manual.’ (CSIRO Publishing: Melbourne).

Raupach M, Tucker BM (1959) The field determination of soil reaction.  J. Aust. Inst. Agric. Sci. 25, 129–133.

Raupach MR, Kirby JM, Barrett DJ, Briggs PR (2001) Balances of water, carbon, nitrogen and phosphorus in Australian landscapes: (1) Project description and results. CSIRO Land and Water Technical Report 40/01, CSIRO, Canberra.

Soil Survey Division Staff (1993) Soil survey manual. United States Department of Agriculture, Handbook No. 18 (US Government Printing Office: Washington).

Speight JG (1988) Land classification. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Speight JG (1990) Landform. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Speight JG, Isbell RF (1990) Substrate. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Steur GGL (1961) Methods of soil surveying in use at the Netherlands Soil Survey Institute. Boor en Spade 11, 59–77.

Stewart GA (1968) Land evaluation. (MacMillan: Melbourne).

Taylor BN, Kuyatt CE (1994) Guidelines for evaluating and expressing the uncertainty of NIST measurement results. NIST Technical Note 1297, United States Government Printing Office, Washington.

Thompson CH, Moore AW (1984) Studies in landscape dynamics in the Cooloola-Noosa River area, Queensland. CSIRO Australia, Division of Soils Divisional Report No. 73.

Walker J, Hopkins MS (1990) Vegetation. In Australian soil and land survey field handbook. (McDonald RC, Isbell RF, Speight JG, Walker J, Hopkins MS) 2nd Edn.  (Inkata Press:  Melbourne).

Wilding LP, Drees LR (1983) Spatial variability and pedology. In ‘Pedogenesis and Soil Taxonomy. I Concepts and interactions.’  (Eds LP Wilding, NE Smeck and GF Hall) Developments in Soil Science 11A (Elsevier: Amsterdam).

Williams J, Ross PJ, Bristow KL (1992) Prediction of the Campbell water retention function from texture, structure and organic matter. In Proc.international workshop on indirect methods for estimating the hydraulic properties of unsaturated soils. (Eds. M Th van Genuchten, FJ Leij, LJ Lund) Univ. of California, Riverside, CA.

Williams J, Hook RA, Hamblin A (2002). ‘Agro-ecological regions of Australia : methodologies for their derivation and key issues in resource management.’ CSIRO Land and Water, Canberra.

# Appendix 1: Conversion for pH in water to pH in CaCl2

The conversion table for pH in water (1:5 soil to water) to pH in CaCl2 (1:5 soil to 0.01M CaCl2) is from Henderson and Bui (2002). It is based on 70,465 observations collated to support ASRIS 2001. The values in italics are to be regarded as more doubtful extrapolations of the statistical curve because they are supported by a smaller number of observations.

Table 63: Conversion for pH in water to pH in CaCl2.

| Observed pH water | Predicted pH CaCl2 | Observed pH water | Predicted pH CaCl2 | Observed pH water | Predicted pH CaCl2 |
| --- | --- | --- | --- | --- | --- |
| 3.0 | 2.8 | 5.4 | 4.6 | 7.8 | 7.2 |
| 3.1 | 2.9 | 5.5 | 4.7 | 7.9 | 7.3 |
| 3.2 | 3.0 | 5.6 | 4.8 | 8.0 | 7.4 |
| 3.3 | 3.0 | 5.7 | 4.9 | 8.1 | 7.5 |
| 3.4 | 3.1 | 5.8 | 5.0 | 8.2 | 7.5 |
| 3.5 | 3.2 | 5.9 | 5.1 | 8.3 | 7.6 |
| 3.6 | 3.2 | 6.0 | 5.2 | 8.4 | 7.7 |
| 3.7 | 3.3 | 6.1 | 5.3 | 8.5 | 7.8 |
| 3.8 | 3.4 | 6.2 | 5.4 | 8.6 | 7.8 |
| 3.9 | 3.5 | 6.3 | 5.5 | 8.7 | 7.9 |
| 4.0 | 3.5 | 6.4 | 5.7 | 8.8 | 8.0 |
| 4.1 | 3.6 | 6.5 | 5.8 | 8.9 | 8.0 |
| 4.2 | 3.7 | 6.6 | 5.9 | 9.0 | 8.1 |
| 4.3 | 3.7 | 6.7 | 6.0 | 9.1 | 8.2 |
| 4.4 | 3.8 | 6.8 | 6.2 | 9.2 | 8.2 |
| 4.5 | 3.9 | 6.9 | 6.3 | 9.3 | 8.3 |
| 4.6 | 3.9 | 7.0 | 6.4 | 9.4 | 8.4 |
| 4.7 | 4.0 | 7.1 | 6.5 | 9.5 | 8.4 |
| 4.8 | 4.1 | 7.2 | 6.6 | 9.6 | 8.5 |
| 4.9 | 4.2 | 7.3 | 6.7 | 9.7 | 8.6 |
| 5.0 | 4.2 | 7.4 | 6.8 | 9.8 | 8.7 |
| 5.1 | 4.3 | 7.5 | 6.9 | 9.9 | 8.7 |
| 5.2 | 4.4 | 7.6 | 7.0 | 10.0 | 8.8 |
| 5.3 | 4.5 | 7.7 | 7.1 | 10.1 | 8.9 |

Appendix 2: Updates to the Technical Specifications

Version 1.4 March 2005

Substantial change to the definition and variables used to characterize Levels 1 to 3. Climate variables are now used as descriptors of land-unit tracts rather than defining variables for boundary placement (primarily Table 3 Section 4.2, and Sections 6–8). Regolith characterization as been refined and summaries of soil taxonomic units added.

Removal of reference to a correction factor for coarse fragments and plant available water capacity. Replacement with a method relying on the percentage of coarse fragments and their porosity (page 55). Addition of porosity of coarse fragments as a variable (Table 4, page 49).

Change in formatted length of the variable feature_id in Table 53 to Table 58.

Coverages of spatial data are recommended to conform to the vector baseline GEODATA COAST 100K 2004 rather than the earlier 1992 version.

Changes under consideration for Version 1.5

Addition of two fields to Table 47 – SDL10 for fluvio-lacustrine and estuarine, and INF00 for ferricrete.

# Footnotes

The term land capability was used in the original brief – this term is usually associated with the United States Department of Agriculture eight-class system for classifying land. The term land suitability is preferred here (see Dent and Young 1981, McKenzie 1991).

Note that some states already have good upper level stratifications (e.g. Vic, WA, Tas) and these, rather than Jennings and Mabbutt,  will form the starting point.

Note that some states already have good upper level stratifications (e.g. Vic, WA, Tas) and these, rather than Jennings and Mabbutt,  will form the starting point.

See the definition by Isbell (1988). Some agencies use a different nomenclature: for example, Soil Groups (Western Australia) are examples of soil profile classes defined at a general level.

See http://lime.isric.nl/index.cfm?contentid=236 for information on SOTER

# Text boxes

(ASRIS)

Land resource survey (ASRIS)

Land condition monitoring

f = exp(-X/ Xi)

Xi = depth where 37% of

water extraction is deeper

=



Profile available

water capacity

Profile has a large percentage of coarse fragments in Layer 2 and an abundance in Layer 4

Weighting for

water extraction

Plant available

water capacity

Weighting = 0 if depth > impeding layer. Four estimates of Xi for notional plan functional forms – the solid line is used in this instance

1

((–10kPa–(–1.5MPa)

Weighting for

water extraction

Plant available

water capacity

Adjustment for coarse fragments (% and porosity)



0

1

0